## Slide 1: Feasibility of reporting: expected UE behaviour with duty-cycle reporting and PMPR method?
Ericsson
3GPP TSG-RAN WG4 Meeting #96-e
Electronic meeting, 17 – 28 August 2020
R4-2010349
Agenda item: 9.2.1
Document for: Approval

## Slide 2: Background and current understanding
NW expected to schedule the EN-DC PC2 UE according to its reported duty-cycle (dc) capability, otherwise EN-DC PC3 fallback
The UE behaviour in the field is unclear
Duty cycle:
  if the ’actual’ NR dc scheduled is less than the reported (maxNRDuty1/2) while the ’actual’ LTE dc scheduled is less than the reference value (dutyLTE1/2), then 26 dBm total EN-DC power
  otherwise fallback to PC3 (23 dBm total power)
PMPR:
  the total EN-DC power is (26 dBm – PMPR) depending on CG duty cycles (proprietary)
  fallback to PC3, unspecified when

## Slide 3: Open issues for duty cycle reporting
Dependence on ’actual’ output power on the CGs given an ’actual’ dc scheduled?
How is the ’actual’ dc measured in the time domain?
  ”Certain evaluation period” been used for TDD, unknown for the scheduler
The PMPR unspecified (this method is actually blind)
  What does ”full duty cycle supported” mean?
SAR is always tested with 100% FDD duty cycle, the UE always tested in PC3 fallback?
There are no proposed test cases for duty cycle reporting and PMPR

## Slide 4: Duty cycle value range and output power
Is the duty cycle reporting applicable at maximum power or other power levels?
  Similar discussion for FR2 duty-cycle reporting
The reporting is semi-static (UE capability), not changed during connection
Two fixed LTE reference configurations, DutyLTE1=70%, DutyLTE2=40% corresponding to the respective
  maxNRDuty1 ∈ {30%, 40%, 50%, 60%, 70%, 80%, 90%, 100% , Full_duty_supported}
  maxNRDuty2 ∈ {30%, 40%, 50%, 60%, 70%, 80%, 90%, 100% }
Maximum power: with 100% NR duty cycle and maximum CG power, the reporting would allow up to
  25.3/24.5 dBm average total power for Case 1 (Duty1/Duty2)
  26 dBm average total power for Case 2 (NR can be at full power, the total 26 dBm)
Considerably higher average power than the 23 dBm normally assumed for HPUE to faciliate SAR and UE heat management
Are the duty-cycle value ranges proposed realistic/feasible?

## Slide 5: Duty cycle: PC3 fallback dependence on CG power?
If the actual FDD dc over the ’certain evaluation period’ is 100%, i.e. greater than the LTE reference dc, the UE presumably falls back to PC3 regardless of the actual NR dc (?)
Is fallback only dependent on dc, i.e. independent of actual output power?
  fallback is only ’necessary’ if the FDD is at maximum power Pmax,LTE; if not, then PC3 fallback is unnecessary, the average total power can still be below 23 dBm, e.g. FDD below 10 dBm att 100% dc with TDD above 25 dBm at 30% dc (the reported NR capability assumed)
Even if not, the MeNB has got limited knowledge of the MCG output power on frame basis, only PHR reports that are relatively scarce
Duty cycle reporting less useful if the UE behaviour is also dependent on the power (as it should be)
(D+X)
U
U
U
U
U
U
U
U
U
U
U
FDD
TDD
Pmax,LTE (PC3 or PLTE)
pscg
pmsg
U
(D+X)
U
U
Pmax,NR (PC3 or PC2)
PMSG
PSCG
U
U
Fallback to PC3 not necessary if the FDD is not at full power even if the LTE duty cycle is 100% > DutyLTE1 and DutyLTE2
FDD not at full power

## Slide 6: Duty cycle: measurement of the duty cycle
How is the duty cycle evaluated in the time domain?
For TDD-TDD EN-DC PC2:
  ” if the field of UE capability maxUplinkDutyCycle-PC2-FR1 is not absent and the percentage of NR uplink symbols transmitted in a certain evaluation period is larger than maxUplinkDutyCycle-PC2-FR1 as defined in TS38.331 (The exact evaluation period is no less than one radio frame)”
Unclear how the reported UE duty-cycle capability (even at maximum UE power) should be interpreted/measured by the MeNB and SgNB
  then add the uncertainty in output power

## Slide 7: PMPR method
PMPR metod ”up to UE implementation” but behaviour is unspecified
  What does ”full-duty supported” mean? 26 dBm total power with 100% NR? Condition on LTE? Power dependence?
Verification of behaviour: if the duty cycle of the total EN-DC transmission is <50% then the peak power at burst should be 26 dBm: verify this in a test case e.g. as follows:
But why fallback to PC3 and when?
  If PLTE < 23 dBm no reason to fall back to anything lower than the total power given by the blind scheme
(D+X)
U
U
U
U
U
U
U
U
U
U
U
FDD
TDD
Pmax,LTE (PC3 or PLTE)
U
(D+X)
U
U
Pmax,NR (PC3 or PC2)
PMSG
PSCG
The TDD shall attain maximum power

## Slide 8: Summing up
Interpretation of the reported duty-cycle capability uncertain both in the power- and time domain
  The UE behaviour not only dependent on the duty cycle
  Similar discussion for duty-cycle reporting in FR2
Uncertain gain, if any at all, at high cost (tight CG scheduling and UE complexity)
Similar issues for TDD-TDD, but slightly less difficult since a duty-cycle (U/D patterns) is an integral part of TDD
The behaviour of the PMPR method (proprietary), if adopted, not specified, UE behaviour in the field unclear
The ”blind scheme” has got none of these deficiencies (and tested like current EN-DC PC3)

## Slide 9: Proposal
The PMPR is the baseline combined with the ”blind scheme”
  but introduce a test case to verify UE behaviour e.g. for total duty cycle less than 50% (then total power should be 26 dBm using P-MPR method)
  Fallback to the power given by the blind scheme when PLTE < 23 dBm, ensures a minimum total power level > 23 dBm in all cases, ”minimum level”
  Up to 26 dBm can be attained also with PLTE = 23 dBm but UE behaviour unclear
Downside: more complex for the UE than the ”blind” scheme alone
Duty cycle reporting optional
  revisit signaling: new fields could be specified in Rel-16, but values and method should be reconsidered
The WI can be closed even if not all signaling details are finalized