## Slide 1: WF on REFSENS requirements for NR V2X UE at licensed/unlicensed bands
LG Electronics,...
3GPP TSG-RAN WG4#96-e Meeting R4-2011708
Electronic Meeting, 17 – 28 August, 2020

## Slide 2: Background
In this meeting, RAN4 discuss several parameters to decide REFSENS requirements for NR V2X UE at licensed/unlicensed bands.
  Issue #2-1-1: Target SNR point
    Option 2: Based on simulation results the target SNR point is changed to -0.5dB
    Option 3: Target SNR is dependent on the MCS setting and diversity gain selected as explained below in Issue 2-2-1.
  Issue #2-1-2: Noise Figure
    Option 2: Keep the NF is 9dB < 3GHz, NF is 10dB>= 3GHz (e.g B42, n77, n78, n79…) at licensed bands at FR1.
    Option 3: RAN4 can decide the Noise Figure considering with Issue #2-1-2, #2-1-5, #1-2-2 jointly [1].
  Diversity gain and Number of RB size already decided in 1st round e-mail summary in [1]

## Slide 3: Issue 2-1-1: Target SNR point for NR V2X
Target SNR -0.5dB is proposed in 1st round based on LLS simulation results. (R4-2010817)
According to CBW and SCS, target SNR level is quite dependent. So the MCS index for REFSENS would be changed in FRC table.(R4-2010015)
Candidate options
    Option 1: Based on simulation results, the target SNR point will be changed from -1.0dB to -0.5dB
    Option 2: Target SNR is dependent on the MCS setting and diversity gain selected as explained below in Issue 2-2-1.
Proposal for WF
  Option 1 is chosen, additional margin 0.5dB will be considered when the RBs size equal to or less than 24RBs.

## Slide 4: Issue 2-1-2: Noise Figure for NR V2X UE
RAN4 need to decide NF for licensed band whether measurement point is consider external components or not. Current RAN4 specification defined as follow in general part for Tx and Rx requirements.
  Unless otherwise stated, the transmitter characteristics are specified at the antenna connector of the UE with a single or multiple transmit antenna(s). For UE with integral antenna only, a reference antenna with a gain of 0 dBi is assumed.
Candidate options
    Option 1: Keep the NF is 9dB < 3GHz, NF is 10dB>= 3GHz (e.g B42, n77, n78, n79…) at licensed bands at FR1.
    Option 2: RAN4 can decide the Noise Figure considering with Issue #2-1-2, #2-1-5, #1-2-2 jointly [1].
Proposal for WF
  Option 1 is chosen, Measurement point description & Figure will be captured in TR38.886 and LS R4-2011710 will send to RAN5

## Slide 5: WF : REFSENS requirements
REFSENS requirements for single licensed/unlicensed bands
NR Operating band / SCS / Channel bandwidth / Duplex-mode |  |  |  |  |  | 
V2X Band | SCS kHz | 10MHz (dBm) | 20MHz (dBm) | 30MHz (dBm) | 40MHz (dBm) | Duplex Mode
n38 | 15 | -96.5 | -93.2 | -91.4 | -90.1 | TDD
 | 30 | -96.1 | -93.4 | -91.7 | -90.2 | 
 | 60 | -96.9 | -93.1 | -91.9 | -90.4 | 
n47 | 15 | -92.5 | -89.2 | -87.4 | -86.1 | HD
 | 30 | -92.1 | -89.4 | -87.7 | -86.2 | 
 | 60 | -92.9 | -89.1 | -87.9 | -86.4 | 

## Slide 6: WF : REFSENS requirements
REFSENS requirements for con-current operations
Inter-band V2X reception |  | Channel bandwidth |  |  |  |  |  |  |  | 
NR V2X Band | NR band | NR Band | SCS (kHz) | 5 MHz (dBm) | 10 MHz (dBm) | 15 MHz (dBm) | 20 MHz (dBm) | 30 MHz (dBm) | 40 MHz (dBm) | Duplex Mode
n47 | n71 | n71 | 15 | -97.2 | -94.0 | -91.6 | -86.0 |  |  | FDD
 |  |  | 30 |  | -94.3 | -91.9 | -87.4 |  |  | 
 |  |  | 60 |  |  |  |  |  |  | 
 |  | n47 | 15 |  | -92.5 |  | -89.2 | -87.4 | -86.1 | HD
 |  |  | 30 |  | -92.1 |  | -89.4 | -87.7 | -86.2 | 
 |  |  | 60 |  | -92.9 |  | -89.1 | -87.9 | -86.4 | 
Inter-band EN-V2X reception |  |  | Channel bandwidth |  |  |  |  |  |  | 
NR V2X Band | E-UTRA or V2X band | Band | SCS (kHz) | 5 MHz (dBm) | 10 MHz (dBm) | 15 MHz (dBm) | 20 MHz (dBm) | 30 MHz (dBm) | 40 MHz (dBm) | Duplex Mode
n38 | Band 20 | Band 20 | 15 | -97 | -94 | -91.2 | -90 |  |  | FDD
 |  | n38 | 15 |  | -96.5 |  | -93.2 | -91.4 | -90.1 | HD
 |  |  | 30 |  | -96.1 |  | -93.4 | -91.7 | -90.2 | 
 |  |  | 60 |  | -96.9 |  | -93.1 | -91.9 | -90.4 | 
RESENS for NR V2X con-current (V2X_n71-n47) in TS38.101-1
RESENS for NR V2X con-current (V2X_20_n38) in TS38.101-3

## Slide 7: References
# of Tdoc | TDoc | Title | Source | Type
1 | R4-2011541 | E-mail summary [96e][108]_5G V2X_UE RF | LG Electronics Inc. | Information
2 | R4-2010822 | On NR V2X reference measurement channels | Huawei, HiSilicon | other
3 | R4-2010823 | draft CR for TS 38.101-1: NR V2X FRC | Huawei, HiSilicon | draftCR
4 | R4-2010824 | draft CR for TR 38.886: NR V2X FRC | Huawei, HiSilicon | draftCR
5 | R4-2010137 | Correction on NR V2X UE RF requirements for single carrier in TS38.101-1 | LG Electronics France | CR
6 | R4-2010025 | Components external to UE | Qualcomm Incorporated | CR
7 | R4-2010137 | Correction on NR V2X UE RF requirements for single carrier in TS38.101-1 | LG Electronics France | CR
8 | R4-2009823 | CR for TS 38.101-1, REFSENS requirements for NR V2X band n38 | CATT | CR
9 | R4-2009826 | REFSENS requirements for NR V2X band n38 | CATT | CR
10 | R4-2010013 | REFSENS requirements and LLS results of REFSENS for NR V2X UE | LG Electronics Inc. | other
11 | R4-2010015 | V2X RX Issues | Qualcomm Incorporated | other
12 | R4-2010027 | REFSENS for V2X | Qualcomm Incorporated | CR
13 | R4-2010817 | SNR evaluation for NR V2X | Huawei, HiSilicon | other