## Slide 1: WF on EVM measurement for UL-MIMO
Anritsu, []
R4-2011747
3GPP TSG-RAN WG4 Meeting #96-e
Online, 17th – 28th Aug 2020
Agenda: 4.2.1
E-mail title: [96e][102] NR_NewRAT_UE_RF_Part_1
Sub-topic: 1-1
WI: NR_newRAT-Core

## Slide 2: Background
Discussions on a clarification of the EVM measurement condition for UL-MIMO are continued from last year [1] and several contributions were provided since then (e.g. [2]-[6], [13][14]). However looking at discussions in the last #95-e meeting [7], there are occasions where it is questionable that companies are aligned with assumptions of the words such as “per layer/ each layer/ each connector” with regards to a reference point for EVM calculation, variety of TPMI configuration, number of layers to be measured simultaneously, and mapping of logical antenna port and physical antenna connector.

## Slide 3: Assumption on the EVM measurement conditions for UL-MIMO
Method | Type of EVM measurement | Reference point for EVM calculation | Num. of configured layers for test | Other measurement conditions / remarks | Related paper/ Specs
1 | Definition of current FR1 EVM spec for MIMO. | UE antenna connector | 2 | EVM of two layers are measured simultaneously. UE RF front end impairments are included in the calculated EVM. | TS38.101-1 [10]
2 | New proposal of EVM test for each layer | Layer / UE antenna port | 2 | EVM of two layers are measured simultaneously by MIMO receiver in the TE. UE RF front end impairments are cancelled by estimating unbiased symbols which are derived utilizing DM-RS. | [4][6][8] Not clear if [3] applies.
3 | Similar definition with current FR2 EVM spec. for MIMO | UE antenna connector | 1 | Test is carried out in series by configuring each layer separately. UE RF front end impairments are included in the calculated EVM. | TS38.101-2 [11] [5] with a compromise. Not clear if [3] applies.
Example of assumptions on the EVM measurement conditions for UL-MIMO [12]

## Slide 4: Assumption on the EVM measurement conditions for UL-MIMO
Reference points for FR1/2 EVM measurements (for information)

## Slide 5: Per/ each/ both layer assumption with regards to test timing
Point 1 to be confirmed:
Apart from the continued discussions on whether the 2-layer measurement shall be simultaneous or not with EVM test, generally speaking, do words “per layer (or connector)”, “each layer”, and “both layer” implicitly have a sense of test timing such as simultaneous or sequential?
Per layer (or connector) : Simultaneous / Sequential/ No clear definition
Each layer (or connector) : Simultaneous / Sequential/ No clear definition
Both layer (or connector) : Simultaneous / Sequential/ No clear definition
Agreement:
No clear definition for all Per/Each/Both layer or connector. (Qualcomm/Motorola/Intel)
However, would make sense measure simultaneously. (Motorola)

## Slide 6: Layer assumption with regards to reference point
Point 2 to be confirmed:
Apart from the existing discussions on whether the reference point of the EVM measurement shall be at the antenna connector or at the logical antenna port, generally speaking, does word “layer” implicitly have a sense of the reference point?
Option 2-1) Reference point of “Layer” is the logical antenna port.
Option 2-2) Reference point of “Layer” is the physical antenna connector.
Option 2-3) Reference point of “Layer” is either antenna port or connector.
Agreement:
Option 2-1) Reference point of “Layer” is the logical antenna port. (Qualcomm, Motorola, Intel)

## Slide 7: Maximum number of Tx antenna connectors in a UE
Point 3 to be confirmed:
As agreed in the previous WF [9], the latest assumption of maximum number of Tx antenna connectors is 2 while we allow the Tx diversity feature implemented in a UE. However this agreement is not clear on whether this “2” may vary depending on a design to cover frequency ranges by 1 connector within FR1, or per UE.
Option 3-1) Depends on covered frequency ranges within FR1. (e.g. possibly 6 connectors if the UE uses 3 different antenna connectors for 3 frequency ranges in FR1.)
Option 3-2) 2 Tx antenna connectors per UE. (i.e. 2 connectors regardless with the supported band in FR1.)
Option 3-3) 4 Tx antenna connectors per UE based on the Tx diversity feature. (i.e. 2 Tx antenna connectors are active during MIMO operation.)
Option 3-4) 2Tx antenna connector per band
Agreement: Maximum number of active antenna connector is 2 during MIMO mode.
Option 3-1) Qualcomm, Motorola
Option 3-3) Rohde&Schwarz, Skyworks
Option 3-4) Intel

## Slide 8: Mapping between antenna port and connector in a UE
Point 4 to be confirmed:
As agreed in the previous WF [9], the latest assumption of maximum number of Tx antenna connectors is 2 while we allow the Tx diversity feature implemented in a UE. Then can we assume that the mapping between a logical antenna port and a physical antenna connector is 1 by 1 during the MIMO operation?
Option 4-1) 1 by 1 per frequency range in FR1 (depends on the outcome of Point 3)
Option 4-2) Not decided yet.
Option 4-3) Not specified (There is no standards mandate on how logical to physical mapping should take place)
Option 4-4) 1 by 1 per band mapping is preferred.
Agreement: This subject is still inconclusive.
Option 4-3) Not specified (There is no standards mandate on how logical to physical mapping should take place) (Qualcomm, Motorola)
Option 4-4) 1 by 1 per band mapping is preferred (Intel)

## Slide 9: Number of configured layers for EVM test of UL-MIMO in FR1
Point 5 to be confirmed:
There are still different views regarding the number of configured layers for EVM test of UL-MIMO in FR1.
Option 5-1) 1 layer (same as the current alternative method in FR2)
Option 5-2) 2 layers (as already defined in TS 38.101-1)
Agreement:
Option 5-2) 2 layers (as already defined in TS 38.101-1) (Qualcomm, Motorola, Intel)

## Slide 10: Reference point of EVM in FR1 during two-layer test
Point 6 to be confirmed:
There are still different views regarding the reference point of EVM in FR1 with two layer simultaneous test.
Option 6-1) At the physical antenna connector. UE RF front-end impairments are included in the calculated EVM.
Option 6-2) At the logical antenna port. UE RF front-end impairments are cancelled during the calculation of EVM.
Agreement: This subject is still inconclusive.
Option 6-1) Ericsson, Huawei (from 1st round comments and contribution), Intel
Option 6-2) Qualcomm, Motorola

## Slide 11: Reference point of EVM in FR2 during two-layer test
Point 7 to be confirmed:
Analysis on the influence of XPD (cross polarization discrimination) by the measurement antenna in the OTA test system was reported [12]. Can we agree Option 7-1 below? It does not mean that the current FR2 specification shall be updated soon.
Option 7-1) As a final goal of EVM measurement for 2-layer UL-MIMO, reference point of EVM calculation should be at UE antenna port when measuring 2 layers simultaneously.
Option 7-2) Further study is needed especially from the TE implementation PoV.
Agreement: This subject is still inconclusive. However at least influence of XPD with the measurement antenna needs to be taken into account.
Option 7-1) Qualcomm, Intel
Option 7-2) Huawei

## Slide 12: Way forward
Way forwards at the end of 2nd round discussion.
Outcome of Point 1 to 4 to be confirmed (related to assumptions of wording)
To eliminate ambiguities in the spec, companies are encouraged to take into account of the following assumptions when defining the EVM requirement.
Words “Per/Each/Both layer or connector” have no clear definition with test timing.
Reference point of “Layer” test is the logical antenna port.
Assumption of the maximum number of antenna connector per UE is not aligned in the group. However max number of active antenna connector is 2 during MIMO mode.
There is no standards mandate on how logical to physical mapping should take place. But one company prefers to define in the spec. Otherwise UE declaration will be needed.
Companies are encouraged to bring views on the necessity of the 1 by 1 mapping between logical antenna ports and physical antenna connectors.

## Slide 13: Way forward
Way forwards at the end of 2nd round discussion.
Outcome of Point 5 to 6 to be confirmed (related to the test method in FR1)
Agreement: Number of configured layers for FR1 EVM is 2 as already defined in TS 38.101-1.
Companies are encouraged to continue discussions with the following aspect of EVM measurement for UL-MIMO in the next meeting.
- Reference point (at logical antenna port or at physical antenna connector)
Outcome of Point 7 to be confirmed (related to the test method in FR2)
Still need further discussions on the reference point of EVM test in FR2. XPD of the measurement antenna needs to be taken into account.

## Slide 14: Reference
[1] R4-1907967,” TX EVM test condition correction for ULMIMO”, Qualcomm Inc., RAN4 #92, Ljublajana, Slovenia
[2] R4-1913226, “TX EVM test condition correction for ULMIMO”, Qualcomm Inc., RAN4 #93, Reno, USA
[3] R4-2006777, “CR to 38.101-1: Revision to ULMIMO EVM spec”, Qualcomm Inc., RAN4 #95-e, Online
[4] R4-2004791, “EVM Definitions for Antenna Ports and MIMO Layers”, Motorola Mobility, RAN4 #94-e-bis, Online
[5] R4-2004866, “FR1 TX EVM test condition correction for ULMIMO”, Qualcomm Inc., RAN4 #94-e-bis, Online
[6] R4-2008214, “On UL MIMO Tx EVM requirement”, Huawei, Hisilicon, RAN4 #95-e, Online
[7] R4-2008934, “Email discussion summary for [95e][103] NR_NewRAT_UE_RF_Part_2”, Moderator (MediaTek Inc.), RAN4 #95-e, Online
[8] R4-2008404, “WF on EVM Requirement for UL MIMO Transmission”, Motorola Mobility, RAN4 #95-e, Online
[9] R4-2008462, “WF on Uplink Full Power Transmission”, Samsung, RAN4 #95-e, Online
[10] TS 38.101-1, “User Equipment (UE) radio transmission and reception; Part 1: Range 1 Standalone”, V16.4.0, 2020-06
[11] TS 38.101-2, “User Equipment (UE) radio transmission and reception; Part 2: Range 2 Standalone”, V16.4.0, 2020-06

## Slide 15: Reference
[12] R4-2009655, “Clarification of assumption on EVM measurement for UL-MIMO”, Anritsu corp., RAN4 #96-e, Online
[13] R4-2011520,” On the Transmit EVM Requirement for UL MIMO Transmission”, Lenovo, Motorola Mobility, RAN4 #96-e, Online
[14] R4-2010810, “On UL MIMO Tx EVM requirement”, Huawei, HiSillicon, RAN4 #96-e, Online