## Slide 1: WF on MR-DC RRM requirements
Nokia, Nokia Shanghai Bell
3GPP TSG-RAN4 Meeting #96e
E-meeting, August 17th – 28th, 2020
R4-2012246
Document for: Approval

## Slide 2: Background
During the RAN4#96e E-meeting the dicussion related to Multi-RAT Dual-Connectivity and Carrier Aggregation enhancements [LTE_NR_DC_CA_enh] continued.
Agreements made during the meeting are captured in this WF.
Summary of the discussions during RAN4#96e meeting (round 1 and round 2) is captured in R4-2012212.
  Ageements based on the discussions are captured in same document.
  Additional ageements may be captured in chairman meeting minutes.

## Slide 3: Agreements Topic #1: NR measurements for EMR (38.133)
Issue 1-2-2-1: Number of non-overlapping EMR carriers:
  The number of non-overlapping inter-frequency EMR carriers is ≤7
Issue 1-2-2-2: Number of non-overlapping EMR carrier when the total number limit is exceeded:
  RAN4 will not define requirements for number of non-overlapping EMR carrier when the total number limit is exceeded
Issue 1-2-3-1: NR inter-frequency beam-level measurement capability:
  RAN4 agree following related to NR inter-frequency beam-level measurement capability:
    FR1: 7 SSBs with different SSB index and/or PCI per inter-frequency layer
    FR2: 10 SSBs with different SSB index and/or PCI per inter-frequency layer

## Slide 4: Agreements Topic #1: NR measurements for EMR (38.133)
Issue 1-2-5-1: For overlapping EMR carriers:
  For overlapping EMR carriers, the UE measurement accuracy requirements for carriers configured for EMR:
    RAN4 to define relaxed NR measurement requirements for overlapping carrier compared to existing NR inter-frequency requirements in terms of SNR and accuracy
    LTE inter-RAT measurement requirements for overlapping carrier follows existing LTE inter-frequency requirements for CA Idle mode measurements for overlapping carrier

## Slide 5: Agreements Topic #2: NR measurements for EMR (36.133)
Sub-topic#2-1: s-NonIntraSearch thresholds and EMR carriers:
  s-NonIntraSearch thresholds and NR inter-RAT EMR carriers follow agreements for NR measurements for EMR.
Sub-topic#2-2: Capturing the UE capability:
  Capture the UE capability according to the proposed applicability text in 36.133 (R4-2010569) with necessary name correction.
Sub-topic#2-3: Number of NR Inter-RAT EMR carriers to measure:
  UE should be able to measure up to 8 overlapping and non-overlapping inter-RAT NR EMR carriers in total:
    Overlapping NR inter-RAT carriers: ≤8
    Non-overlapping NR inter-RAT carriers: ≤2

## Slide 6: Agreements Topic #2: NR measurements for EMR (36.133)
Sub-topic#2-4: Measurement requirements for non-overlapping NR inter-RAT EMR carrier:
  Measurement requirements for non-overlapping NR inter-RAT carriers are defined same as overlapping NR inter-RAT carriers.
Sub-topic#2-5: Measurement accuracy requirements for NR Inter-RAT EMR carrier:
  For Measurement accuracy requirements for NR Inter-RAT EMR carrier same principles as in Issue 1-2-5-2 will be applied.
Sub-topic#2-6: Beam level measurement capability:
  For NR inter-RAT EMR, the UE beam-level measurement capability requirements for EMR is the same as the number of beams in the existing Rel-15 inter-frequency requirements for RRC_CONNECTED state:
    FR1: 7 SSBs with different SSB index and/or PCI per inter-frequency layer
    FR2: 10 SSBs with different SSB index and/or PCI per inter-frequency layer

## Slide 7: WF on Topic #1: s-NonIntraSearch thresholds and EMR carriers (38.133)
Tentative agreement:
  Option 1:
    UE applies EMR carrier measurements disregards whether the signal exceeds the configured s-NonIntraSearch thresholds
    UE will follow conventional measurement interval for both overlapping and non-overlapping EMR carrier measurements when s-NonIntraSearch thresholds are configured
      Note: conventional measurement interval is the measurement period used for cell reselection purpose
  Option 2:
    No requirements defined for the case s-NonIntraSearch thresholds are configured
  Other options are under email discussion.

## Slide 8: WF on Topic #1: s-NonIntraSearch thresholds and EMR carriers (38.133)
  Option 3 (Moderator compromise proposal):
    RAN4 does not capture in RAN4 Rel-16 specifications anything specific related to search thresholds when UE is configured to perform EMR measurements. Following is proposed:
      UE shall be able to support EMR measurement both when search thresholds are configured and when search thresholds are not configured.
      UE has to fulfil the accuracy requirements for overlapping EMR measurements as defined 38.133 (to be defined)

## Slide 9: Agreement on Sub-topic#1-3 beam-level measurement requirements (38.133)
Issue 1-2-3-3: beam-level measurement requirements:
Agreement:
  RAN4 agree to allow UE additional time period in measurement requirement for UE who supports the beam level EMR reporting:
  TtimeIndex,NR_Interf = [X]* Tmeasure,NR_Interf,
    where X is [3, 5].

## Slide 10: WF on Sub-topic#1-6 Conditions for ‘actively measured’ (38.133)
Conditions for ‘actively measured’ is FFS

## Slide 11: WF on Sub-topic#1-7 Other (38.133)
Definitions of EMR carriers
  Option 1: Follow the agreed definitions of overlapping and non-overlapping EMR carriers
  Option 2: Based on search thresholds and carrier priority
  Option 3: While T331 is running:
    overlapping carrier: a carrier configured for EMR and mobility.
    non-overlapping carrier: a carrier configured for EMR only.
  Option 5: No need for differentiation (added by Moderator)

## Slide 12: Sub-topic#2-3 Number of NR Inter-RAT EMR carriers to measure (36.133)
UE shall be able to measure at least 1 NR inter-RAT carrier for EMR per FR.
  Option 1: yes
  Option 2: no
Agreement:
  Option 2. No need to explicitly mention that the UE shall be able to measure at least 1 NR inter-RAT carrier for EMR per FR.

## Slide 13: Sub-topic#2-5 Measurement accuracy requirements for NR Inter-RAT EMR carrier (36.133)
Agreement in sub-topic 2-5 was covering non-overlapping EMR carriers.
RAN4 also need to define measurement accuracy for overlapping NR inter-RAT EMR carriers.
  Option 1: follow the agreement for overlapping EMR carriers in sub-topic 1-5 Issue 1-2-5-1
  Option 2: other
Agreement:
  Option 1:
    For overlapping inter-RAT EMR carriers, the UE measurement accuracy requirements for carriers configured for EMR:
      RAN4 to define relaxed NR measurement requirements for overlapping carrier compared to existing NR inter-RAT requirements in terms of SNR and accuracy

## Slide 14: Sub-topic#2-7 Beam level measurement requirements (36.133)
Conclusion from first round was not captured as agreement.
Agree on the conclusion from 1st round and follow agreements in 1-2-3-3:
  Option 1: yes
  Option 2: no
Agreement:
  Option 1:
    RAN4 agree to allow UE additional time period in measurement requirement for UE who supports the beam level EMR reporting:
    TtimeIndex,NR_InterRAT = [X]* Tmeasure,NR_InterRAT,
      where X is [3, 5].