## Slide 1: 3GPP TSG-RAN WG4 Meeting #96-e Electronic Meeting, 17– 28 August, 2020
Huawei, HiSilicon
WF on requirements for RSTD and UE Rx-Tx time difference measurement
R4-2012251

## Slide 2: Measurement period for RSTD (1)
The exact measurement period for RSTD is captured in CR R4-2012129 or its further revision.
If during the measurement period of one or more positioning frequency layers, MG pattern is reconfigured to enable UE to measure different DL PRS resources, the measurement period will be longer to account for RRC reconfiguration of the MG pattern
Measurement period requirements are defined independent of responseTime. RAN4 not to define any UE behaviour related to responseTime

## Slide 3: Measurement period for RSTD (2)
Open issues to be discussed at RAN4#97-e
  Calculation of PRS sample duration
    Option 1: Based on the type (type 1 or type 2) as UE used to report {N,T}
    Option 2: Based on Type 2. RSTD measurement period for Type 1 PRS duration calculation shall be no longer than Type 2.
    Note: sample duration refers to Lprs (defined as K in clause 5.1.6.5 of 38.214)
  Multiple PRS periodicities
    Option 1: Use the maximum PRS resource periodicity among all PRS resource in a same positioning frequency layer
    Option 2: Use the maximum PRS resource periodicity among all PRS resource among all configured PRS frequency layers.
  Measurement period extension due to SSB collision
    Option 1: RSTD measurement period to be defined for cases when PRS occasions are not dropped
    Option 2: The RSTD measurement period can be extended to compensate for the number of PRS symbols not available at the UE due to their overlap with SSB symbols
    Option 3: The same measurement period requirement shall be met, regardless of whether some of the PRS symbols are dropped or not during this measurement period
  Measurement period when configured with PRS-RSRP
    Option 1: If RSTD is configured together with PRS-RSRP, then the measurement periods for both measurements are defined as: max(TRSTD,TPRS-RSRP), where TPRS-RSRP and TRSTD are the measurement periods for PRS-RSRP and RSTD, when configured without other measurements.
    Option 2: RSTD measurement period is not impacted by PRS-RSRP measurement.

## Slide 4: Measurement period for UE Rx-Tx time difference (1)
The exact measurement period for RSTD is captured in CR R4-2012130 or its further revision
For UE Rx-Tx in FR1, no impact of UE RX beam sweeping on UE Rx-Tx time difference measurement period shall be considered.
Measurement period in case of HO
  UE restarts the measurement

## Slide 5: Measurement period for UE Rx-Tx time difference (2)
Open issues to be discussed at RAN4#97-e
  Whether SRS periodicity should be accounted in measurement period
    Option 1: No
    Option 2: UE Rx-Tx measurement period depends on max(PRS periodicity, SRS periodicity)
    Option 3: clarify that the requirements can be more relaxed if SRS is more sparse than PRS
  Whether SRS dropping should be accounted in measurement period
    Option 1: No, FFS: RAN4 to define requirements for UE Rx-Tx time difference measurement period assuming no SRS dropping due to any reason
    Option 2: The UE Rx-Tx measurement period can also be extended to compensate for the number of dropped SRS transmissions, at least when the number of dropped SRS transmissions is large.
    Option 3: clarify in the requirements that the measurement period can be longer if some (or more than X) SRS are dropped
  SRS/PRS proximity
    Option 1: The measurement requirements is applicable only if any SRS transmission is within [-X, X] msec of at least one DL PRS resource of each of the TRPs in the assistance data. Accuracy requirements is independent of PRS and SRS separation
    Option 2: The measurement accuracy requirements for UE Rx-Tx time difference is applicable regardless of time separation of SRS transmissions and PRS receptions. Accuracy requirements shall be a function of maximum time separation among SRS transmissions and their corresponding closest PRS receptions
    Option 3: The requirements for UE Rx-Tx apply regardless of the time separation between SRS and PRS. If the closest subframes #i and #j are separated by more than ½ subframe, the UE shall compensate for the difference in the received timing of radio frame #i used for TUE-TX estimation and the subframe #j.
    Option 4: Add proper TRS settings in both all timing accuracy requirements and test cases so that UE can compensate the crystal clock frequency offset by measuring TRS

## Slide 6: Measurement period for UE Rx-Tx time difference (3)
Open issues to be discussed at RAN4#97-e
  SRS/PRS being in same band
    Option 1: Basic requirements for UE Rx-Tx time difference measurements shall be based on the assumption that positioning SRS resources are in the same band as PRS frequency layers.
    Option 2: RAN4 to define Rx-Tx time difference requirements only for the case where SRS resource is in the same band as PRS resource.
  Measurement period in case of TA change (due to TA command)
    Option 1: UE Rx-Tx time difference measurement requirements are not applicable if TA change is received during the measurement period.
    Option 2: UE shall discard the UE Rx-Tx time difference measurement if the uplink transmission timing changes during the UE Rx-Tx measurement period.
    Option 3: UE could continue UE/gNB Rx-Tx time difference measurement during which timing adjustment for its UL transmissions.
  Measurement period in case of TA change (due to UE autonomous adjustment)
    Option 1: UE Rx-Tx time difference measurement requirements are applicable for UE autonomous adjustment of UL timing.
    Option 2: UE shall discard the UE Rx-Tx time difference measurement if the uplink transmission timing changes during the UE Rx-Tx measurement period.
  Measurement period in case of NTA_offset change
    Option 1: It is clarified in UE Rx-Tx measurement requirements (section 9.9.4 in TS 38.133) that the UE shall discard the UE Rx-Tx measurement if the NTA_offset changes during the measurement period
    Option 2: No need to clarify UE Rx-Tx measurement requirements in case of NTA_offset change.

## Slide 7: Measurement capability (1)
RAN4 not to define any additional requirements for the case when PRS configuration in assistance data exceeds reported capabilities in terms of number of PRS resources, resource sets, frequency layers, TRPs.
The applicable values for X are MGL/MGRP values of the gap patterns that are applicable for PRS measurement and supported by the UE

## Slide 8: Measurement capability (2)
Open issues to be discussed at RAN4#97-e
  Whether RAN4 to define capability requirements for PRS measurement
    Option 1: No
    Option 2: Yes
  Requirements when duration of a single PRS resource exceeding UE processing capability
    Option 1: If the time span of a DL PRS resource instance is greater than UE reported capability N, measurement requirements do not apply for this resource
    Option 2: If the capability is smaller then what is configured, then the requirements are to be relaxed.

## Slide 9: Side condition and accuracy for RSTD (1)
Open issues to be discussed at RAN4#97-e
  Side condition for FR2
    Option 1: -3dB for reference TRP and -10 dB for neighbor TRP
    Option 2: -6dB for reference TRP and -13 dB for neighbor TRP
  Number of PRS samples or PRS repetitions for defining accuracy
    Option 1: Accuracy requirements are defined based on number of PRS samples, where each samples includes a number of PRS repetitions. Single PRS sample is assumed for accuracy requirements
    Option 2: Accuracy requirements are defined based on the number of PRS comb patterns in time
  Whether accuracy requirements are agnostic to comb size
    clarify what “comb size” refers to
  Antenna panel assumption
    Option 1: RAN4 specifies at least the RSTD accuracy requirements (+/-Y dB) under the assumption of using the same antenna panel for receiving both the reference and neighbor PRS resources. For different antenna panels within the same RSTD measurement, the RSTD accuracy can be specified as +/-Y+ ΔY dB, or there can be a note that the accuracy can be worse
    Option 2: RAN4 not to define separate accuracy requirements for RSTD measured with same panel and with different panels

## Slide 10: Side condition and accuracy for RSTD (2)
Open issues to be discussed at RAN4#97-e
  Applicable PRS BW for defining accuracy
    Option 1 : If reference and neighbor PRS resources belong to different positioning frequency layers, the minimum PRS BW of the positioning frequency layers should be used for applicability of accuracy requirements.
    Option 2: FFS
  Assumption on TRS setting for defining accuracy and test
    Option 1: add proper TRS settings in both RSTD accuracy requirements and test cases so that UE can compensate the crystal clock frequency offset by measuring TRS.
    Option 2: FFS for Performance part
  Applicable accuracy requirement in case of HO
    Option 1: Define applicable accuracy requirements for RSTD measurements under cell change, considering the cases of intra-frequency HO and inter-frequency HO, e.g. the most relaxed applies between the one before and the one after the HO.
    Option 2: Applicable accuracy requirements is not impacted by HO.
  Applicable propagation channel for accuracy requirement
    Option 1: Exclude number from simulations for TDL-C channel model with 300 ns delay spread in FR1 from consideration for defining the RSTD and UE Rx-Tx timing difference accuracy requirements.
    Option 2: Take into account number from simulations for TDL-C channel model with 300 ns delay spread in FR1 from consideration for defining the RSTD and UE Rx-Tx timing

## Slide 11: Side condition and accuracy for UE Rx-Tx time difference (1)
For defining UE Rx-Tx time difference accuracy requirements, follow the same conclusion for RSTD on
  Number of PRS occasions or PRS repetitions for defining accuracy
  Whether accuracy requirements are agnostic to comb size
  Antenna panel assumption
  Applicable propagation channel for accuracy requirement

## Slide 12: Side condition and accuracy for UE Rx-Tx time difference (2)
Open issues to be discussed at RAN4#97-e
  Accuracy for serving/neighbor cells
    Option 1: Only one set of accuracy requirements applicable to both serving and neighbor cells to be defined
    Option 2: Define separate side conditions for serving and neighbor cells
      Serving cell side condition for UE Rx-Tx: -3 dB, for FR1 and FR2
      FFS: same or different requirements for serving and neighbor cells
  Rx-Tx calibration error budget at UE and gNB
    Option 1: The Rx-Tx calibration error budget at UE and gNB shall be defined to be of the same scale.
    Option 2: FFS in Performance part
  Applicability of accuracy requirements in case of HO
    Option 1: UE Rx-Tx time difference accuracy requirements do not apply with HO during the measurement period.
    Option 2: Define the applicable accuracy requirements for UE Rx-Tx measurements under cell change, considering the cases of intra-frequency HO and inter-frequency HO
  Applicability of accuracy requirements in case of NTA_offset change
    Option 1: RAN4 not to capture applicability of UE Rx-Tx time difference accuracy requirements under NTA_offset change during the measurement period
    Option 2: Clarify in section 10.1.25.2 in TS 38.133: “UE Rx-Tx time difference accuracy requirements shall not apply if NTA_offset defined in Table 7.1.2-2 in 38.133 changes during the UE Rx-Tx measurement period.”

## Slide 13: Report mapping
Open issues to be discussed at RAN4#97-e
  Relation between k1 and k2
    Option 1 :
      i is the positioning layer frequency layer index of all RSTD measurements of the same TRP pair.
    Option 2: k2 >= k1
    Option 3: RAN4 not to define relationship between k1 and k2
    Option 4: k2 <= k1
    Option 5: the UE shall choose k2 <= k1 if it supports at least one such k2, otherwise the UE may choose k2>k1 (the smallest value of k2 supported by the UE can be UE capability).
  Applicable values for k in FR1
    Option 1: {1,2,3,4,5}
    Option 2: {2,3,4,5}
    Option 3: {0,1,2,3,4,5}
    Option 4: {3,4,5}