## Slide 1: WF on spatial relation switch
Mediatek Inc.
3GPP TSG-RAN WG4 #96-e Meeting
Electronic Meeting, 17th - 28th Aug. 2020
R4-2012258

## Slide 2: Background
In RAN Plenary #86, the WI of NR RRM enhancement requirements for R16 was revised. The following issue is agreed to be discussed.
  Active spatial relation switch for uplink
Scenario overview
# | Scenario | PHY channel | Triggering method | associated source | Whether to introduce requirement
1 | PUCCH-RRC-DL | PUCCH | RRC | DL RS | No
2 | PUCCH-RRC-UL | PUCCH | RRC | UL SRS | No
3 | PUCCH-MAC-DL | PUCCH | MAC | DL RS | Yes
4 | PUCCH-MAC-UL | PUCCH | MAC | UL SRS | No
5 | PUSCH-DCI | PUSCH | DCI | - | No
6 | pSRS-RRC-DL | P-SRS | RRC | DL RS | Yes
7 | pSRS-RRC-UL | P-SRS | RRC | UL SRS | No
8 | spSRS-MAC-DL | SP-SRS | MAC | DL RS | Yes
9 | spSRS-MAC-UL | SP-SRS | MAC | UL SRS | No
10 | aSRS-DCI-DL | A-SRS | DCI | DL RS | Yes
11 | aSRS-DCI-UL | A-SRS | DCI | UL SRS | No

## Slide 3: Agreement
  No consensus to define requirements for UL signal that has spatial relation to an unknown DL RS. Companies can further bring contributions as a part of maintenance.
Do not consider timing tracking when associated DL-RS is known but QCLed with a different qcl-Type1 RS
Define delay requirement for MAC CE based spatial relation info switching associated with DL-RS for PUCCH and SP-SRS
  For known spatial relation but the DL RS is not in the active TCI list: (THARQ +3ms)/NR slot length
Delay requirement for RRC based spatial relation info switching associated with DL-RS for P-SRS
  For known spatial relation but the DL RS is not in the active TCI list: TRRCprocessing/NR slot length

## Slide 4: Way Forward
When the UL signal has spatial relation to an unknown DL RS,
  Option 1: Do not define requirements
  Option 2: Define requirements

## Slide 5: Way Forward
If the answer of the issue in slide 4 is Option 2,
  Define delay requirement for MAC CE based spatial relation info switching associated with DL-RS for PUCCH and SP-SRS
  For unknown spatial relation
    Option 1: THARQ + 3ms+ TL1-RSRP
    Option 2: THARQ + 3ms+ TL1-RSRP + time for time tracking if applicable
  Delay requirement for RRC based spatial relation info switching associated with DL-RS for P-SRS
  For unknown spatial relation
    Option 1: TRRCprocessing + TL1-RSRP
    Option 2: TRRCprocessing + TL1-RSRP + time for time tracking if applicable

## Slide 6: Way Forward
If the answer of the issue in slide 4 is Option 2,
Sub 1. Whether to define UE behavior during the transition period when UL signal is configured with unknown DL-RS? (Where the transition period is the period after THARQ + 3ms or TRRCprocessing to UE finished spatial relation switch.)
  Option 1: Define
  Option 2: Do not define
Sub 2. If the answer of the sub 1 is Option 1,
  What’s the UE behavior during the transition period when UL signal is configured with unknown DL-RS?
    Option 1: UE transmits using previous TX beam
    Option 2: Drop UL transmission until spatial relation info is known