## Slide 1: Way forward on UE power imbalance requirements for FR1 CA and EN-DC
NTT DOCOMO
3GPP TSG-RAN4 Meeting #96-e Electronic Meeting, 17 - 28 Aug, 2020 Agenda item: 7.16.1.4
R4-2012691

## Slide 2
RAN4 # 95-e
  WF: R4-2008848
Background: WF in previous meeting

## Slide 3: Wayforward
For FR1 intra-band contiguous CA
Channel bandwidth combination for defining performance requirements
  Define generic methodology for selection of CBW combination among all CBW combinations in supported CA configurations, and define bandwidth agnostic requirements.
Channel bandwidth combination for testing
  As baseline, use the following approach
    Step 1: First select the CBW combinations with the same BWs in each carrier
      If there is no such CBW combination, select the CBW combinations with smallest CBW difference between the two carriers, and the carrier with smaller CBW will be used for test.
    Step 2: Among the CBW combinations selected from step 1, select the CA combination with largest aggregated CBW

## Slide 4: Wayforward
For FR1 intra-band contiguous CA
PDSCH RB allocation
  Full RB allocation
MCS
  Modulation order: 64QAM for 2Rx and 4Rx
  MCS
    Option 1: MCS 27 for 2Rx, MCS 28 for 4Rx
    Option 2: MCS 25 for 2Rx
Applicability rule
  Option 1: Reuse the following applicability rule from LTE CA power imbalance test
    For FDD or TDD CA power imbalance tests, if they are tested with FDD or TDD intra-band contiguous CA configurations with 2 DL CCs, the test coverage can be considered fulfilled with FDD or TDD intra-band contiguous CA configurations with 3 or more DL CCs supported by the UE.
    For FDD or TDD 2 DL CCs, only test the supported intra-band contiguous CA configurations covering the lowest and highest operating bands.
  Other options are not precluded.

## Slide 5: Wayforward
For intra-band contiguous and non-contiguous EN-DC
Tested carrier
  Allocate the test RBs on NR carrier
Channel bandwidth combination for defining performance requirements
  Reuse the agreement from FR1 intra-band contiguous CA
    Define generic methodology for selection of CBW combination among all CBW combinations in supported EN-DC configurations, and define bandwidth agnostic requirements.
SCS (TDD)
  Option 1: 30kHz
  Option 2: 15kHz and 30kHz
    Test #2b: LTE TDD + NR TDD 30 kHz, in case UE supports it, otherwise LTE TDD + NR TDD 15 kHz
TDD pattern for 15kHz SCS (if needed)
  Option 1: DSU+DD
  Option 2: DDDSU
  Option 3: Not need

## Slide 6: Wayforward
For intra-band contiguous and non-contiguous EN-DC
RAN4 uses the following test parameters if no technical issues will be figured out.
For the other test parameters and applicability rules, if not explicitly discussed, reuse the same agreements from CA power imbalance test.
Parameters | Value
Reference testing point | 85% of maximum throughput
PDSCH DMRS configurations | DMRS type: Type 1 Number of additional DMRS: 1 (i.e., 1+1)
Transmission rank | Rank 1
MCS | Same value as FR1 intra-band contiguous NR CA
Max number of HARQ transmission | 1 (RV = {0})
Precoding configuration | SP Type I, Random per slot with PRB bundling granularity
PRB bundling size | WB

## Slide 7: Wayforward
For intra-band contiguous EN-DC and non-contiguous EN-DC
Channel bandwidth combination for testing
  Option 1
    Step 1: First select the CBW combinations with the same BWs in each carrier
      If there is no such CBW combination, select the CBW combinations with smallest CBW difference between the two carriers.
    Step 2: Among the CBW combinations selected from step 1, select the CBW combinations where the NR carrier has smaller CBW than the LTE carrier; if no such CBW combination, directly go to step 3.
    Step 3: Among the CBW combinations selected from step 2, select the EN-DC combination with largest aggregated CBW
  Option 2
    Step 1: First select the CBW combinations with the same BWs between LTE carrier (single carrier or aggregated carriers) and NR carrier
      If there is no such CBW combination, select the CBW combinations with smallest CBW difference between the two carriers.
        If frequency range of NR carrier is higher than LTE carrier, then the test RBs will be allocated on the highest part of NR carrier.
        If frequency range of NR carrier is lower than LTE carrier, then the test RBs will be allocated on the lowest part of NR carrier.
    Step 2: Among the CBW combinations selected from step 1, select the EN-DC combination with largest aggregated CBW.
  Option 3
    Step 1: First select the CBW combinations with the same BWs in each carrier. If there is no such CBW combination, go to Step 1a and Step 1b, otherwise Step 2.
      Step 1a: Select the CBW combinations that the BW of NR carrier is smaller than the BW of LTE carrier
      Step 1b: Among the CBW combinations selected from Step 1a, select the CBW combinations with the smallest CBW difference between the two carriers
    Step 2: Among the CBW combinations selected from Step 1, select the EN-DC combination with the largest aggregated CBW
  Option 4
    Step 1: First select the CBW combinations with the same BWs between LTE carrier (single carrier or aggregated contiguous carriers) and NR carrier. If there is no such CBW combination, go to Step 1a, Step 1b and Step 1c.
      Step 1a: Select the CBW combinations that the BW of NR carrier is smaller than the (aggregated) BW of LTE carrier(s). If there is no such CBW combination, go to Step 1c.
      Step 1b: Among the CBW combinations selected from Step 1a, select the CBW combinations with the smallest CBW difference between NR carrier and LTE carrier(s)
      Step 1c: select the EN-DC combinations with smallest CBW difference between the NR carrier and LTE carrier(s).
    Step 2: Among the CBW combinations selected from Step 1, select the EN-DC combination with the largest aggregated CBW
  Other options are not precluded.

## Slide 8: Wayforward
For intra-band contiguous and non-contiguous EN-DC
Channel bandwidth combination for testing
  Whether to consider the aggregated contiguous carriers for LTE if UE supports it?
    Option 1: Consider the aggregated contiguous carriers for LTE
    Option 2: Do not consider the aggregated contiguous carriers for LTE
  Whether to test partial PRB or full PRB for NR carrier, in case the CBW is different in LTE carrier(s) and NR carrier?
    Option 1: Partial PRB
    Option 2: Full PRB
LO position
  Option 1: “LO in middle” (1st priority)
  Option 2: “LO in middle” and “LO at edge of one CC” (2nd priority)
    FFS: Channel bandwidth combination for testing
    FFS: whether some limitations on frequency separation between two CCs should be included in applicability rule for non-contiguous EN-DC

## Slide 9: Wayforward
For intra-band non-contiguous EN-DC
Test applicability rules
  Option 1
    UE supports only intra-band contiguous EN-DC, i,e., if UE does not indicate “intraBandENDC-Support”,
      power imbalance requirement for intra-band contiguous EN-DC is applied
    UE supports only intra-band non-contiguous EN-DC, i.e., if UE indicates “non-contiguous” in “intraBandENDC-Support” or UE does not indicate “interBandContiguousMRDC”,
      power imbalance requirement for intra-band non-contiguous EN-DC is applied
    UE supports both intra-band contiguous and non-contiguous EN-DC, i.e., if UE indicates “both” in “intraBandENDC-Support” or UE indicates “interBandContiguousMRDC”,
      power imbalance requirement for FR1 intra-band contiguous EN-DC
  Option 2
    UE supports only intra-band contiguous EN-DC, i,e., if UE does not indicate “intraBandENDC-Support”,
      power imbalance requirement for intra-band contiguous EN-DC is applied
    UE supports only intra-band non-contiguous EN-DC, i.e., if UE indicates “non-contiguous” in “intraBandENDC-Support”
      power imbalance requirement for intra-band non-contiguous EN-DC is applied
    UE supports both intra-band contiguous and non-contiguous EN-DC, i.e., if UE indicates “both” in “intraBandENDC-Support”
      power imbalance requirement for FR1 intra-band contiguous EN-DC