## Slide 1: 3GPP TSG-RAN WG4 Meeting #96-e Electronic Meeting, 17– 28 August, 2020
Huawei, HiSilicon
WF on requirements for RSTD and UE Rx-Tx time difference measurement
R4-2012127

## Slide 2: Measurement period for RSTD (1)
The exact measurement period for RSTD is captured in CR R4-2012129 or its further revision.
If during the measurement period of one or more positioning frequency layers, MG pattern is reconfigured to enable UE to measure different DL PRS resources, the measurement period will be longer to account for RRC reconfiguration of the MG pattern
Measurement period requirements are defined independent of responseTime. RAN4 not to define any UE behaviour related to responseTime

## Slide 3: Measurement period for RSTD (2)
Open issues to be discussed at RAN4#97-e
  Calculation of PRS occasion duration
  Multiple PRS periodicities
  Measurement period extension due to SSB collision
  Measurement period when configured with PRS-RSRP

## Slide 4: Measurement period for UE Rx-Tx time difference (1)
The exact measurement period for RSTD is captured in CR R4-2012130 or its further revision
For UE Rx-Tx in FR1, no impact of UE RX beam sweeping on RSTD measurement period shall be considered.

## Slide 5: Measurement period for UE Rx-Tx time difference (2)
Open issues to be discussed at RAN4#97-e
  Whether SRS periodicity should be accounted in measurement period
  Whether SRS dropping should be accounted in measurement period
  SRS/PRS proximity
  SRS/PRS being in same band
  Measurement period in case of HO
  Measurement period in case of TA change (due to TA command)
  Measurement period in case of TA change (due to UE autonomous adjustment)
  Measurement period in case of NTA_offset change

## Slide 6: Measurement capability (1)
RAN4 not to define any additional requirements for the case when PRS configuration in assistance data exceeds reported capabilities in terms of number of PRS resources, resource sets, frequency layers, TRPs.
The applicable values for X are MGL/MGRP values of the gap patterns that are applicable for PRS measurement and supported by the UE

## Slide 7: Measurement capability (2)
Open issues to be discussed at RAN4#97-e
  Whether RAN4 to define capability requirements for PRS measurement
  Requirements when duration of a single PRS resource exceeding UE processing capability

## Slide 8: Side condition and accuracy for RSTD
Open issues to be discussed at RAN4#97-e
  Side condition for FR2
  Number of PRS occasions or PRS repetitions for defining accuracy
  Whether accuracy requirements are agnostic to comb size
  Antenna panel assumption
  Applicable PRS BW for defining accuracy
  Assumption on TRS setting for defining accuracy and test
  Applicable accuracy requirement in case of HO
  Applicable propagation channel for accuracy requirement

## Slide 9: Side condition and accuracy for UE Rx-Tx time difference (1)
For defining UE Rx-Tx time difference accuracy requirements, follow the same conclusion for RSTD on
  Number of PRS occasions or PRS repetitions for defining accuracy
  Whether accuracy requirements are agnostic to comb size
  Antenna panel assumption
  Applicable propagation channel for accuracy requirement

## Slide 10: Side condition and accuracy for UE Rx-Tx time difference (2)
Open issues to be discussed at RAN4#97-e
  Accuracy for serving/neighbor cells
  Rx-Tx calibration error budget at UE and gNB
  Applicability of accuracy requirements in case of HO
  Applicability of accuracy requirements in case of NTA_offset change

## Slide 11: Report mapping
Open issues to be discussed at RAN4#97-e
  Relation between k1 and k2
  Applicable values for k in FR1