## Slide 1: WF on CSI-RS based L3 measurement requirements
OPPO
3GPP TSG-RAN4 Meeting #96e
Electronic Meeting, 17– 28 Aug., 2020
R4-2012178

## Slide 2: Sub-topic 2-1: Measurement delay
Keep agreements in last meeting and clarify whether SBI acquisition can be skipped
  Cell identification and measurement period
    T CSI-RS_identify_intra = (TPSS/SSS_sync + T CSI-RS_measurement_period_intra + TSSB_time_index) ms
    T CSI-RS_identify_inter = (TPSS/SSS_sync + T CSI-RS_measurement_period_inter + TSSB_time_index) ms
    If deriveSSB-IndexFromCell is indicated, UE can skip PBCH decoding for intra-frequency measurement, i.e., TSSB_time_index = 0.
    If UE has already detected the SSB of the target cell, UE can skip cell detection, i.e., TPSS/SSS_sync = 0.

## Slide 3: Sub-topic 2-2: Tuning time of inter-frequency GAP of CSI-RS measurement
  The tuning time for CSI-RS based measurement is equal to the gap switch time for measuring the inter-frequency SSBs

## Slide 4: Sub-topic 2-3: Restriction on CSI-RS resources configuration
Introduce the same time domain restriction for intra-frequency measurement and inter-frequency measurement in Rel-16.
  Do not associate CSI-RS location with SMTC
  CSI-RS resources per frequency layers are configured within 5 ms window at any location
  CSI-RS periodicities for L3 measurement: 10, 20, 40 ms
  Up to 1 CSI-RS periodicity can be configured per CSI-RS intra-frequency layer
  Up to 1 CSI-RS periodicity can be configured per CSI-RS inter-frequency layer
  The exact relative location between CSI-RS and SMTC can be decided by NW to make sure a single MG pattern can cover both CSI-RS and SMTC for inter-frequency layer.
  Note: the restrictions above are the conditions to apply the requirements for both Core and Performance part
Do not introduce frequency domain restriction

## Slide 5: Sub-topic 2-4: Rx beam sweeping
UE is allowed to perform Rx beam sweeping for CSI-RS based L3 measurement in FR2, in the case that
  CSI-RS resources in the same OFMD symbol are QCL-ed with different associated SSB
Scaling factor N = [8] for RX beam sweeping in FR2 band

## Slide 6: Sub-topic 2-7: Scheduling Restriction for intra-frequency measurement
Issue 2-7-3: When UE performs Rx beam sweeping in FR2 band:
  Scheduling restriction apply for data OFDM symbols overlapped by to-be-measured CSI-RS resources only.
Issue 2-7-2: When UE performs CSI-RS intra-frequency measurements in a TDD band
  FFS: UE is not expected to transmit on data OFDM symbols overlapped by CSI-RS resource symbols to be measured, and [1] OFDM symbols before and after each consecutive CSI-RS symbols

## Slide 7: Sub-topic 2-7: Scheduling Restriction
Issue 2-7-4: Whether to specify scheduling restriction for associated SSB
  The scheduling restriction for associated SSB should also be specified, and the existing SSB requirements can be re-used.

## Slide 8: Sub-topic 2-8: Measurement Restriction
Do not define CSI-RS measurement requirements in Rel-16 for the collision case:
  Collision between CSI-RS L3 measurement of neighbor cell and serving cell measurement for RLM/BFD or other CSI-RS L1 measurements

## Slide 9: Reference
R4-2009009, WF on CSI-RS based L3 measurement capability and requirements, OPPO
R4-2012056, Email discussion summary for [96e][225] NR_CSIRS_L3meas_RRM_2, OPPO