## Slide 1: WF on gNB requirements for NR positioning
Ericsson
3GPP TSG-RAN WG4 Meeting # 96-e
Electronic Meeting, August 17-28, 2020
Agenda: 7.7
R4-2012140

## Slide 2: SRS configurations for gNB measurement accuracy
SRS configurations for defining accuracy requirements are derived from link level simulations.
SRS configurations for which accuracy requirements are met are FFS.

## Slide 3: Accuracy dependency on SRS BW
gNB positioning measurement accuracy is defined based on the SRS BW.

## Slide 4: Selection of option for gNB measurement accuracy requirements
FFS: gNB measurements for which accuracy shall be defined.
Candidate options:
  Option 1:
    Define accuracy for SRS-RSRP and gNB Rx-Tx time difference
  Option 2:
    Define accuracy for SRS-RSRP, gNB Rx-Tx time difference and UL RTOA

## Slide 5: Optionality of gNB accuracy requirements
FFS: whether gNB positioning measurement accuracy is optional or mandatory if gNB supports the positioning measurement.
Candidate options:
  Option 1:
    Mandatory for gNB to meet accuracy for supported positioning measurement
  Option 2:
    Optional for gNB to meet accuracy for supported positioning measurement

## Slide 6: Side conditions for gNB measurement accuracy
Issue-1: FFS: One set or separate set of side conditions (e.g. SINR) for defining gNB positioning measurement accuracy.
  Option 1:
    One set of side conditions to meet accuracy for UE in serving as well as in neighbour cells
  Option 2:
    Separate side conditions to meet accuracy for UE in serving and for UE in neighbour cells
Issue-2: FFS: Methodology for deriving gNB positioning measurement accuracy.
  Candidate options for deriving side conditions:
    Option 1:
      Side conditions based on clause 7.2, TS 36.111
    Option 2:
      Side conditions derived from system simulations

## Slide 7: Beam configuration for gNB measurement accuracy
FFS: Antenna beam configuration assumption in gNB for defining gNB positioning measurement accuracy.
Candidate options:
  Option 1:
    Fixed antenna beams are assumed in gNB for deriving accuracy
  Option 2:
    Accuracy does not depend on antenna beam configuration in gNB i.e. do not assume fixed gNB antenna beams

## Slide 8: SRS configurations for gNB measurement accuracy
FFS: Whether accuracy is defined and met for all or subset of SRS configurations:
Candidate options:
  Option 1:
    Accuracy is defined for all SRS configurations but is met only for subset of SRS configurations declared by the manufacturer
  Option 2:
    Accuracy is defined and met for subset of SRS configurations.

## Slide 9: Accuracy for different BS types (1-C, 1-H, 1-O, 2-O)
gNB positioning measurement accuracy requirement depends on BS type (1-C, 1-H, 1-O, 2-O).
  Note: This issue can be further checked after the side condition is defined.