## Slide 1
WF on work scope and general assumptions for NR V2X demodulation performance
3GPP TSG-RAN WG4 Meeting #96-e Electronic Meeting, 17 – 28 August, 2020
Agenda Item: 7.3.7
R4-2012612
LG Electronics

## Slide 2: Specification structure
Spec. structure for NR V2X demodulation
  Introduce new section (such as chapter 11) for NR V2X performance requirements in TS38.101-4
  Further discuss the detailed section title
e.g.) 11. V2X requirements 11.1 Demodulation performance requirements (conducted requirements) 11.1.1 General 11.1.2 PSSCH demodulation requirements 11.1.3 PSCCH demodulation requirements 11.1.4 PSBCH demodulation requirements 11.1.5 PSFCH demodulation requirements ...

## Slide 3: Work scope
List of test cases to define demodulation performance requirements in Rel-16
  Whether to define SDR with active sidelink test case need further discussion
 | Test cases | Note
Single link test | PSSCH demodulation | 
 | PSCCH demodulation | 
 | PSBCH demodulation | 
 | PSFCH demodulation | 
Multiple link test | Power imbalance test | 
 | HARQ buffer soft combining | Just one test depending on UE capability declaration
 | PSCCH/PSSCH decoding capability | 
 | PSFCH decoding capability | 
 | [SDR with active sidelink] | 

## Slide 4: Work scope
Do not define 2nd-stage SCI performance requirement explicitly
Do not define performance requirements for CSI reporting in Rel-16

## Slide 5: Reference receiver
Common assumptions for reference receiver
  LTE V2X reference receiver assumption is used as starting point.
  Companies are encouraged to provide which algorithm used for CFO and CE when simulation results are provided in next meeting if diverse simulation results from companies are observed.

## Slide 6: General simulation assumption
Frequency range
  Define performance requirements for FR1 only
Antenna configuration
  1T2R antenna configuration
Channel bandwidth and SCS
  20MHz CBW and 30kHz SCS as baseline for performance tests without maximum PSCCH/PSSCH allocation
  FFS on CBW for PSCCH/PSSCH decoding capability test
    Option 1: 20MHz
    Option 2: 40MHz
Rank for PSSCH
  Define performance requirements based on Rank 1
Propagation condition
  TDL-A 30ns as baseline

## Slide 7: General simulation assumption
Relative velocity for test cases
  Candidate values for test cases
    30km/h
    260km/h
    500km/h
The number of DMRS for PSSCH
  Option 1: Following cases can be used depending on decision on relative velocity
    Case 1: Max speed: 500km/h DMRS symbol: 4 for slots without PSFCH, 3 for slots with PSFCH.
    Case 2: Moderate speed: 260km/h DMRS symbol: 3 for slots without PSFCH, 2 for slots with PSFCH
    Case 3: low speed: 30km/h DMRS symbol: 2 for slots with/without PSFCH
  Option 2: 3 DMRS symbols for all test cases
  Other options are not precluded

## Slide 8: General simulation assumption
TO and FO
  Tx UE side
    FO: 0.1ppm for GNSS
    TO: 12Ts for GNSS 0 if Tx UE is used as SyncRefUE, otherwise 8Ts
    TO/FO are values with respect to sync source reference timing/frequency
  Rx UE side
    FO: 0.2ppm for GNSS 0.1ppm for SyncRefUE
    TO: 24Ts for GNSS 8Ts (30kHz SCS) for SyncRefUE
    TO/FO are values with respect to Tx UE timing/frequency
      TO/FO are sum of TO/FO from Tx UE and TO/FO for Rx UE itself
  FFS on TO and FO based on gNB sync source if gNB based test case is agreed to define

## Slide 9: General simulation assumption
Feedback loop for test method
  PSFCH feedback instead of AT commands can be used to test NR V2X UE’s performance
  PSFCH configuration for test cases
    PSFCH are transmitted on
      Option 1: every 4 slots
      Option 2: every slot
Number of S-SSB per SL period for 30kHz SCS
  Option 1: 1
  Option 2: 2
256QAM reception capability
  256QAM reception is an optional UE capability.
  FFS on introduction of 256QAM demodulation test case

## Slide 10: Work split
Work split for draft CR
Test case | Volunteer company | Note
General part | Intel | 
PSSCH demodulation test | LG Electronics | 
PSCCH demodulation test | Intel | 
PSBCH demodulation test | CATT | 
PSFCH demodulation test | MediaTek | 
Power imbalance test | Huawei | 
PSCCH/PSSCH decoding capability | Huawei | 
HARQ buffer soft combining | [Qualcomm] | 
PSFCH decoding capability | [Huawei or MediaTek] | 
SDR with active sidelink |  | No decision yet
Big one CR | LG Electronics | It includes all draft CRs for test cases and related configuration.

## Slide 11: Power imbalance test
Methodology for power imbalance test as starting point(reuse LTE V2X)
  The target requirement ICS = X dBc (for information, -27dBc has been used for LTE V2X)
  Select SINR2 from simulation results for SNR@10% BLER point.
  Select SNR2 such that SNR2 >> SINR2 (e.g., 5dB higher)
  Compute SNR1 from the relation: SINR2 = SNR2 – 10*log10(10^((SNR1 + ICS)/10)+1).
Companies are encouraged to provide simulation assumptions to derive SINR2 and ICS level in the next meeting, and also other methodologies are not precluded.