## Slide 1: Rel-16 FR1 intra-band UL CA GTW status
Moderator (Huawei, HiSilicon)
R4-200XXXX
3GPP TSG-RAN WG4 #96-e
August 17th – 28th, 2020
Electronic meeting

## Slide 2: Background
Two major topics related to UE feature under discussion:
  Additional DC location reporting for intra-band UL CA
    In Rel-15, 3301(undetermined location) is allowed to report for intra-band UL CA, considering LO shift when CCs are activated/deactivated
    Goal: explicit DC location for intra-band UL CA can be reported to network
  UE feature for intra-band uplink CA
    For intra-band contiguous uplink CA, WF(R4-2008466) agrees on the MPR requirement applicability on PA architecture, i.e. 1PA architecture for BW class B, 1PA and 2PA architecture for BW class C
    For intra-band non-contiguous uplink CA, WF(R4-2005660) agrees on the relation among frequency separation, MIMO and PA architecture, i.e.
      1PA/1LO:
        instantaneous TX bandwidth: ~200MHz
        Number of TX chain: 1 (2TX to support UL MIMO)
      2PA/2LO:
        instantaneous TX bandwidth: >200MHz can be supported (and below obviously)
        Number of TX chain: 2 (4TX to support UL MIMO)
    Goal: Complete UE feature for intra-band uplink CA

## Slide 3: Additional DC location reporting
Issue 1: Additional DC location reporting solution for intra-band UL CA.
Option 1: UE shall report the LO position after BWP activation command with same method as uplinkTxDirectCurrentList.
  Option 1-1: gNB is required to transmit RRCReconfiguration to the UE after each CC or BWP activation, and UE report DC location for the active BWPs by current RRC signalling.
  Option 1-2: UE report the LO position after CC or BWP activation by new L1/L2 signalling.
Note for discussion:
1-1 RRC and DCI processing delay are not matched. Stringent requirement on gNB side to provide RRCRconfig very frequently.
1-2 Big change on spec. both RAN1 and RAN2 spec may be impacted considering BWP switching can be DCI triggered. Current DC location reporting by RRC signalling is changed.
Option 2: additional DC location is reported by RRC signalling per BWP pair for all possible combinations of configured BWPs on the UL CCs
  E.g.
  4 BWPs are configured for CC1, as BWP1,1 BWP1,2 BWP1,3 BWP1,4, and 4 BWPs are configured for CC2, as BWP2,1 BWP2,2 BWP2,3 BWP2,4
  UE additionally report the DC location for each possible BWP pair which can be activated simultaneously for intra-band UL CA:
  DC1: BWP1,1+ BWP2,1
  DC2: BWP1,1+ BWP2,2
  DC3: BWP1,1+ BWP2,3
  …
  DC12: BWP1,4+ BWP2,4
Agreements:
  QC to send an LS to RAN1/2 including both option 1-2 and option 2 for both FR1 and FR2
Note for discussion: For 2UL CCs, 16 additional locations need to be reported, more bit number is required. It does not change the current DC location reporting mechanism by RRC signalling. Have no impact to RAN1 spec.

## Slide 4
Additional DC location reporting-con’d
Issue 2: UE capability for Additional DC location reporting for intra-band UL CA
Option 1: Introduce new UE capability to indicate whether UE support Additional DC location reporting solution for intra-band UL CA
Option 2: no need to introduce UE capability
Agreements:
  Option 1

## Slide 5: Feature on Intra-band contiguous UL CA
7-3b | NR CA class List for Intra-band contiguous CA | Indicate the contiguous CA bandwidth class that UE can support [On the condition that component 1 is indicated, indicate the PA architecture, i.e, 1PA or 2PA On the condition that component 1 and component 2 are indicated, indicate the MIMO layer number for each UL CC separately] NOTE1: there is dependency for the three components as given above | Intra-band UL contiguous CA band combination | Yes | N/A | [Network cannot schedule intra-band contiguous UL CA transmission properly] | FFS | No need | FR1 | N/A | [for each contiguous CA bandwidth class, if 2PA architecture is indicated, MIMO is not supported for both UL CCs by default] | [Optional with capability signalling, ]
Components 1/2/3 are the capability based on the existing signaling.
Bandwidth class, PA architecture and MIMO layer are relevant for intra-band contiguous UL CA, the relation is clarified in the feature list
Issue 1: whether the below feature item for intra-band contiguous UL CA is added to RAN4 feature list?
  Option 1: Yes
  Option 2: No
Agreements:
  Option 1, but components 2 and 3 need further discussion

## Slide 6
Feature on Intra-band contiguous UL CA-con’d
Issue 2: clarification on capability for intra-band contiguous CA
Proposals
  Option 1: For bandwidth class B, only 1PA architecture is valid. For bandwidth class C, if 2PA architecture is indicated by UE, UL MIMO is not supported by default, but additional signalling is provisioned for UL MIMO support
  Option 2: No clarification in RAN2 spec
Agreements:
  TBD

## Slide 7
Feature on Intra-band non-contiguous UL CA- Background
7-3a | [NR CA class List for intra-band non-contiguous CA] | [Option 1:] Indicate the maximum UL frequency separation that UE can support for each UL transmission chain for intra-band non-contiguous CA in the following format {{UL separation class for UL FR chain 1; UL separation class for UL FR chain 2} Note1: maximum UL frequency separation means maximum frequency span between lower edge of lowest component carrier and upper edge of highest component carrier that UE can support in uplink [Option 2:] Indicate the maximum UL frequency separation that UE can support which includes the gap between two non-contiguous CCs for intra-band non-contiguous CA Note: maximum UL frequency separation means maximum frequency span between lower edge of lowest component carrier and upper edge of highest component carrier that UE can support in uplink [Option 3: three components] Indicate the NC CA bandwidth class that UE can support, which includes gap between two non-contiguous CCs for intra-band non-contiguous CA On the condition that component 1 is indicated, indicate the PA architecture, i.e, 1PA or 2PA On the condition that component 1 and component 2 are indicated, indicate the MIMO layer number for each UL CC separately NOTE: there is dependency for the three components as given above | Intra-band UL non-contiguous CA band combination | Yes | N/A | [Network cannot schedule intra-band non-contiguous UL CA transmission properly] | For Option 1 in component item: Type 3 (per BC) For Option 2 in component item: Type 4 (per FS) For Option 3 in component item, Type 3 (per-BC) for component 1 and 2, Type 5 (per FSPC) for component 3 | No need | FR1 only | N/A | Based on the agreed WF R4-2005660 both 1PA and 2PA architecture for intra-band non-contiguous UL CA will be considered for UE capability, and MIMO supporting with 4TX for 2PA UL NC CA should not be excluded. The maximum UL CC number for intra-band UL CA is 2 in Rel-16. NC CA bandwidth class candidate values: Class1: NC CA separation class≤ 100MHz Class2: 100< NC CA separation class≤ 200MHz Class3: NC CA separation class > 200MHz and <600MHz | [Optional with capability signalling, ]

## Slide 8
Feature on Intra-band non-contiguous UL CA
Issue 1: implication of the new introduced NC CA bandwidth class
Option 1: A parameter for the specific NC CA configuration which is similar as bandwidth class for contiguous CA, NC CA bandwidth class includes both the bandwidths of UL CCs and gap between CCs
Option 2: the maximum frequency separation UE can support, which is similar as separation class defined for FR2
Agreements:
  TBD
Maximum frequency separation UE can support
One parameter of the specific NC CA configuration
Assume UE physically implements 2PAs on Band n77
The maximum frequency separation for 1PA is 200MHz, for 2PA is ‘no limitation’ or ‘600MHz’(maximum value)
For NC CA configuration at Band n77(2A), i.e. 2CC, aggregated bandwidth=200MHz：
  If UE reports the max frequency separation is 200MHz, PA architecture is 1PA, then it can support MIMO layer=2
  If UE reports the max frequency separation is 600MHz,
  PA architecture is 2PA, then it can support MIMO layer=1
Since MIMO and PA architecture are relevant, it is not clear to just report one maximum frequency separation, because UE do not know PA architecture before NC CA is configured to the UE
For each NC CA configuration, introduce a new parameter on the bandwidth class which includes bandwidths of UL CCs and gap between CCs
Assume UE physically implements 2PAs on Band n77
For NC CA configuration at Band n77(2A), i.e. 2CC, aggregated bandwidth=150MHz
  For NC CA bandwidth class= 100MHz-200MHz, UE can report PA architecture is 1PA, MIMO layer=2
  For NC CA bandwidth class= 200MHz-600MHz, UE can report PA architecture is 2PA, MIMO layer=1
It is clear for UE to report PA architecture and MIMO layer for different NC CA bandwidth classes, where different bandwidth classes are attributes to the same aggregated bandwidth

## Slide 9
Issue 2: NC CA bandwidth class definition if introduced (including both the bandwidths of UL CCs and gap between CCs)
Option 1:
Class 1: 10-100MHz
Class 2: 100-200MHz
Class 3: 200-600MHz currently only applicable to n77
Class 4: for future use
Option 2:
Class 1: 10-100MHz
Class 2: 100-200MHz
Class 3: >200MHz
Feature on Intra-band non-contiguous UL CA-con’d
Agreements:
  TBD

## Slide 10
Feature on Intra-band non-contiguous UL CA-con’d
Issue 3: MIMO layer, NC CA bandwidth class and PA architecture relation for intra-band non-contiguous CA feature
  Option 1: Clarify on the relation among MIMO layer, NC CA bandwidth class and PA architecture in the feature list
1. Indicate the NC CA bandwidth class that UE can support, which includes gap between two non-contiguous CCs for intra-band non-contiguous CA
2. On the condition that component 1 is indicated, indicate the PA architecture, i.e, 1PA or 2PA
3. On the condition that component 1 and component 2 are indicated, indicate the MIMO layer number for each UL CC separately
NOTE: there is dependency for the three components as given above
  Option 2: No need to clarify on the relation
Agreements:
  TBD

## Slide 11
Feature on Intra-band non-contiguous UL CA-con’d
Issue 4: clarification on capability for intra-band non-contiguous CA
Option 1: if UE indicate 2PA architecture for intra-band UL NC CA configuration, then UL MIMO is not supported by default, but additional signalling is provisioned for UL MIMO support
Option 2: No limitation
Agreements:
  TBD

## Slide 12
Feature on Intra-band non-contiguous UL CA-con’d
Issue 5: UE capability on In-gap ACLR and SEM/SE: indicate the in-gap ACLR and/or SEM/SE need to be relaxed for intra-band non-contiguous UL CA
Option 1: Introduce UE capability on In-gap ACLR and SEM/SE
Option 2: No need to introduce
Note for discussion: it is already agreed in previous RAN4 meeting WF: For 1PA/1LO architecture, exception should be allowed while the leakage and image falling on a frequency belonging to another licensee assuming synchronization across licensees, or if LO leakage lands on licensee's own spectrum holding.
Agreements:
  TBD