## Slide 1: [111] LTE_NR_DC_CA_enh_RF GTW FG [6-2] ’ Only supporting single switched UL ’
Moderator (Ericsson)
R4-20xxxxx
3GPP TSG-RAN WG4 Meeting #96-e
Online Meeting, Aug 2020
Agenda: 7.5.2, 8

## Slide 2: Background FG [6-2] ’ Only supporting single switched UL ’
[6-2] | Only supporting single switched UL | Only supporting single switched UL for specific inter-band ENDC combination | N/A | Yes | N/A | UE can’t support the specific inter-band ENDC combination | Per BC | No | FR1 only | N/A | This capability is restricted to specific band combinations. If this capability isn’t supported for the specific inter-band ENDC combination, the UE can support simultaneous UL transmissions when the inter-band ENDC combination is supported. UE can’t simultaneously report this capability and IE “singleUL-Transmission” for the specific inter-band ENDC combination. IE “tdm-Pattern” will be reused to indicate whether the UE supports the tdm-PatternConfig for this capability associated functionality. The field doesn’t apply to any other fallback band combinations. For super set combination, the UL configuration can refer to sub-clause 5.5B.4.1 from 38.101-3. | Optional with capability signalling

## Slide 3
Issue 1-1-1: Need for new capability ‘Only supporting single switched UL’
Proposals
  Option 1: specify a new capability ‘Only supporting single switched UL’
  Option 2: modify the capability singleUL-Transmission
  Option 3: implicit indication of SUO as proposed in R4-2011524
  Option 4: do not specify a capability ‘Only supporting single switched UL’
Recommended WF
  Further clarify the network/UE behaviors between “single switched UL” and “SUO/SUO allowed”, including the use of TDM patterns being mandatory or optional
  Based on the finding, pick an option
Status FG [6-2] (#111)
Notes: Ericsson: added text in blue

## Slide 4
[1] | R4-20XXXXX | R4-20XXXXX email discussion summary [96e][111] LTE_NR_DC_CA_enh_RF v1.0_HW2_TMUS_SKWS_QC_Intel_vivo_CHTTL_EAB_QC2 | Moderator(Ericsson)
References