## Slide 1: WF on spatial relation switch
Mediatek Inc.
3GPP TSG-RAN WG4 #96-e Meeting
Electronic Meeting, 17th - 28th Aug. 2020
R4-2012154

## Slide 2: Background
In RAN Plenary #86, the WI of NR RRM enhancement requirements for R16 was revised. The following issue is agreed to be discussed.
  Active spatial relation switch for uplink
Scenario overview
# | Scenario | PHY channel | Triggering method | associated source | Whether to introduce requirement
1 | PUCCH-RRC-DL | PUCCH | RRC | DL RS | No
2 | PUCCH-RRC-UL | PUCCH | RRC | UL SRS | No
3 | PUCCH-MAC-DL | PUCCH | MAC | DL RS | Yes
4 | PUCCH-MAC-UL | PUCCH | MAC | UL SRS | No
5 | PUSCH-DCI | PUSCH | DCI | - | No
6 | pSRS-RRC-DL | P-SRS | RRC | DL RS | Yes
7 | pSRS-RRC-UL | P-SRS | RRC | UL SRS | No
8 | spSRS-MAC-DL | SP-SRS | MAC | DL RS | Yes
9 | spSRS-MAC-UL | SP-SRS | MAC | UL SRS | No
10 | aSRS-DCI-DL | A-SRS | DCI | DL RS | Yes
11 | aSRS-DCI-UL | A-SRS | DCI | UL SRS | No

## Slide 3: Agreement
When the UL signal has spatial relation to an unknown DL RS,
  Option 1:
    Do not define requirements or UE behavior for the case when the UL signal has spatial relation to an unknown DL RS
  Option 2:
    Do not define UE behavior during the transition period
    UE transmits using newly configured UL spatial relationship after the transition period

## Slide 4: Way Forward
Define delay requirement for MAC CE based spatial relation info switching associated with DL-RS for PUCCH
For known spatial relation but the DL RS is not in the active TCI list
  Option 1:
    (THARQ +3ms)/NR slot length
  Option 2:
    If the spatial relation associated downlink RS is in the active TCI state list, UE shall be able to transmit a PUCCH with target spatial relation at slot n+ (THARQ +3ms)/NR slot length
    If the spatial relation associated downlink RS is not in the active TCI state list, no requirement is defined.
For unknown spatial relation
  Option 1: THARQ + 3ms+ TL1-RSRP
  Option 2: THARQ + 3ms+ TL1-RSRP + time for time tracking if applicable
  Option 3: No requirements will be defined
# | Scenario | Whether to introduce requirement
3 | PUCCH-MAC-DL | Yes

## Slide 5: Way Forward
Delay requirement for RRC based spatial relation info switching associated with DL-RS for P-SRS
For known spatial relation but the DL RS is not in the active TCI list
  Option 1:
    TRRCprocessing
  Option 2:
    The RRC based spatial relation info switching associated with DL-RS for P-SRS is TRRCprocessing when the target spatial relation associated to DL RS is known and the DL RS is in the active TCI list
    If the spatial relation associated downlink RS is not in the active TCI state list, no requirement is defined.
For unknown spatial relation
  Option 1: TRRCprocessing + TL1-RSRP
  Option 2: TRRCprocessing + TL1-RSRP + time for time tracking if applicable
  Option 3: No requirements will be defined
# | Scenario | Whether to introduce requirement
6 | pSRS-RRC-DL | Yes

## Slide 6: Way Forward
Whether to consider timing tracking when associated DL-RS?
  Sub1. Whether to consider timing tracking when associated DL-RS is known but QCLed with a different qcl-Type1 RS?
    Option 1: No
    Option 2: Only define the requirement when DL RS is in the active TCI list; Fine timing tracking isn’t needed when the DL RS has already added in the active TCI state list.
  Sub2. Whether to consider timing tracking when associated DL-RS is an unknown DL RS?
    Option 1: No
    Option 2: Yes
    Option 3: No requirement will be defined

## Slide 7: Way Forward
If the answer of the issue in agreement is Option 2,
Whether to define UE behavior during the transition period when UL signal is configured with unknown DL-RS? (Where the transition period is the period for L1-RSRP measurement for RX beam refinement.)
  Option 1: Define
  Option 2: Do not define
Whether to define UE behavior after the transition period when UL signal is configured with unknown DL-RS? (Where the transition period is the period for L1-RSRP measurement for RX beam refinement.)
  Note: This sub-issue depends on whether we agreed to define requirements for unknown case
  Option 1: Define
  Option 2: Do not define