## Slide 1: WF on IAB-MT Pcmax, power control and dynamic range
CATT
3GPP TSG-RAN WG4 Meeting # 96-e Electronic Meeting, 17-28 Aug., 2020
R4-2012616

## Slide 2: Background
The following contributions were provided and discussed in RAN4#96e
  R4-2010111, Discussion on IAB-MT Pcmax, CMCC
  R4-2010147, Discussion on remaining issues for IAB-MT Tx power related requirements, Samsung
  R4-2010293, TP to TR 38.809 Completing IAB-MT power related requirements, Nokia, Nokia Shanghai Bell
  R4-2010724, TP to TS 38.174: Output power requirements, Nokia, Nokia Shanghai Bell
  R4-2010950, Further discussion on IAB-MT power requirement, ZTE Corporation
  R4-2011032, IAB-MT maximum output power for FR1, Ericsson
  R4-2011293, TP to TS 38.174 -IAB TX dynamic range, Huawei

## Slide 3: LA IAB-MT MOP and scaling factor agreements
MOP for LA IAB-MT type 1-H: 24 dBm per TAB connector
MOP for LA IAB-MT type 1-O: 24 + 10*log10(NTXU,counted)
Scaling factor for LA IAB-MT type 1-H: NTXU,counted = min(NTXU,active , 8×Ncells)
Scaling factor for LA IAB-MT type 1-O: NTXU,counted = min(NTXU,active , 8×Ncells)
  Note: Applied the same method for Tx emission and Rx emission as well

## Slide 4: Pcmax agreements
The following factors are not included in the Pcmax definition.
  PowerClass, ΔPPowerClass, MPR/A-MPR, Pemax, and Interband CA, SUL and SRS related.
Pcmax definition:
  Option 1: Pcmax = Pdeclared
    Pdeclared includes the declared back off power.
      Further work on the definition of Pdeclared in TP R4-2012618.
    FFS whether accuracy needed or not, if needed, it can be referred to the existing specified values ; further discuss this in conformance phase.
    At least include EIRP based, FFS whether TRP based needed or not
    Applied for IAB-MT class: At least for both local-area IAB-MT, FFS whether applicable for and wide-area IAB_MT

## Slide 5: Power control agreements
Power control requirements are not defined for WA IAB-MT.
Absolute power tolerance is not defined for LA IAB-MT.
Relative power tolerance for LA IAB-MT
  Taking Nokia TP R4-2012618 as basis with the requirements with [ ]/values as TBD
  These values can be further discussed and modified in conformance phase if needed
Aggregated power tolerance for LA IAB-MT
  Include the requirements in the core specification
  Taking Nokia TP R4-2012618 as basis with the requirements with [ ] /values as TBD
  FFS whether need to have test cases which can be further discussed in conformance phase considering test tolerance and dynamic range requirements
  Further discuss (the consistent command period non-contiguous transmissions time period value [21ms] in response to 0 dB commands) value [21ms]

## Slide 6: PHR agreements
PHR mapping will be discussed in RRM session.
  If there’re some related RF issues, they can be discussed in the maintenance stage.

## Slide 7: Dynamic range agreements
Both X and Y will be captured in the core spec, the final wording for the side condition is captured in TP R4-2012621. with the following wording
  The IAB-MT dynamic range is the difference between the maximum and the minimum transmit power for a specified reference condition.
    NOTE 1: The upper limit of the dynamic range is the IAB-MT maximum output power when transmitting on one RB or all RBs. The lower limit of the dynamic range is the IAB-MT minimum output power when transmitting on all RBs.
    Note 2: The maximum output power and the minimum output power are defined as the mean power in at least one sub-frame 1 ms.