## Slide 1: Way forward on CA CQI reporting requirements
China Telecom
3GPP TSG-RAN4 Meeting #96e
Electronic Meeting, 17 Aug - 28 Aug, 2020
Agenda item: 7.16.1.5
R4-2012692
Document for: Approval

## Slide 2: Background: WF in previous meetings
RAN4 #94e-Bis
  WF: R4-2005548
  RAN4 #95e
  WF: R4-2008849

## Slide 3: Test Parameters #1
Duplex mode and SCS combinations
  For the performance requirements:
    Option 1: Reuse the duplex mode and SCS combination of PDSCH normal CA requirements (CTC, CMCC, DCM)
    Option 2: (Ericsson, Huawei, Qualcomm, Intel)
      FR1: FDD + FDD with 15 kHz SCS and TDD + TDD with 30 kHz SCS
      FR2: TDD + TDD with 120 kHz SCS
    Option 3: (Ericsson, Intel)
      FR1: FDD + FDD with 15 kHz SCS, TDD + TDD with 30 kHz SCS, FDD 15 kHz +TDD 30kHz
      FR2: TDD + TDD with 120 kHz SCS
    Proposed WF: Option 1
  Test applicability rule if the above proposed WF is agreed for FR1:
    Option A: Test 3 cases (CMCC)
    Option B : Test 2 cases (CTC)
      Candidate option for detailed applicability rule:
        Test #1: FDD 15 kHz + TDD 30 kHz > FDD 15 kHz + FDD 15 kHz > FDD 15 kHz + TDD 15 kHz
        Test #2: TDD 30 kHz + TDD 30 kHz > TDD 15 kHz + TDD 30 kHz
    Option C: Test 1 cases
    Proposed WF: option B, detailed applicability rule to be decided in the next meeting

## Slide 4: Test Parameters #2
    Channel bandwidth and test applicability rule
  Proposed WF: Define CA CQI performance requirements in a bandwidth agnostic way (CTC, Huawei, CMCC, Ericsson, DCM)
  Proposed WF: For the test applicability rule, use the following (CTC, Huawei, CMCC, Ericsson, DCM)
    For each agreed duplex mode and SCS combination for testing
      CA capability where the tests apply: Test any of one of the supported CA capabilities with largest aggregated CA bandwidth combination
      CA configuration from the selected CA capability where the tests apply: Test any one of the supported CA configurations with largest aggregated CA bandwidth combination

## Slide 5: Test Parameters #3
  TDD pattern
  For 15kHZ SCS, if agreed to cover TDD 15kHz
    Option 1: 3D1S1U with S=10:2:2
  For 120kHZ SCS, 2D1S1U with S=11:3:0 (CTC, Ericsson, Qualcomm, Huawei, DCM)
Antenna configuration for CA CQI test
  1T2R and 1T4R for FR1, and 1T2R for FR2 (Agreement in RAN4 #95e, Huawei, CTC, QC)
Signal power density for 2Rx and 4Rx requirements
  Confirm the baseline agreed in the last meeting, i.e., for 4Rx requirements, reduce the signal power density by 3dB compared to that for 2Rx (E///, Huawei, CTC, QC, CMCC)

## Slide 6: Test Metric
  SNR configuration for 2DL CA CQI test
  Option 1: SNRPcell = 10dB and SNRScell = 4dB for FR1 and FR2 (CTC, Huawei, Qualcomm)
  Option 2: SNRPcell = 16dB and SNRScell = 10dB for FR1, and SNRPcell = 14dB and SNRScell = 8dB for FR2 (Ericsson)
  Proposed WF: Option 1?
  SNR configuration for 3 or more DL CA CQI test
  Option 1: SNRPcell = 12dB, SNRScell1 = 6dB, SNRScell2, 3,… = 0dB for FR1 and FR2 (CTC, Huawei, Qualcomm)
  Option 2: SNRPcell = 18dB, SNRScell1 = 12dB, SNRScell2, 3,… = 6dB for FR1, and SNRPcell = 16dB, SNRScell1 = 10dB, SNRScell2, 3,… = 4dB for FR2 (Ericsson)
  Proposed WF: Option 1?
    Delta CQI threshold for CA CQI test
  thr = 2 for 2 or more DL CA in FR1 and FR2 (CTC, Ericsson, Huawei, Qualcomm)

## Slide 7: Agreed test parameters in previous meetings
Parameter | Value
Propagation condition | AWGN
TDD pattern | For 30kHZ SCS: 7D1S2U with S=6:4:4
CSI reporting type | Periodic
CSI reporting periodicity | For 15kHz SCS: 5 slots For 30kHz SCS: 10 slots For 120kHz SCS: 8 slots
Antenna configuration | 1T2R and 1T4R for FR1, and 1T2R for FR2
Signal power density for 2Rx and 4Rx requirements | For 4Rx requirements, reduce the signal power density by 3dB compared to that for 2Rx as baseline.
CQI Table | For FR1: CQI Table 2 For FR2: CQI Table 1
Test metric general principle | Following the methodology used in LTE, the difference between the wideband CQI indices of Pcell and the first Scell as well as the difference between the wideband CQI indices of the first Scell and the other Scell(s) (if any) shall be not smaller than a threshold, for more than 90% of the time