## Slide 1: WF on BS demodulation requirements for 2-step RACH
ZTE
3GPP TSG-RAN WG4 Meeting #96-e
E-meeting, 17th – 28th Aug., 2020
R4-2012706

## Slide 2: Background
Agreed WFs in previous meetings (Newest first)
  RAN4#95-e
    R4-2008864 WF on BS demodulation requirements for 2-step RACH
  RAN4#94bis-e
    R4-2005555 WF on BS demodulation performance requirements for 2-step RACH
  RAN4#94-e
    R4-2002389 WF on BS demodulation requirements for 2-step RACH

## Slide 3: Way forward (1) – TO compensation
  For TO compensation, keep the current agreement that TO compensation is assumed at BS side for specifying performance requirements for 2-step RACH

## Slide 4: Way forward (2) – FRC configuration and mapping type
Considering the decisions on (DMRS configuration, number of PRB, number of symbols, MCS, mapping type) together
  FR2: (1+1,2,10,2,B)
  FR1:
    Number of PRB numbers: 2
    Number of symbols: 14
    MCS: 1
    Mapping type: A & B
    DMRS configuration:
      Option 1: 1+1+1 (Ericsson, Samsung, ZTE, Nokia, Intel)
      Option 2: 1+1 (Huawei)
Companies are encouraged to provide simulation results with two options for DMRS configurations for FR1 in next meeting

## Slide 5: Way forward (3) – Medium level TO cycling values
For TO cycling values for medium level TO (scaling between 15k and 30k SCS, and between 60k and 120k SCS, and starting from 0):
  15k SCS: [0:0.4:2], 30k SCS: [0:0.2:1]
  60k SCS: [0:0.1,0.5], 120 SCS: [0:0.05,0.25]

## Slide 6: Way forward (4) – High level TO cycling values
For TO cycling values for high level TO (scaling between 15k and 30k SCS, and between 60k and 120k SCS, and starting from 0):
  Option 1:
    15k SCS: [0:0.1:3.8], 30k SCS: [0:0.1:3.8]
    60k SCS: [0:0.1,0.6], 120 SCS: [0:0.1,0.6]
  Option 2: Do not introduce requirements for high level TO cycling values
Companies are encouraged to provide simulation results for high level TO cycling values shown above, or preferred values in the next meeting.

## Slide 7: Way forward (5) – Test coverage
Discuss further the implications of adopting medium only or medium/high TO on test coverage,
  Option 1: only test the requirements for medium level TO cycling, i.e., lack of test coverage for large cell operation is OK
  Option 2: test the requirements for both medium and high level TO cycling
  Option 3: test either the medium T0 or the high T0 (but never both) depending on vendor declaration
  Option 4: Only test the requirements for high level TO cycling, considering no performance difference after TO compensation for medium and high level TO.

## Slide 8: Way forward (6) – Test metric
Set BLER = 1% as a baseline
Companies are encouraged to provide SNRs for both 1% and 10% at the same time

## Slide 9: Way forward (7) – TO error update
The TO error is assumed to be the same for a MsgA-PRACH preamble and MsgA-PUSCH pair
The TO error is updated per each occasion of PRACH preamble + MsgA during the test

## Slide 10: Way forward (3) - CR work split
 | CRs | Assigned Company
#1 | CR to TS 38.104 BS demodulation requirements for 2-step RACH (Section 8.2.6 and Annex) | ZTE
#2 | CR to TS 38.141-1 BS demodulation requirements for 2-step RACH (Section 8.2.6) | Ericsson
#3 | CR to TS 38.104 BS demodulation requirements for 2-step RACH (Section 11.2.1 and 11.2.2) | Huawei
#4 | CR to TS 38.141-1 BS demodulation requirements for 2-step RACH (Annex) | Nokia
#5 | to TS 38.141-2 BS demodulation requirements for 2-step RACH (Section 8.2.6) | Samsung
#6 | CR to TS 38.141-2 BS demodulation requirements for 2-step RACH (Annex) | Intel

## Slide 11: Simulation setup
Parameter | Values for FR1 | Values for FR2
Preamble format | Free choice | 
Waveform | CP-OFDM | 
Power offset between preamble and MsgA | Free choice | 
Subcarrier spacing for PUSCH | 15kHz, 30kHz | 60kHz, 120 kHz
PUSCH Mapping Type | Type A and Type B | Type B
MCS level | 1 | 2
Number of symbols | 14 | 10
Number of PRBs | 2 | 2
TBS | 56 - 72 bits 72 bits | 
DMRS | Option 1: 1+1+1 Option 2: 1+1 | Baseline: 1+1
Antenna configuration | 1T2R | 1T2R
Propagation channel | TDLC300-100 | TDLA30-300
TO values | Medium level cycling values: 15k SCS: [0:0.2:2], 30k SCS: [0:0.1:1] [High level cycling values 15k SCS: [0:0.1:3.8], 30k SCS: [0:0.1:3.8]] | Medium level cycling values: 60k SCS: [0:0.05,0.5], 120 SCS: [0:0.025,0.25] [High level cycling values: 60k SCS: [0:0.1,0.6], 120 SCS: [0:0.1,0.6]]
Test metric (BLER of MsgA when preambles are correctly detected) | Baseline: 0.01 | Baseline: 0.01
Re-transmission | No retransmission considered |