## Slide 1: WF on unsynchronized NW between n40 and n41
Agenda item: 7.19.3
Source: Huawei, HiSilicon, CMCC
3GPP TSG-RAN WG4 Meeting # 97-e R4-2016831
Electronic Meeting, Nov 2nd – 13th, 2020

## Slide 2: Background
In Rel-15, RAN4 discussed the spurious emission about UE to UE co-existence between band n40 and n41 [1][2][3]. The UE to UE coexistence requirements between n40 and n41 were removed based on the assumption that the same TDD pattern between band n40 and n41 would be deployed in China. However, the operators in China has a plan to use the different TDD pattern deployments between band n40 and n41.
Based on the analysis [4], spurious emissions about UE co-existence between band n40 and n41 were proposed.
This WF focus on single carrier band operation. The other issues are FFS.

## Slide 3: Assumptions
  When band n40 is transmitting power:
    It’s assumed that band n40 PA spurious emission at band n41 Rx frequency range is about -101dBm/Hz ~ -125dBm/Hz.
    Noise level depends on the UL resource allocation or transmission BW
    For band n40 post PA Filter, [20-30]dB attenuation is assumed at band n41 Rx frequency range.
    Range of filter rejection depends on how PA interacts with filter load
  When band n41 is transmitting power:
    It’s assumed that band n41 PA spurious emission at band n40 Rx frequency range is about -98dBm/Hz ~ -120dBm/Hz.
    Noise level depends on the UL resource allocation or transmission BW
    For band n41 post PA Filter, 9dB attenuation is assumed at band n40 Rx frequency range
  Investigate PC2 and PC3 Performance
  Investigate if resource allocation needs to be restricted for given channel BW (80 MHz Max BW is considered for n40 in Rel-16 spec)
  Include TX distortion in analysis
    RX IM2
    CIM3 = -60dBc
    CIM5 = -70dBc

## Slide 4: WF
  It’s proposed that spurious emissions for UE-to-UE co-existence between band n40 and n41 will be specified since Rel-16 as below.
    To introduce [TBD] dBm/MHz spurious emission requirements for band n41 frequency range when band n40 transmitting power.
    To introduce [TBD] dBm/MHz spurious emission requirements for band n40 frequency range when band n41 transmitting power.
      [TBD] value will be studied and specified in next meeting.
  The AMPR/NS_XX will not be considered for this case due to the legacy UE.
  The other solutions are not precluded.

## Slide 5: Reference
[1] R4-1816229, n41 – B40 Coexistence, Qualcomm Incorporated
[2] R4-1902001, Draft CR to 38.101-1 on n41 – B40 coexistence, Qualcomm Incorporated
[3] R4-1903124, Draft CR on n40-b41 coexistence, Intel
[4] R4-2015553, Discussion on spurious emission about UE co-existence between band n40 and n41, Huawei, HiSilicon, CMCC