## Slide 1: WF on RRC based BWP switching for SCell
Apple
3GPP TSG-RAN4 Meeting #97-e
Electronic Meeting, Nov 2 – 13, 2020
Agenda item: 4.7
R4-2017039
Document for: Approval

## Slide 2: Background
RRC based BWP switch is triggered by RRC re-configuration of firstActiveDownlinkBWP-Id or firstActiveUplinkBWP-Id
In TS 38.331:
The above text implies that for Scell firstActiveDownlinkBWP-Id is used upon Scell activation
Requirements for RRC based BWP switch do not capture applicability of requirements
firstActiveDownlinkBWP-Id If configured for an SpCell, this field contains the ID of the DL BWP to be activated upon performing the RRC (re-)configuration. If the field is absent, the RRC (re-)configuration does not impose a BWP switch. If configured for an SCell, this field contains the ID of the downlink bandwidth part to be used upon activation of an SCell. The initial bandwidth part is referred to by BWP-Id = 0. Upon PCell change and PSCell addition/change, the network sets the firstActiveDownlinkBWP-Id and firstActiveUplinkBWP-Id to the same value.

## Slide 3: Background
RRC-based BWP switch delay requirements in clause 8.6.3, TS 38.133, Rel-15, are applicable when the RRC reconfiguration involves active BWP switching or involves any parameter change of the active BWP as shown below:
8.6.3 RRC based BWP switch delay on a single CC Editor Notes: More than one BWP configurations for RRC-based BWP switch on SCell is FFS. The requirements in this clause only apply to the case that the BWP switch is performed on a single CC with one or more than one BWP configuration(s) configured. For RRC-based BWP switch, after the UE receives RRC reconfiguration involving active BWP switching or parameter change of its active BWP, UE shall be able to receive…

## Slide 4: Way Forward
Send LS to RAN2 clarifying applicability of RRC based switch to SCell
Update Editor’s note as :
  FFS if RRC based BWP switch is applicable to SCell
RRC based BWP switch requirements for SCell defined in Rel-15 can be updated based on RAN2 response, if needed
Requirements for RRC based BWP switch for SCell (Rel-16 onwards)
  Can be updated to follow RAN2’s agreements in Rel-16, if needed