## Slide 1: Rel-16 FR1 intra-band UL CA DC location GTW status
Moderator (Huawei, HiSilicon)
R4-200XXXX
3GPP TSG-RAN WG4 #97-e
Nov 2nd – 13th, 2020
Electronic meeting

## Slide 2: Background
Comments from companies in RAN#89-e on the above solutions:
2 solutions provided in approved LS R4-2011906:
Report TX DC location after every activation of BWP’s including CC activation, BWP switching procedure, etc.
Report each TX DC location based on permutations of all possible simultaneously activated BWPs within configured BWPs
Agreement in RAN#89-e for intra-band UL CA DC location:
Proposal: a mechanism of DC location reporting for intra-band UL CA should be specified in Rel-16
• RAN2 is tasked to provide at least one RAN2-based signalling solution for at least 2 UL CCs of intra-band UL CA in FR1 to RAN#90, considering forward compatibility to other combinations (more than 2 UL CCs and/or FR2)
• Other solutions are not precluded and can be discussed in RAN1, RAN2 and RAN4. Selection between solutions can be discussed at RAN#90 or later (if possible).
conclusion: proposal is endorsed
Almost all companies prefer solution 2 for Rel-16 considering the limited time budget and the potential spec impact to RAN1
It can be referred in RP-202018

## Slide 3: Issue 1: whether only UE indicates with 1PA architecture need to report the combined DC location?
Option 1: yes
Option 2: No
Note: UE with 2PA architecture report DC location separately for each CC by current Rel-15 DC reporting signaling, similar as for inter-band CA.

## Slide 4
Issue 2: whether UE Tx DC location is dependent only on the active BWPs in lowest and highest CC activated?
Option 1: yes
Option 2: No

## Slide 5
Issue 3: whether DC location is decided by CC/BWP configuration only?
1) whether UE DC location can be considered by default in the centre calculated by the lower edge of the lowest CC and the higher edge of the highest CC among all the active CCs?
2) Whether DC location can be considered by default in the centre of the lower edge of the lowest active BWP and the higher edge of the highest active BWP among all the active CCs?
Option 1: yes
Option 2: No

## Slide 6
Issue 4: whether DC location can be reported for each 2CC pair with all permutations of BWP pairs?
…
Step1: we have N UL CCs
Step2: select all 2CC pairs in the N CCs
CC1
CC2
CC3
CC4
CCN
CC pairs | CC1+CC2 | CC1+CC3 |  | CC1+CCN | CC2+CC3 | CC2+CC4 | 
…
…
Step3: indicated all BWP permutations for each 2CC pair
CC pairs | DC location for BWP pair1 | DC location for BWP pair2 | … | DC location for BWP pair16
CC1/CC2 | Value | Value |  | Value
CC1/CC3 | Value | Value |  | ---
… |  |  |  | 
CC1/CCN | Value | Value |  | Value
CC2/CC3 | Value | Value |  | ---
…. | …. | …. |  | ….
Option 1: yes
Option 2: No

## Slide 7
Issue 5: whether network could provide a list of likely BWP permutations to UE
in advance?
Option 1: yes
Option 2: No

## Slide 8
Issue 6: if yes to Issue5, how to report the DC location for the list of likely BWP permutations?