## Slide 1: WF on EN-DC large BW Cross Band Noise
Qualcomm, […]
­­­3GPP TSG-RAN WG4 Meeting # 97-e R4-2016839
Electronic Meeting, 2nd – 13th Nov., 2020

## Slide 2: 2 options
Option 1 (left): Specify RB position for valid MSD for all supported BWs
  Supported by [1], [3], [4].
  Notes required in Tables.
  Similar approach to LTE, NR single carrier 1UL/2DL NCCA.
Option 2 (right): Specify MSD for large BW regardless of RB position
  Similar to proposal from last meeting [5]. See Appendix.
  Supported by [2], [MediaTek].
  CIM3 definition, although defined in the note, should not be confused with the actual CIM3.
  MSD is applied to all DL BWs, which may not be the case.
  Still require notes in the main table that band combinations with large BW indicating that MSD is only applicable for the BWs <= X MHz.

## Slide 3: Any decision?
Agree on option 1 and keep it simple.

## Slide 4: References
R4-2014170, “Handling new channel bandwidths for ENDC and NRCA band combinations with MSD”, Qualcomm Inc., 3GPP TSG-RAN WG4 #97-e
R4-2015552, “Consideration on Cross band isolation impact with larger BW”, Huawei, 3GPP TSG-RAN WG4 Meeting # 97-e
R4-2015795, “Discussion on handling the cross-band isolation requirement for larger channel BW in Rel.16”, CHTTL, 3GPP TSG-RAN WG4 #97-e
R4-2015042, “Discussion on the MSD of the new channel BW for EN-DC and NR CA band combinations”, ZTE, 3GPP TSG-RAN WG4 #97-e
R4-2011777, “WF on handling new channel BW’s for EN-DC and NR CA band combinations with MSD”, Qualcomm, MediaTek, CHTTL, [ZTE], 3GPP TSG-RAN WG4 #97-e

## Slide 5: Appendix
Proposal from last meeting 96-e
E-UTRA or NR Band / Channel bandwidth of the affected DL band / MSD |  |  |  |  |  |  |  |  |  |  |  |  |  | 
UL band | DL band | 5 MHz (dB) | 10 MHz (dB) | 15 MHz (dB) | 20 MHz (dB) | 25 MHz (dB) | 30 MHz (dB) | 40 MHz (dB) | 50 MHz (dB) | 60 MHz (dB) | 80 MHz (dB) | 90 MHz (dB) | 100 MHz (dB) | 
n13 | 3 | 3.0 | 2.3 | 2 | 1.8 |  |  |  |  |  |  |  |  | 
n13,5 | 3 | [4.5] | [4.1] | [3.9] | [3.8] |  |  |  |  |  |  |  |  | 
n13,6 | 3 | [16.9] | []16.0 | [14.3] | [13.2] |  |  |  |  |  |  |  |  | 
NOTE 3: These requirements apply when the uplink is active in Band n1, n84 and the separation between the lower edge of the uplink channel in Band n1, n84 and the upper edge of the downlink channel in Band 3 is < 60 MHz. For each channel bandwidth (≤20MHz) in Band 3, the requirement applies regardless of channel bandwidth in Band n1, n84. NOTE 5: Applicable only for n1 UL BW = 25, 30, 40MHz. NOTE 6: Applicable only for n1 UL BW = 50MHz. |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | E-UTRA or NR Band / Channel bandwidth of the affected DL band / MSD |  |  |  |  |  |  |  |  |  |  |  | 
UL band | DL band | 5 MHz (dB) | 10 MHz (dB) | 15 MHz (dB) | 20 MHz (dB) | 25 MHz (dB) | 30 MHz (dB) | 40 MHz (dB) | 50 MHz (dB) | 60 MHz (dB) | 80 MHz (dB) | 90 MHz (dB) | 100 MHz (dB)
n40 | 1 | 8.3 | 8.3 | 8.3 | 8.3 |  |  |  |  |  |  |  | 
n40 | 13 | [21.5] | [21.5] | [21.5] | [21.5] |  |  |  |  |  |  |  | 
NOTE 3: Applicable only for n40 UL BW = 80MHz. |  |  |  |  |  |  |  |  |  |  |  |  | 
E-UTRA or NR Band / SCS / Channel bandwidth of the affected DL band / UL RB allocation of the agressor band |  |  |  |  |  | 
UL band | DL band | SCS of UL band (kHz) | 5 MHz (LCRB) | 10 MHz (LCRB) | 15 MHz (LCRB) | 20 MHz (LCRB)
n403 | 1 | 30 |  | [50] | [50] | [50]
NOTE 3: Applicable only for n40 UL BW = 80MHz. |  |  |  |  |  | 
NOTE 1: The UL configuration applies regardless of the channel bandwidth of the UL band. UL resource blocks allocation in the table shall be further limited to that specified in Table 7.3.1-2 in TS 36.101 [4] or Table 7.3.2-3 in TS 38.101-1 [2]. NOTE 2: The UL resource blocks shall be located as close as possible to the downlink operating band but confined within the transmission bandwidth configuration for the channel bandwidth. NOTE 3: When the maximum UL RB allocation “LCRB” value is less than the maximum transmission bandwidth configuration “NRB” defined in Table 5.3.2-1 in 38.101-1 [2] for the specified UL band SCS, the UL band should be configured using the lowest CBW that is compatible with the maximum specified LCRB value.