## Slide 1: WF on SAR solutions for PC2 NR inter-band CA and SUL configurations
China Telecom
R4-201xxxx
3GPP TSG-RAN WG4 Meeting # 97-e
Electronic Meeting, 2-13 Nov., 2020
Agenda: 10.19

## Slide 2: Background
The contributions submitted in RAN4 #97e meeting for SAR solutions:
  R4-2014383, Discussion on SAR issues for inter-band and SUL 2UL CA PC2, CATT
  R4-2015040, Discussion on SAR solution for NR PC2 inter-band CA, ZTE Corporation
  R4-2015190, Discussion on SAR schemes for UE power class 2 NR inter-band CA with 2UL, China Telecom
  R4-2015260, Discussion on SAR issue for HP UE inter-band UL CA, Xiaomi
  R4-2015287, Discussion on the SAR solutions for UL CA band combinations, Huawei, HiSilicon
  R4-2015329, Discussion on SAR solution for PC2 inter-band NR CA, vivo
  R4-2015346, Discussion on inter-band CA HPUE SAR, OPPO
  R4-2015983, Facilitating SAR compliance for UL inter-band CA PC2, Ericsson
  R4-2015041, Discussion on SAR solution for NR PC2 SUL, ZTE Corporation
  R4-2015191, Discussion on SAR schemes for UE power class 2 NR SUL configurations, China Telecom
  R4-2015286, Discussion on the SAR solutions for SUL band combinations, Huawei, HiSilicon
  R4-2015330, Discussion on SAR solution for PC2 UE with SUL, vivo
  R4-2015345, Discussion on SUL HPUE SAR, OPPO

## Slide 3: WF on SAR solutions- baselineRAN 4 Agreement
Agreement on P-MPR solution:
  UE implementation based solution, i.e. P-MPR is always available as the baseline solution for NR PC2 inter-band CA and SUL configurations
Agreement on release independency:
  The requirements for NR PC2 inter-band CA and SUL configurations are release independent from Rel-15 based on the P-MPR solution.

## Slide 4: WF on other SAR solutions- options
Duty Cycle based solutions
  Option 1: Report the duty cycle capability per band combination (CTC, Intel, ZTE, Huawei, Apple)
    Main issue commented by companies：Nonlinear Unequal responses for the SAR effects in different band frequencies.
  Option 2: Report the duty cycle capabilities per band (CATT, Xiaomi, ZTE, OPPO, vivo, CMCC)
    Main issue commented by companies: Too many pairs of signalling's, more detailed signalling design and values need to be provided, especially for the reference band.
Blind scheme solution (Ericsson, Verizon, T-Mobile USA)
  It is proposed to consider (Scell) power dropping behavior due to power prioritization for UL CA and SUL configurations
Other solutions/options are not precluded

## Slide 5: Other open issues (all solutions)
Verification (test cases) for all solutions, including proprietary
  Predicatbility of UE behaviour
  Example requirement: for FDD-TDD, inter-band TDD-TDD CA PC2 and SUL PC2 combinations the total average output power over FFS radio frames shall be at least [23] dBm
Consideration of (Scell) power dropping behavior due to power prioritization
  applies for NR CA and SUL, not for EN-DC PC2

## Slide 6: WF on release independency
NR PC2 inter-band CA and SUL configurations are release independent from Rel-15 based on the P-MPR solution.