## Slide 1: WF on power configuration for PC2 NR inter-band CA
Qualcomm Incorporated
R4-201xxxx
3GPP TSG-RAN WG4 #97-e
Nov 2nd ‒ 13th, 2020
Electronic Meeting

## Slide 2: Motivation
UE higher maximum output power has been seen as beneficial by the operators. The interest in higher output powers has been steadily growing with increasing requests for PC2 and PC1.5.
UE’s with dual PA are also becoming more relevant with features such as UL CA, TxD, EN-DC
  For example, UE’s supporting simultaneous transmission of 23 + 26 dBm Tx paths and 26 + 26 dBm Tx paths have been assumed
For UE’s already equipped with dual PA’s, they may be able to deliver higher output power, up to 28 dBm or 29 dBm
  No additional Tx hardware cost
  New PA designs are not needed

## Slide 3: Technical concerns and resolution
Some concerns have been identified with possible resolution in [1]
  Coexistence and other emission requirements
  SAR and complexity in diverse duty cycle reporting and fallback behavior
  MPR and A-MPR
  Self-desense (MSD)
  Regulatory Tx power limits and behavior of network vendor to reduce regulatory risk
  Others

## Slide 4: Spec implementation
One example is provided in [1]; a very simple modification to the spec
  PCMAX_H = MIN{10 log10 ∑ pEMAX,c , PEMAX,CA, PPowerClass}
  PPowerClass is removed from PCMAX_H for UL CA
    PPowerClass is 26 dBm for PC2 and would normally set the upper bound of PCMAX to no higher than 26 dBm
    PEMAX,CA remains in case of regulatory or other constraints that need to be applied by the network
    ∑ pEMAX,c remains so that the PCMAX will be bound by the sum of the individual cell groups
  PCMAX_L is unmodified
    MPR and A-MPR are still available to meet emissions
    The UE in UL CA is not required to transmit higher max power since PCMAX_L is not increased, but is allowed to since PCMAX_H is increased
2UL IMD MSD needs to be evaluated for higher output powers
Another possible option is to introduce a higher power class, for example PC 2.1 with 27.8 dBm MOP

## Slide 5: Way Forward
For RAN4 #98-e
  Companies to check the concerns and possible resolution
    Concerns and methods for resolution are not limited to those in Slide 3 or as documented in [1]
  Companies to consider spec implementation
    Examples in Slide 4, but other options are not precluded
  Companies to consider applicability and scope
    Presently, the discussion is under the context of 2UL inter-band CA
    Which release? Which work item? What completion timeline?

## Slide 6: Reference
[1] R4-2016439, “Upper limits on output power for dual PA,” Qualcomm Incorporated