## Slide 1: WF on multi-band relaxation of n262
Apple
R4-200xxxx
3GPP TSG-RAN WG4 Meeting #97-e
Electronic meeting, 2nd Nov – 13 Nov 2020

## Slide 2: Background
For UEs that support multiple FR2 bands, minimum requirement for peak EIRP/EIS and EIRP/EIS spherical coverage shall be decreased per band by:
  The peak EIRP/EIS relaxation parameter MBP,n
  The EIRP/EIS spherical coverage relaxation parameter MBS,n
Extension of the scope of the UE multi-band support in Rel-17 (n257, n258, n261, n260, n259, and now including band n262).

## Slide 3: WF – Multi-band relaxation (MBR) for n262
Regardless of the transceiver architecture, UE implementation with antenna arrays that span frequency range 37 – 48.2 GHz is anticipated
  Companies are encouraged to study and quantify RF impairments associated to such an antenna array implementation, including considerations for antenna element spacing and form factor integration trade-offs.
Open issues:
  Companies are encouraged to consider band grouping scenarios and architecture options, and their impact on MBR.
  To start the analysis, MBR should consider all possible combinations, including the UE which supports all Rel-17 FR2 bands
  Other studies which might have any impact on antenna design and MBR are not precluded
Companies are encouraged to provide next RAN4 meeting values for MBR for n262 based on the above considerations.