## Slide 1: WF on UE RF requirement of n262
Qualcomm, Nokia, Sony …
R4-2016879
3GPP TSG-RAN WG4 Meeting #97-e
Online Meeting, Nov 2020
Agenda: 10.28
Email Thread: #130

## Slide 2: Background 1
n262 PC3 Min Peak EIRP and REFSENS Proposals:
 | min pk EIRP (dBm) | REFSENS (dBm), 100 MHz, SNR = -1 dB
R4-2014263 Qualcomm | 14.8 | -81.5
R4-2015855 Sony, Ericsson | 18.0 18.0 | -81.5 -81.5
R4-2015888 Intel | 17.0 | -80.2
R4-2016229 Vivo | 16.3 | -78.5
R4-2016296 Apple | 12.7 | -76.0
Mean n262 (47.7 G) | 16.5 (mean over mW) 16.1 (mean over dBm) | -79.3 (mean over mW) -79.89(mean over dBm)
n259 (41.5 G for reference) | 18.7 | -81.7
n260 (38.5 G for reference) | 20.6 | -82.7

## Slide 3: Background 2
PC3 EIRP and EIS degradation from peak direction to 50th %ile direction:
 | peak to 50th %ile degradation(dB)
n258 (26.0 GHz) | 10.9
n257/n261 (28.0 GHz) | 10.9
n260 (39.5 GHz) | 12.6
N259 (41.5 GHz) | 12.9
Extrapolated n262 (47.5 G) | 13.X ?
Chart: FR2 PC3 sph. cov. gain drop
| 25.9 | 28 | 38.5 | 41.5
 | 10.9 | 10.9 | 12.6 | 12.9
 | 12.9 | 12.9
 | 12.9 | 13.4
 | 12.9 | 13.9

## Slide 4: WF on PC3 EIRP
min. pk. EIRP:
  Companies are encouraged to provide a view if 16.5 dBm or 16.1 dBm can be specified or not.
Pmin:
  Companies encouraged to study if deviation from Pmin value of -13.0 dBm is justified
Beam correspondence
  Companies are encouraged to bring proposals for DEIRPBC to include n262 in table 6.6.4.2-1 of TS 38.101-2

## Slide 5: WF on PC3 REFSENS
REFSENS for 100 MHz BWchan
  Companies are encouraged to provide a view if -79.3 dBm or -79.89 dBm can be specified or not.
Assumption: -1 dB target SNR

## Slide 6: WF on PC3 spherical coverage
REFSENS and peak EIRP degradation parameter value (‘gain drop’) along 50th %ile direction:
  Companies are encouraged to provide a view if the extrapolation from existing FR2 trend: 13.4 dB can be specified or not.
Chart: FR2 PC3 sph. cov. gain drop
| 25.9 | 28 | 38.5 | 41.5
 | 10.9 | 10.9 | 12.6 | 12.9
 | 12.9 | 12.9
 | 12.9 | 13.4
 | 12.9 | 13.9

## Slide 7: WF on PC3 MPR for n262
Companies are encouraged to study if deviation from existing FR2 EVM side conditions is justified:
  Study impact of PTRS on UL EVM in RAN4#98
Companies are encouraged to study if deviation from existing FR2 MPR values is justified:
  PA Non-linearity characteristics deviation from other bands
  Any general emissions requirements unique to n262
  Other study subjects not precluded