## Slide 1: WF on FR2 enhancement part 3: UL gap
Apple, …
3GPP TSG-RAN WG4#97-e Meeting R4-2016919
Electronic Meeting, 2nd – 13th Nov., 2020

## Slide 2: Way Forward – UL gap use cases / evaluation metric
Identified UL gap use case for further study.
  UE power/coverage enhancement
  PA calibration
  Transceiver calibration
  Other options are not precluded
Candidate metric for UL gap performance gain evaluation
  more UL power to enhance the coverage
  less MPR allowance to enhance the high MCS coverage
  better EVM to improve throughput
  Better emissions performance to reduce adjacent channel interference and inband emission
  More accurate power control
  Other options are not precluded
Interested companies are encouraged to provide the inputs on the list of exact evaluation metric per UL gap use case in RAN4#98e.

## Slide 3: Way Forward – UL gap categories
UL gap can be further classified into two types based on UE behavior during the gap
  Type 1: No UL scheduling during the gap is needed. NW can assign those resources to other UE for UL transmission.
  Type 2: UL scheduling, including dedicated time and frequency resources reserved for self-calibration and monitoring, during the gap is needed. NW cannot assign those resources to other UE for UL transmission.
Per identified UL gap use case, interested companies are encouraged to provide inputs on the detailed evaluation assumptions for both UE/NW and applicable UL gap type(s) in RAN4#98e.

## Slide 4: Way Forward – Performance evaluation
Performance evaluation should focus on the testable improvements with and without gap (R16 baseline).
  R16 baseline should be the RF performance requirements defined in current spec, and the assumption behind is that UE has no UL gap for calibration.
  It is FFS if performance gain needs to be shown in RF requirements or other requirements.
NW impact related evaluation include the impact of scheduling restriction, UL overhead (e.g. gap length, periodicity) and the potential UL interference when calibration is performing.
  Evaluation can be done after further details are agreed.

## Slide 5: Contributions List in RAN4#97-e
T-doc No. | Title | Company
R4-2014393 | Discussion on UL gaps for self-calibration and monitoring | CATT
R4-2014590 | On performance improvements from self-calibration in UL gaps | Intel Corporation
R4-2014716 | UE calibration gap motivation and view to the requirements | Qualcomm Incorporated
R4-2014963 | Discussion on UL gap for self-calibration and monitoring | vivo
R4-2015349 | Discussion on Rel-17 FR2 calibration gap | OPPO
R4-2016061 | Analysis on power calibration gaps | Ericsson, Sony
R4-2016536 | on gaps for self-calibration and monitoring | Huawei, HiSilicon
R4-2016560 | Further discusison on UL gaps for self-calibration and monitoring | Apple
R4-2014218 | Discusison on UL gaps for self-calibration/monitoring | Apple
R4-2014516 | Assumptions for study on FR2 UL gaps for self-calibration and monitoring | Nokia, Nokia Shanghai Bell

## Slide 6: Reference
[1] R4-2016978, “Email discussion summary for [97e][137] NR_FR2_req_enh2_Part_3”, Apple