## Slide 1: 3GPP TSG-RAN WG4 Meeting #97-e Electronic Meeting, Nov. 2 - 13, 2020
Intel
WF on NR Positioning Performance Requirements
R4-2017151

## Slide 2
Agreements in the 1st round/GTW
Agreements in the 2nd round
Still open for discussion

## Slide 3: WI Work Plan
Work Plan for Performance part:
  the workplan is based on the following GTW agreement:
    Define test cases for
      SA FR1 without CA
      SA FR2 without CA
      FFS: NR-DC with FR1 PCell and FR2 PSCell
  The detailed work plan can be found in [R4-2017158]
CR Splitting plan was included in [R4-2017158]

## Slide 4: Specification structure
Change for TS38.133 structure
  According to GTW agreements on the scenarios of test cases in Subtopic 5-2, the specification structure for test cases can be defined for SA scenario firstly
  The new clauses needed for NR Positioning test cases be found in [R4-2017152]

## Slide 5: Measurement Accuracy Requirements for RSTD(1)
SINR side condition for FR2:
  -6dB for reference TRP and -13 dB for neighbor TRP
Define the requirements at least for the cases without repetition and multiple repetitions (within the slot and across the slots within one PRS period (i.e. TPRS)) can be considered for small BW
Antenna panel assumption: FFS
  Option 1. RAN4 not to define separate accuracy requirements for RSTD measured with same panel and with different panels.
  Option2. The requirements relaxed for the UE using different antenna panel for receiving both reference and neighbor PRS.
Assumption on TRS setting for defining accuracy and test:
  No need to consider TRS when defining PRS measurement accuracy requirements.
  For test case can be FFS
Applicable accuracy requirement in case of HO: FFS
  Option 1. Applicable accuracy requirements are not impacted by HO
  Option 2. The same RSTD measurement accuracy requirements shall apply for intra-frequency HO and inter-frequency HO, before and after the HO
Applicable propagation channel for accuracy requirement: FFS
  Option 1 : No need to define the applicability with propagation channels for accuracy requirement. (e.g. TDL-C channel model with 300 ns delay spread shall be considered also)
  Option 2: Need the applicability with propagation channels for accuracy requirement (e.g. Exclude number from simulations for TDL-C channel model with 300 ns delay spread in FR1 for defining the RSTD accuracy requirements.)
RAN4 needs to decide on the group delay calibration margin.
  margin equals to zero if the reference and neighbouring resources are on the same frequency layer in FR1

## Slide 6: Measurement Accuracy Requirements for RSTD(2)
Define the requirements at least for the cases without repetition and multiple repetitions (within the slot and across the slots within one PRS period (i.e. TPRS)) can be considered for small BW
The proposals for accuracy requirements and corresponding configuration parameters are to be collected until the next meeting according to template below
Accuracy [Tc] | PRS BW, PRBs (or MHz) | SCS, kHz | Repetition factor | Comb size
[Req Set 1] |  |  |  | 
[Req Set 2] |  |  |  | 
…. |  |  |  | 

## Slide 7: Measurement Accuracy Requirements for PRS RSRP(1)
SINR side condition for serving/neighbor TRP : FFS
  Option 1a: -3dB for serving TRP
  Option 1b: -6dB for serving TRP
  Option 1c : defining two levels in side conditions for the target (no need to call “serving” or “neighbor”) measured PRS-RSRP: [-3 dB or -6 dB] and [-13 dB].
  Option 2: for neighbor cell/TRPs ONLY
  Option 3: For the reference cell/TRPs and neighbour cell/TRPs
    Same as that for the reference cell in PRS-RSTD
Define PRS RSRP measurement accuracy requirements for 2 SINR side conditions
  SINR side condition #1: [-3 dB or -6 dB].
  SINR side condition #2: [-13 dB].
  No differentiation between serving and neighbor cell/TRPs
  Same side condition apply for FR1 and FR2
  FFS whether the test case will cover both side condition
Number of samples for PRS RSRP accuracy requirements
  Follow the same principle as for RSTD measurement
Type of requirements :
  Option 1. Define ONLY relative accuracy requirements for PRS-RSRP
  Option 2. Define both absolute and relative accuracy requirements for PRS-RSRP
  Option 2a.
    At least the absolute accuracy requirements for PRS-RSRP are defined
    FFS the need to define relative accuracy requirements for PRS-RSRP
How to define the accuracy requirements with the combinations of PRS BW and other parameters
  Follow the same principle as for RSTD measurement, but the parameters can be different

## Slide 8: Measurement Accuracy Requirements for UE Rx-Tx time difference(1)
SINR side condition : FFS on whether to define one or two side conditions
Define UE Rx-Tx time difference measurement accuracy requirements for 2 SINR side conditions
  SINR side condition #1: [-3 dB or -6 dB]
  SINR side condition #2: [-13 dB]
  No differentiation between serving and neighbor cell/TRPs
  Same side condition apply for FR1 and FR2
  FFS whether the test case will cover both side conditions
Antenna panel assumption: Can follow the same conclusion as for RSTD requirements
RAN4 to decide on the margin to account for the group delay calibration error for both UE Rx and Tx. The same margin for gNB can be FFS separately

## Slide 9: Measurement Accuracy Requirements for UE Rx-Tx time difference(2)
Applicability of accuracy requirements in the case of NTA_offset change : FFS
  Option 1: RAN4 not to capture applicability of UE Rx-Tx time difference accuracy requirements under NTA_offset change during the measurement period
  Option 2: Clarify in section 10.1.25.2 in TS 38.133: “UE Rx-Tx time difference accuracy requirements shall not apply if NTA_offset defined in Table 7.1.2-2 in 38.133 changes during the UE Rx-Tx measurement period.”
UE Rx-Tx time difference accuracy requirements do NOT apply with HO during the measurement period
Applicability of accuracy requirements in the case of cell change which is different from HO: FFS
  Option 1. The same UE Rx-Tx measurement accuracy requirements shall apply before and after the cell change (not HO) which does not impact SRS configuration, when the UE continues the measurement
Applicability of accuracy requirements under TA adjustment : FFS
  Option 1. UE Rx-Tx measurement accuracy requirements shall not apply if the uplink transmission timing changes during the UE Rx-Tx measurement period due to autonomous adjustment or based on network-configured TA
How to define the accuracy requirements with the combinations of PRS BW and other parameters
  Follow the same principle for that of RSTD measurement

## Slide 10: Test case design principles
No need to define separated E-CID test case in Rel16
Define test cases for
  SA FR1 without CA
  SA FR2 without CA
  FFS: NR-DC with FR1 PCell and FR2 PSCell
NO DRX case will be tested only for NR positioning measurement requirements in Rel16
General PRS configuration for NR Positioning test case : FFS
SRS configuration for NR Positioning test case: FFS
Number of cells/TRPs for NR Positioning test case : FFS
  Option 1a. for RSTD measurement requirements, test cases with 3 cells are developed: NR PCell (cell 1) and two NR neighbor cells (cell 2, cell 3);
    for RSTD measurement accuracy requirements, test cases with 2 cells can be sufficient, provided separate test cases are developed for measurements on the same and different frequency layers: NR PCell (cell 1) and one NR neighbor cell (cell 2)
    for PRS-RSRP (DL-AoD) and UE Rx-Tx time difference measurement requirements and measurement accuracy requirements, the same test set-up as for RSTD can be used
  Option 2: two TRPs in the test case
Number of positioning frequency layers : FFS
  Option 1: The number of positioning frequency layers measured cannot be larger than 2.
  Option 2: : There are one PRS frequency layer
Synchronous/Asynchronous cells : FFS
Muting pattern :FFS whether to use muting or not in test cases

## Slide 11: Test case list
Define measurement following cases (totally 12 test cases)
FFS: NR-DC with FR1 PCell and FR2 PSCell
Index | Test case
1 | RSTD measurement requirements for FR1 in SA
2 | RSTD measurement requirements for FR2 in SA
3 | PRS RSRP measurement requirements for FR1 in SA
4 | PRS RSRP measurement requirements for FR2 in SA
5 | UE Rx-Tx time difference measurement requirements for FR1 in SA
6 | UE Rx-Tx time difference measurement requirements for FR2 in SA
7 | RSTD measurement accuracy for FR1 in SA
8 | RSTD measurement accuracy for FR2 in SA
9 | PRS RSRP measurement accuracy for FR1 in SA
10 | PRS RSRP measurement accuracy for FR2 in SA
11 | UE Rx-Tx time difference measurement accuracy for FR1 in SA
12 | UE Rx-Tx time difference measurement accuracy for FR2 in SA