## Slide 1: WF on R16 RRM enhancement part 2 – SRS Carrier switching, CGI reading, Mandatory MG patterns
ZTE, …
3GPP TSG-RAN WG4 Meeting #97-e
Electronic Meeting, Nov. 2nd – Nov. 13th 2020
R4-2017180

## Slide 2: SRS carrier based switching
Core maintenance
Test cases

## Slide 3: Agreements on core requirements
Agreements:
Introduce requirements in TS 36.133 for interruption on LTE victim cell for LTE SRS carrier based switching under EN-DC and NE-DC
Tentative agreements:
Collision of NR SRS carrier based switching and UE BWP switching
  UE is not expected to execute SRS carrier switching when it is colliding with UL BWP switching on either carrier

## Slide 4: Agreements on test cases
Do not define delay test cases for SRS carrier-based switching for NR deployments, similar to LTE.
  For NR SRS carrier based switching define tests for SA and EN-DC
  For EN-DC the interruptions for LTE and NR carriers are tested.
  For SA the following combinations are tested
    FR1 CA
    FR2 CA
    FFS: FR1+FR2 CA with SRS switching within same FR
    FFS: FR1+FR2 CA with SRS switching between different FRs
  For E-UTRA SRS carrier based switching define tests for EN-DC
  Capture all test cases in TS 38.133

## Slide 5: Agreements on test cases
TC list for SRS carrier based switching in this meeting
Test No. | Test | Test configuration | Company
TC1 | SA interruptions at NR SRS carrier based switching | PCell in FR1, SCell in FR1 | ZTE
TC2 | SA interruptions at NR SRS carrier based switching | PCell in FR2, SCell in FR2 | Ericsson
TC3 | E-UTRAN – NR interruptions at NR SRS carrier based switching | PSCell in FR1, SCell in FR1 | Nokia
TC4 | E-UTRAN – NR interruptions at NR SRS carrier based switching | PSCell in FR2, SCell in FR2 | Apple
TC5 | E-UTRAN – NR interruptions at E-UTRA SRS carrier based switching | PSCell in FR1, E-UTRA SCell | Huawei
TC6 | E-UTRAN – NR interruptions at E-UTRA SRS carrier based switching | PSCell in FR2, E-UTRA SCell | OPPO

## Slide 6: Open issues on test cases
FFS: FR1+FR2 CA with SRS switching within same FR
FFS: FR1+FR2 CA with SRS switching between different FRs
FR1+FR2 CA tests should be considered in following scenarios
  SA interruptions at NR SRS carrier based switching
  E-UTRAN – NR interruptions at NR SRS carrier based switching
  E-UTRAN – NR interruptions at E-UTRA SRS carrier based switching
Companies are encouraged to bring further analysis on the necessity and testability of above test cases.
UE type for test
  Option 1: Tests are specified for UE capable of per-UE gap and capable of per-FR gap
  Option 2: No mention of UE type in the test

## Slide 7: CGI reading
Core maintenance
Test cases

## Slide 8: Agreements on tests
Requirements for both CGI reading delay, and interruptions to serving cell during CGI reading should be verified by the same tests
Test requirement for interruption during CGI reading should be defined by counting number of total missed ACK/NACKs during the CGI reading procedure.
20ms NR SMTC periodicity is used in the test
Test configuration for SI-RNTI scheduling periodicity
  FR1: 20ms
  FR2: 40ms
Do not define test cases for CGI reading in LTE SA
Test cases for CGI reading in NR SA
    Test 2a: LTE CGI reading in NR SA, FR1 PCell
    Test 3a: NR intra-frequency CGI reading in NR SA, FR1 PCell and FR1 target cell
    Test 4b: NR inter-frequency CGI reading in NR SA, FR2 PCell and FR2 target cell
Test cases for CGI reading in EN-DC
    Test 5a: NR intra-frequency CGI reading in EN-DC, FR1 PSCell and FR1 target cell
    Test 6b: NR inter-frequency CGI reading in EN-DC, FR2 PSCell and FR2 target cell

## Slide 9: Agreements on test cases
TC list for CGI reading
Test No. | Test | Test configuration | Company
TC1 | SA intra-frequency CGI identification of NR neighbor cell in FR1 | FR1 PCell, FR1 target cell (Test 3a) | ZTE
TC2 | SA inter-frequency CGI identification of NR neighbor cell in FR2 | FR2 PCell, FR2 target cell (Test 4b) | Ericsson
TC3 | EN-DC intra-frequency CGI identification of NR neighbor cell in FR1 | FR1 PCell, FR1 target cell (Test 5a) | Nokia
TC4 | EN-DC inter-frequency CGI identification of NR neighbor cell in FR2 | FR2 PCell, FR2 target cell (Test 6c) | Huawei
TC5 | SA CGI identification of E-UTRA neighbor cell | FR1 PCell (Test 3a) | Mediatek

## Slide 10: Open issues
Issue 2-1-5a: How to calculate missed ACK/NACK during CGI reading
  Option 1: Missed ACK/NACK is tested based on total allowed interruption during entire CGI reading, with the total number
      Option 1a: number of interrupted slots + K1
      Option 1b: 2 * number of interrupted slots
      Option 1c: FFS
Issue 2-1-7a: LTE power up time, as defined in 6.1.2.1.2 inter-RAT HO, 30ms is needed for LTE power up. How to capture in the spec?
  Option 1: In test requirement, add 30ms LTE power up time
  Option 2: In core requirement, embedded in RRC procedure delay, specifying that 15ms RRC procedure delay for intra-RAT CGI reading, additional 30ms is added for inter-RAT CGI reading.
Issue 2-1-7b: LTE power off time takes another 20ms. How to capture in the spec?
  Option 1: In test requirement, add 20ms LTE power off time
  Option 2: In core requirement

## Slide 11: Mandatory gap pattern
Test cases

## Slide 12: Agreements on test cases
Use existing tests for inter frequency measurement without SSB index detection and with no DRX as baseline
Introduce test cases only for some of the new mandatory gap patterns
    [#2] for per-UE gap capable UE in FR1
    [#11] for per-FR gap capable UE in FR1
    #17 in FR2
FFS if Rel-16 UE is allowed to skip some of the Rel-15 tests
Tentative agreement:
Separated test cases for additional mandatory gap pattern are specified for Rel-16, i.e. test cases are introduced in different clauses than Rel-15 test cases which is baseline for Rel-16 test cases

## Slide 13: Agreements on test cases
TC list for mandatory gap pattern
Test No. | Test | Test configuration | Company
TC1 | SA event triggered reporting tests with additional mandatory gap pattern | FR1 PCell, FR1 neighbor cell Test 1: [GP#2] for UE capable of per-UE gap only Test 2: [GP#11] for UE capable of per-FR gap | ZTE
TC2 | SA event triggered reporting tests with additional mandatory gap pattern | FR2 PCell, FR2 neighbor cell Test 1: GP#17 | Ericsson

## Slide 14: Open issues
FFS if Rel-16 UE is allowed to skip some of the Rel-15 tests