## Slide 1: WF on NR NTN RRM requirements
Moderator, THALES

## Slide 2: Outline
Proposed way forward based on the outcomes of “Email discussion summary for [97e][232] NR_NTN_solutions_RRM”
See R4-2017302

## Slide 3: Content
Topic #1: General RAN4 RRM NTN related aspects
Topic #2: GNSS requirements
Topic #3: PVT Satellite precision
Topic #4: NTN UL Time synchronization requirements
Topic #5: NTN UL frequency synchronization requirement
Topic #6: NTN Measurements
Topic #7: RRM requirements for beam switching

## Slide 4: Summary
Main RRM issues and preliminary proposals have been discussed
  In green: proposals for which no concern have been raised
  In orange: proposals for which a potential agreement may be found with suggested changes (needs further discussion)
  In purple: proposals for which there is no agreement
However RRM highly depends on
  Use cases/scenarios selected and defined
  RAN1/2 work progressed
  Possibly on exemplary band(s) selected

## Slide 5: Topic #1: General RAN4 RRM NTN related aspects
Select and define NTN use cases and scenarios. Please also refer to [97e][312] NTN_Solutions.
  Explanation: NTN use cases and scenarios to be selected and further defined in accordance with RAN4 RF session.
  No concern raised so far
Wait for the Reference Point (RP) to be defined by RAN1.
  No concern raised so far

## Slide 6: Topic #1: General RAN4 RRM NTN related aspects (cont’d)
Work method to down select the list of NTN-related RRM KPIs:
  1st step: Establish list of candidate RRM requirements for NTN based on existing Rel-16 set of parameters (e.g. TS 38.133);
  2nd step: Based on use cases/scenarios definition as well as RAN1/2 framework definition, down-select the requirements to be considered with priority for NTN in Rel-17 and consider the need to add some additional ones.
No agreement. However, there is a common consensus that RRM related agreements can be done once RAN1/RAN2 design has sufficiently progressed and there are agreements on RF on scenarios etc.

## Slide 7: Topic #2: GNSS requirements
UEs with GNSS capabilities are assumed (also in WID).
  No concern raised so far
Further discuss the need for 3GPP to assume GNSS capability on board of satellites.
  No concern raised so far
Further discuss the required accuracy (depending on the scenarios) of external reference to be used for UE timing & frequency pre-compensation and how this compares with the accuracy provided by GNSS in a practical setup.
  No concern raised so far

## Slide 8: Topic #3: PVT Satellite precision
Topic not yet mature to be discussed.

## Slide 9: Topic #4: NTN UL Time synchronization requirements (cont’d)
The following requirements shall be defined but require RAN1 further progress
  Timing Advance adjustment accuracy considering
    At least the total error budget for regulating TA during a call: ΔUE-pos, ΔSat-pos, Timing Advance adjustment accuracy and TA command resolution error
    FFS for other cases
  Timing error limits & UE Time alignment behaviour
    More investigation required for timing error requirement;
    FFS: at least CP will have to be preserved.
  Timing Issues and Requirements for UE with 2 feeder-links
    Service link related, and depending if the feeder-link switch is soft or hard.

## Slide 10: Topic #4: NTN UL Time synchronization requirements (cont’d)
Test definition should be considered by RAN4 for NTN delay compensation. The test can be discussed once the core requirements are completed.
  Potential agreement with changes: “Test definition should be considered by RAN4 for NTN delay compensation. The test can be discussed once the core requirements are completed, if such a test is found feasible”.

## Slide 11: Topic #5: NTN UL frequency synchronization requirement
Even if UE Doppler UL pre-compensation method is based on GNSS, NTN UL Synchronization Requirement can be considered in RF session.
  No concern raised so far. It is agreed to have UL pre-compensation method based on GNSS. The final UE UL frequency accuracy requirement is defined in RAN4 UE RF session.
Test definition should be considered by RAN4 for NTN Doppler compensation. The test can be discussed once the core requirements are completed.
  Potential agreement with changes: “Test definition should be considered by RAN4 for NTN Doppler compensation. The test can be discussed once the core requirements are completed, if such a test is found feasible”.

## Slide 12: Topic #6: NTN Measurements
At least RSRP measurement accuracy for NTN-specific operation should be considered as a candidate option.
  No concern raised so far. There are also other measurements like RSRQ and SINR to consider.
Consider new measurement type requirements for
  New HO procedures defined by RAN2 if any (part of normal RAN4 working process)
  All scenarios NTN-to-NTN, NTN-to-TN and TN-to-NTN
    Discuss once the Intra NTN mobility has sufficiently progressed. Intra NTN mobility refers to idle and connected mode mobility between NTN cells (e.g. intra or inter satellite).
  No concern raised so far

## Slide 13: Topic #6: NTN Measurements
Select a list of (core) measurement requirements to be considered with priority.
  After sufficient progress is made in RAN1 / RAN2.
  However, an initial list has been already proposed.

## Slide 14: Topic #7: RRM requirements for beam switching
Define necessary beam management RRM requirements for UEs supporting NTN, depending on the selected NTN solution:
  e.g. beam(s)-to-cell mapping, is same PCI for several satellite beams, if one PCI per satellite beam etc.
  RAN4 beam management requirements do not cover PCI change. Too early, we also need to understand if new procedures are introduced in other groups.
As baseline, similar procedures as for TN beam switching RRM requirements should apply to NTN.
  It is too early to conclude. NTN beam switching is not yet defined. There is no such thing as TN beam switching in legacy NR
  The context of beam management is not clear

## Slide 15: Open issues (others)
Topic #1: General RAN4 RRM NTN related aspects
  FFS the required PVT accuracy. Need more RAN1 agreement/conclusion.
Topic #2: GNSS requirements
  It is assumed that there are no interruptions of GNSS measurements during NTN operation
  Wait for RAN RF exemplary (FR1) band decision
  GNSS measurement & report required periodicities
Topic #3: PVT Satellite precision
  The Satellite position accuracy (ΔU) and satellite velocity accuracy (ΔV) topic is not yet mature to be discussed.
  Wait for RAN1 decisions
Topic #5: NTN UL frequency synchronization requirement
  Further discuss NTN UL Synchronization Behaviour
  Wait for RAN1 decisions

## Slide 16
Annex for information

## Slide 17: Possible NTN Parameters
SA Mobility States | Essential Parameter | Parameter Name
RRC_IDLE state mobility | Cell Re-selection | UE measurement capability
 |  | Measurement and evaluation of serving cell
 |  | Measurements of intra-frequency NR cells
 |  | Measurements of inter-frequency NR cells
 |  | Maximum interruption in paging reception
RRC_CONNECTED state mobility | Handover Parameters - NR Handover | NR FR1 - NR FR1 Handover
 | RRC Connection Mobility Control | SA: RRC Re-establishment
 |  | Random access
 |  | SA: RRC Connection Release with Redirection
Table 1 for information: Possible NTN Parameters related to SA mobility states

## Slide 18: Possible NTN Parameters (cont’d)
Essential Parameter | Parameter Name
Timing Parameter | UE transmit timing
 | UE timer accuracy
 | Timing advance
Signalling characteristics Parameter | Radio Link Monitoring
Table 2 for information : Possible NTN Parameters related to Timing and Signaling Characteristics
Parameter Name | Specific parameter requirement
General measurement requirement | Measurement gap
 | UE Measurement capability
NR intra-frequency measurements | Requirements applicability
NR inter-frequency measurements | Requirements applicability
Table 3 for information: Possible NTN Parameters related to Measurement Procedures

## Slide 19: Possible NTN Parameters (cont’d)
Intra-frequency RSRP accuracy requirements for FR1: Specific-NTN Absolute SS-RSRP Accuracy Specific-NTN Relative SS-RSRP Accuracy
Inter-frequency RSRP accuracy requirements for FR1 Specific-NTN Absolute SS-RSRP Accuracy Specific-NTN Relative SS-RSRP Accuracy
RSRP Measurement Report Mapping
Table 4 for information : Possible NTN Parameters related to Measurement Performance Requirements (NR Measurements only)