## Slide 1: WF on ultra-low BLER requirements
R4-2017057
Moderator (Ericsson)

## Slide 2: Agreements from first round (UE FMCS)
Preliminary requirement values for UE:
  15kHz, 2RX: [3.2] dB
  15kHz, 4RX: [3.3] dB
  30kHz 2RX: [0.6] dB
  30kHz, 4RX: [0.7] dB
  Can be updated next meeting if further simulations available

## Slide 3: Agreements from first round (BS)
Requirement values
15kHz, 5MHz Bandwidth, Type A mapping | -5.1 dB
15kHz, 10MHz Bandwidth, Type A mapping | -5.9 dB
30kHz, 10MHz Bandwidth, Type A mapping | -5.4 dB
30kHz, 40MHz Bandwidth, Type A mapping | -6.2 dB
15kHz, 5MHz Bandwidth, Type B mapping | -5.2 dB
15kHz, 10MHz Bandwidth, Type B mapping | -5.9 dB
30kHz, 10MHz Bandwidth, Type B mapping | -5.5 dB
30kHz, 40MHz Bandwidth, Type B mapping | -6.2 dB

## Slide 4: Agreements from the first round (CQI)
Use pass/fail criteria for the CQI test
LS to be sent to RAN5 once CQI requirement is finalized

## Slide 5: Agreements from the second round (CQI)
Parameters
  Can be fine tuned in the next meeting, but these parameters are suggested for simulation
Parameter |  |  | Unit | FDD |  | TDD
Bandwidth |  |  | MHz | 10 | 40 | 
Number of allocated PDSCH resource blocks |  |  |  | 52 | 106 | 
Subcarrier spacing |  |  | kHz | 15 | 30 | 
MCS table |  |  |  | Table 3 |  | 
PDSCH starting symbol/length |  |  |  | 2/12 |  | 
Number of PDSCH MIMO layers |  |  |  | 1 |  | 
PDSCH mapping type |  |  |  | Type A |  | 
DMRS type |  |  |  | Type 1 |  | 
DMRS duration |  |  |  | single-symbol DMRS |  | 
Number of additional DMRS |  |  |  | 1 |  | 
Slot pattern |  |  |  | N/A | 7D1S2U, S=6D: 4G: 4U | 
Propagation channel |  |  |  | AWGN |  | 
Antenna configuration |  |  |  | 1x2, ULA low​ 1x4, ULA low​ |  | 
Beamforming Model |  |  |  | As specified in Annex B.4.1 |  | 
ZP CSI-RS configuration | CSI-RS resource Type |  |  | Periodic |  | 
 | Number of CSI-RS ports (X) |  |  | 1 |  | 
 | CDM Type |  |  | No CDM |  | 
 | Density (ρ) |  |  | 1 |  | 
 | First subcarrier index in the PRB used for CSI-RS (k0) |  |  | Row 2,4 |  | 
 | First OFDM symbol in the PRB used for CSI-RS (l0) |  |  | 9 |  | 
 | CSI-RS periodicity and offset |  | slot | 5/1 | 10/1 | 
NZP CSI-RS for CSI acquisition | CSI-RS resource Type |  |  | Periodic |  | 
 | Number of CSI-RS ports (X) |  |  | 1 |  | 
 | CDM Type |  |  | No CDM |  | 
 | Density (ρ) |  |  | 3 |  | 
 | First subcarrier index in the PRB used for CSI-RS (k0, k1) |  |  | Row 1,(0,-) |  | 
 | First OFDM symbol in the PRB used for CSI-RS (l0) |  |  | 13 |  | 
 | NZP CSI-RS-timeConfig periodicity and offset |  | slot | 5/1 | 10/1 | 
CSI-IM configuration | CSI-IM resource Type |  |  | Periodic |  | 
 | CSI-IM RE pattern |  |  | 0 |  | 
 | CSI-IM Resource Mapping (kCSI-IM,lCSI-IM) |  |  | (4, 9) |  | 
 | CSI-IM timeConfig periodicity and offset |  | slot | 5/1 | 10/1 | 
ReportConfigType |  |  |  | Periodic |  | 
CQI-table |  |  |  | Table 3 |  | 
reportQuantity |  |  |  | cri-RI-PMI-CQI |  | 
timeRestrictionForChannelMeasurements |  |  |  | Not configured |  | 
timeRestrictionForInterferenceMeasurements |  |  |  | Not configured |  | 
cqi-FormatIndicator |  |  |  | Wideband |  | 
pmi-FormatIndicator |  |  |  | Wideband |  | 
Sub-band Size |  |  | RB | 8 | 16 | 
Csi-ReportingBand |  |  |  | 1111111 |  | 
CSI-Report periodicity and offset |  |  | slot | 5/0 | 10/9 | 
aperiodicTriggeringOffset |  |  |  | Not configured |  | 
Codebook configuration |  | Codebook Type |  | typeI-SinglePanel |  | 
 |  | Codebook Mode |  | 1 |  | 
 |  | (CodebookConfig-N1,CodebookConfig-N2) |  | Not configured |  | 
 |  | CodebookSubsetRestriction |  | 010000 |  | 
 |  | RI Restriction |  | 00000001 |  | 
Physical channel for CSI report |  |  |  | PUCCH |  | 
CQI/RI/PMI delay |  |  | ms | 8 | 9.5 | 
Maximum number of HARQ transmission |  |  |  | 1 |  | 
Target BLER |  |  |  | 10^-5 |  | 
PBCH |  |  |  | slot#0 per 20ms periodicity |  | 
PT-RS |  |  |  | Disabled |  | 
PDSCH is not scheduled on slots containing CSI-RS or slots which are not full DL |  |  |  |  |  | 

## Slide 6: Open issues (CQI)
Issue 1 Confidence level and X: Make decision in RAN4#98e
  Op1: 98.6% Confidence level with X = 0 dB
  Op2: 99% Confidence level with X = 0 dB
  Op3: 99.999% Confidence level with X = [0.5] dB
Issue 2a: CQI Lower bound
  Option 1: Lower bound
  Option 2: No lower bound
Issue 2b: SNR pairs
  Companies are requested to provide their view at the next meeting whether CQI requirement should be defined on SNR pairs that are 1dB apart (test is passed at either of the pair)
Issue 2c: FFS 1 or 2 SNR test points
  2 SNR test points means that two SNR points or two SNR pairs are defined and that the UE must pass at both SNR pairs
  Companies are requested to provide views on whether to define 1 or 2 SNR pairs at the next meeting
  SNR points may have a single SNR per point or a pair of SNR 1dB apart for each test point, depending on the outcome of 2b
Issue 3: Applicability rule for FMCS and CQI if op3 in issue 1 agreed
  Option 1: Define applicability rule
  Option 2: No applicability rule
Companies are encouraged to bring simulation results for BLER and CQI reporting with 0.5dB step to discuss the feasibility of X=[0.5]dB