## Slide 1: WF on NTN solutions
Moderator, THALES

## Slide 2: Outline
Proposed way forward based on the outcomes of “Email discussion summary for [97e][312] NTN_Solutions”
See R4-2017630

## Slide 3: Content
Topic #1: General RAN4 use cases related aspects
Topic #2: System NTN RF core requirements
Topic #3: FR1 proposed Exemplary Frequency band for NTN
Topic #4: FR2 proposed Exemplary Frequency band for NTN
Topic #5: Exemplary Frequency band for HAPS/HIBS
Topic #6: RAN4 Proposed RF core requirements

## Slide 4: Summary
List of proposals for each topics discussed
  Only the “green” proposals are agreeable in this WF.
  The “purple” proposals are not agreed.
  The “orange” proposals are not agreed:
    If there is a GTW session and we could agree on some of them, this WF will be revised anyway;
    Please also note that the “orange” proposals were the results of “agreed with changes” comments.

## Slide 5: Topic #1: General RAN4 use cases related aspects (cont’d)
RAN4 should consider all the relevant sources (including but not limited to ITU-R Radio Regulations, relevant national regulations, pre-existing Harmonized Standards developed for example in ETSI, coexistence studies approved by regulatory bodies and/or 3GPP specifications) in order to specify NTN RF requirements.
  no concerns raised so far
RAN4 should select appropriate exemplary bands for NTN and to carry the needed adjacent channel coexistence studies in order to specify NTN RF requirements.
  no concern raised so far
3GPP RAN4 should provide/conduct relative independent adjacent channel coexistence studies to develop RF requirements for NTN.
  no concern raised so far

## Slide 6: Topic #1: General RAN4 use cases related aspects (cont’d)
No impact on IMT network is a pre-requisite.
  no concern raised so far
For coexistence studied, both NTN/NTN and NTN/TN in adjacent channels should be considered.
  no concern raised so far
RAN4 need to consider how to take into account the heterogeneous cell patterns of NTN and TN networks assuming that they serve the same areas.
  no concern raised so far
TSG-RAN to decide the change from “HAPS” to “HIBS” in the NTN WI
  no concern raised so far

## Slide 7: Topic #1: General RAN4 use cases related aspects (cont’d)
For exemplary band in FR1, RAN4 should consider at least satellite scenarios C1.1, C2.1 (LEO Earth Fixed Beams and Earth Moving Beams) and A1 (GEO):
  C1.1: LEO @ 600 km altitude, FR1, Earth fixed beams
  C2.1: LEO @ 600 km altitude, FR1, Earth moving beams
  A1: GEO @ 35,786 km altitude, FR1, Earth fixed beams
  no concern raised so far
Further include following scenarios:
  C1.2: LEO @ 1200 km altitude, FR1, Earth fixed beams
  C2.2: LEO @ 1200 km altitude, FR1, Earth moving beams
  no concern raised so far

## Slide 8: Topic #1: General RAN4 use cases related aspects (cont’d)
Further discuss if and which HAPS scenarios should be considered by RAN4 as part of the WI NR-NTN-solutions.
  no concern raised so far
ATG is to be considered for separate WI by RAN.
  no concern raised so far
Use TR 38.821 as a baseline/starting point, as long as HAPS is still included, and NTN study aligns with WID in RAN.
  no concern raised so far
Select exemplary bands before going to the detail of RF core requirements.
  no concern raised so far

## Slide 9: Topic #1: General RAN4 use cases related aspects (cont’d)
RAN4 should consider both Earth fixed beam & Earth moving beam.
  no concern raised so far
The simulation scenarios shall be defined based on the permutation and/or combination between NTN/TN or NTN/NTN scenarios.
  no concern raised so far
Networks layout (cell coverage for NTN and TN) and NTN UEs distribution would need to be further aligned.
  no concern raised so far
Further discuss simulation assumptions and the down selection of scenarios for the coexistence studies.
  no concern raised so far

## Slide 10: Topic #2: System NTN RF core requirements
Interfaces between different NTN entities should be clarified.
  no concern raised so far
Do not consider the feederlink from the RAN4 RF perspective in NTN Release-17.
  no concerns raised so far

## Slide 11
Open issues

## Slide 12: Topic #1: General RAN4 use cases related aspects (cont’d)
At least one exemplary frequency band per FR1 should be defined for satellite.
  Still discussion on replacement of “At least” by “Only”
At least one exemplary frequency band per FR2 should be defined for satellite.
  Proposal not agreeable
Although RAN4 will select exemplary band(s) in the current NR-NTN-solutions WI, the definition of additional NR bands for satellite will be part of dedicated RAN4 led Release-17 work items.
  Potential agreement with changes: “Although RAN4 will select exemplary band(s) in the current NR-NTN-solutions WI, the definition of additional NR bands for satellite can be part of dedicated RAN4 led work items based on TSG-RAN’s decision.”
The frequency ranges considered for satellite should be spectrum allocated by ITU to satellite services should be considered.
  Potential agreement with changes: “Spectrum allocated by ITU to mobile satellite services shall be considered”

## Slide 13: Topic #1: General RAN4 use cases related aspects (cont’d)
RAN4 should further discuss and decide ACS & ACLR requirements to be considered for TN in the coexistence study with NTN, depending on FR and BW configuration.
  Upon clarification request, the proposal is revised as follow by Moderator “For the purpose of simulations for the coexistence study between TN & NTN, the TN BS/UE ACLR & ACS parameters need to be further discussed. It may depend on FR and BW configuration”
NTN RF requirements shall be specified assuming no impact on TN RF requirements.
  Possible agreement if changes « NTN RF requirements shall be specified assuming no significant impact on TN RF requirements.”

## Slide 14: Topic #1: General RAN4 use cases related aspects (cont’d)
RAN-WG4 may consider the definition of additional NR bands for HAPS as part of dedicated RAN4 led Release-17 work items.
  Proposal not agreeable: More discussion required about HAPS definition and bands
LS to RAN plenary for guideline and the accurate definition for HAPS.
  Proposal not agreeable: One company commented no need to send any LS if the WI is proposed for update in next RAN meeting.
  No need to send LS if discussion for WID update in RAN plenary.

## Slide 15: Topic #1: General RAN4 use cases related aspects (cont’d)
“At least for FR1, RAN4 shall consider Handheld UE & VSAT UE with described characteristics:
  Handheld: Omnidirectional antenna, 500 km/h (e.g. on board a high speed train), Linear: +/-45°X-pol, up to 200 mW (UE power class 3)
  VSAT: Directive antenna (up to 60 cm equivalent aperture diameter), Up to 1200 km/h (e.g. mounted UE on a building or moving platforms, e.g., aircrafts, trains, vessels or vehicles. Examples of such UE can be ESIM and VSAT), Circular polarisation, up to 20 W Tx power.”
  Potential agreement with changes: Remove “ESIM and”.
“Further discuss other UE-types to be considered for FR1 & FR2”.
  Potential agreement with changes: Remove “& FR2”.
Use 3GPP TS 38.101-1 and 38.101-2 for NTN RF UE requirements.
  Potential agreement with changes: Remove “and 38.101-2”.

## Slide 16: Topic #1: General RAN4 use cases related aspects (cont’d)
For some selected UE RF requirements, it is expected to adopt same performance requirements (e.g. REFSENS, Tx Power) for NTN to ensure operational compatibility across NTN and TN.
  Proposal not agreeable: Unknown for the time being.
Possible adaptations based on the co-existence studies outcomes (NTN with TN or NTN with NTN) may be considered for NTN RF BS requirements.
  Proposal not agreeable: 2 companies disagree.

## Slide 17: Topic #2: System NTN RF core requirements
Consider NTN Payload+NTNGW as a single entity (e.g. Repeater or Remote Radio Head).
  Potential agreement with changes: “Consider NTN Payload + feederlink + NTNGW as a single entity (e.g. Repeater or Remote Radio Head)”
Consider only the service link from the RAN4 RF perspective in NTN Release-17.
  Proposal not agreeable: To be further discussed. One company shows interest to clarify NTNGW-gNB interface.
Consider only “BS” RF requirements on the service link i.e. at satellite output for DL and at satellite input for UL.
  Proposal not agreeable: Further discussion required for the interface between NTNGW and gNB.

## Slide 18: Topic #3: FR1 proposed Exemplary Frequency band for NTN
Band characteristics (e.g. available BW, UL/DL configuration, maximum configurable BW size, coexistence conditions) of the candidate bands should be considered for comparison purposes. Note that views from operators should be taken into account in priority.
  Proposal not agreeable: further discuss criteria to be used (if any criteria) at RAN4#98e

## Slide 19: Topic #4: FR2 proposed Exemplary Frequency band for NTN
No agreement
  Several companies showed disagreement for coexistence scenarios NTN FDD with TN TDD in adjacent bands in FR2.

## Slide 20: Topic #5: Exemplary Frequency band for HAPS/HIBS
To early to discuss, postponed to RAN4#98e

## Slide 21: Topic #6: RAN4 Proposed RF core requirements
RAN4 shall define NTN UE RF requirements based on existing UE RF requirements (specified in TS 38.101-1 and 38.101-2).
  Potential agreement with changes: Remove “and TS 38.101-2”
  38.101-2 cannot be reused as baseline for FDD NTN UE;
Continue discussion with respect to potential NTN UE RF requirements that might be different from TN UE RF.
  Proposal not agreeable: too early for such proposal.
Continue discussion with respect to NTN UE RF requirements (e.g. REFSENS, Maximum Transmitted Power) that should be kept the same as for TN, in order to allow operational compatibility across NTN and TN.
  Proposal not agreeable: Coexistence study and technical analysis required before