## Slide 1: Way Forward on NR-U UE demodulation requirements
Qualcomm
3GPP TSG-RAN4 Meeting #97-e
November 2 - 13 2020
Agenda Item: 7.1.8.1/2/3
Tdoc Num: R4-2017685

## Slide 2: Test Scope
Semi-static Channel Access Devices v/s Dynamic Channel Access Devices
Prioritize test cases agnostic to semi-static and dynamic channel access devices if it is feasible.
Do not define additional test cases dedicated to FBE/LBE devices.

## Slide 3: Test Scope
Test Scenarios
Define requirements for the unlicensed CC, and apply to both Scenario A and C;
FFS: Details of the test set-up for scenario A and C;
For reference:
  Scenario A (Carrier aggregation between licensed band NR (PCell) and NR-U (SCell))
  Scenario C (Stand-alone NR-U (PCell))

## Slide 4: Test Scope
Define tests with fixed DRS window duration set to 1ms.
Tests with SMTC duration larger than COT duration should be deprioritized.

## Slide 5: Test Scope
Bandwidth to be used for Requirements definition
  Option 1: 20 and 80 MHz;
  Option 2: 20, 40, 60 and 80 MHz with applicability rule to test the largest supported BW;
  Option 3: 40MHz (as in rel-15 TDD Demod);
  Option 4: 20 and 40MHz;
    Option 4b: With applicability rule to test the largest supported BW of the two;
  Option 5: Define requirements including 20 MHz ;

## Slide 6: Test Scope
Do not define tests for NR-U Demod PDCCH demodulation requirements;
FFS whether to define CQI Requirements, discuss the parameters and UE behaviour for CQI reporting tests;

## Slide 7: Downlink Transmission Model
Use Burst Transmission Model for LAA (36.101-4, B.8) as a starting point.
Define tests with fixed DL Transmission duration
  With Fixed DL transmission duration in each of the DL transmission duration, the actual number of transmitted slots is random with below candidate options
  FFS for the fixed duration length
Values for random COT (S1)
  Option 1: {2, 6, 10, 16} Slots;
  Option 2: {1,6,10,16} Slots;
  Option 3: {1,2,3,4} Slots;
  Note: 1 slot is shorter than the agreed 1ms DRS duration window
Notes: Intel: Change DRS duration window as 0.5ms.
Intel: We should not exclude partial last slot and 1 slot cases.

## Slide 8: Downlink Transmission Model
Length of the last Slot in the burst (S2)
  Option 1: Random length, {6, 9, 12, 14} Symbols with the first 2 symbols allocated for PDCCH transmission;
  Option 2: Fixed length according to proposed model;
Notes: Intel: Change DRS duration window as 0.5ms.
Intel: We should not exclude partial last slot and 1 slot cases.

## Slide 9: Downlink Transmission Model
Slot format
  Option 1: For 30kHz, 2ms, DDDS (S=7D:2G:2U) derived from the DL Model;
  Option 2: For 30kHz, 7D -1S-2U;
  Option 3: For 30kHz, {D, DS, DDS, DDDS} derived from the DL Model;
  Other options
Other Parameters
  Option 1: (see table)
  Other options not precluded
DL Transmission Model (Note 1) | Maximum COT Duration | ms | 1.9
 | Minimum Idle Time after COT | ms | 0.1
 | Fixed Frame Period (Note 2) | ms | 2
 | Probability of LBT Failure pLBT |  | [TBD]
 | Guard Symbols |  | 2 Symbols
 | UL Symbols |  | 2 Symbols
 | Number of slots between PDSCH and corresponding HARQ-ACK information |  | 3 if mod(i,4) = 0 2 if mod(i,4) = 1 5 if mod(i,4) = 2 4 if mod(i,4) = 3
Notes: According to the definition proposed in [2] This Parameter applies only for ChannelAccessType-r16 = ‘semistatic’. |  |  | 

## Slide 10: LBT Parameters
Model LBT Failure as part of the Downlink Transmission model;
Apply the Downlink Transmission model to all DL signals in unlicensed carrier (including SSB and TRS transmission);
FFS whether is needed to define a separate LBT model for FBE and LBE;
Do not define tests with sub-band LBT failure (either all sub-bands are transmitted, or no sub-band is transmitted).

## Slide 11: LBT Parameters
Probability of LBT Failure for Scenario C:
  Option 1: 0 (always clear channel);
  Option 2: Same probability as Scenario A;
  Option 3: TBD>0 (probability of occupied channel);
Probability of LBT Failure for Scenario A:
  Option 1: TBD>0 (probability of occupied channel)

## Slide 12: Simulation Assumptions for PDSCH Tests
Use 20 MHz LBT BW (for channel sensing and clear channel assessment).
Do not multiplex SSB and Data.
Define tests for TDD 30kHz only.
Define tests with low delay spread and low doppler speed propagation channel.
Q factor for SSB: = 8;

## Slide 13: Simulation Assumptions for PDSCH Tests
Test Design
  Option 1: Use NR PDSCH Demod Performance Tests as a starting point (R16 NR CA for Scenario A, R15 PDSCH for Scenario C);
  Option 2: Use LTE LAA Demod Performance Test setup as a starting point for scenario A

## Slide 14: Simulation Assumptions for PDSCH Tests
PDSCH Type
  Option 1: Type A only;
  Option 2: Type B only for UE with capability, Type A otherwise;
  Option 3: Type A plus Rel-15 Type B for partial slots, dedicated test to verify typeB-PDSCH-length-r16 capability with corresponding applicability rule;
PDSCH Type B Start and Length for PDSCH Performance Tests (if agreed to use PDSCH mapping Type B)
  Option 1: Subset of fixed [start, length] values: [2,4], [2,12];
  Option 2: Random start in Symbol {2, 9} and length {12, 5} for first slot of burst. Start in Symbol 2 and length {4, 7, 10, 12} for last slot of burst. Start in Symbol 2 and length 12 for other slots;
  Option 3: Start in Symbol {7} and length {4} symbols;

## Slide 15: Simulation Assumptions for PDSCH Tests
PDCCH Format to be used
  Option 1: Format 2-0, using CO-DurationPerCell-r16 to indicate the COT duration;
  Option 2: Do not use DCI Format 2-0;