## Slide 1: 3GPP TSG-RAN WG4 Meeting #97-e Electronic Meeting, 2nd – 13th Nov, 2020
Huawei, HiSilicon
Way forward on NR-U BS demodulation requirements for general part and PUSCH
R4-2017688

## Slide 2: Background
R4-2012611, Way Forward on NR-U BS demodulation requirements, RAN4#96-e, Ericsson

## Slide 3: General: Test scopes
Define BS performance requirements as band agnostic way
Test applicability
  Define the applicability rules based on BS’s declaration on features rather than scenarios:
    The performance requirements for interlaced PUSCH should apply only if BS declares to support PUSCH with interlaced resource allocation
    The performance requirements for interlaced PUCCH should apply only if BS declares to support PUCCH with interlaced resource allocation
    The performance requirements for wideband PRACH should apply only if BS declares to support PRACH with long sequence L=1151 for 15kHz SCS and L=571 for 30kHz SCS
How to handle Rel-15 test requirements for BS supporting NR-U
  Option 1: Reuse the existing Rel-15 test applicability rules for NR Rel-15 performance requirements testing
  Other options not precluded

## Slide 4: General: Test Scenarios
  Define requirements that are agnostic to wideband operation 1 and 2
Not consider LBT model for NR-U BS performance requirements definition
Always schedule PRBs between 2 contiguous LBT sub-bands during the test, i.e. not configure guard band

## Slide 5: PUSCH
Bandwidth
    Option 1: Define the requirements for single carrier with 20MHz only with the test applicability rule that a BS only has to perform tests for the largest supported bandwidth based on BS vendor’s declaration.
      The applicability rule defined in NR Rel-15 for different channel bandwidths needs to applied: the tests shall be done only for the supported widest supported channel bandwidth. If performance requirement is not specified for this widest supported channel bandwidth, the tests shall be done by using performance requirement for the closest channel bandwidth lower than this widest supported bandwidth; the tested PRBs shall then be centered in this widest supported channel bandwidth.
    Option 2: Define the requirements for single carrier with 20MHz,40MHz,60MHz and 80MHz, with the test applicability rule that a BS only has to perform tests for the largest supported bandwidth based on BS vendor’s declaration.

## Slide 6: PUSCH
Waveform: CP-OFDM
Use first single interlace per slot.
SCS: Both 15kHz and 30kHz
Test applicability rule for different SCS:
  Test performance requirements for 15kHz and/or 30kHz SCS based on BS’s declaration
  If BS declares to support both 15kHz and 30kHz
    Only test performance requirements for 30kHz
TDD pattern:
  7D2S1U S=6D:4G:4U for 30kHz SCS
  3D1S1U S=10D:2G:2U for 15kHz SCS

## Slide 7: PUSCH
  PUSCH mapping type
  Option 1: Only Type B
  Option 2: Both Type A and Type B
  Number of scheduled symbols for PUSCH transmission:
  14 symbols per slot
DM-RS configuration:
  DM-RS configure type 1 with single-symbol and dmrs-AdditionalPosition ‘pos1’
MCS
  MCS 20, FFS MCS 16
  Antenna configuration: 1x2
Propagation condition:
  TDLA30-10

## Slide 8: PUSCH
Maximum number of HARQ transmission: 4
RV sequence
  Option 1: {0,2,0,2}
  Option 2: {0,2,3,1}
Test metric for PUSCH performance requirements:
  SNR@70% max throughput
Performance requirements for CG-UCI multiplexed on PUSCH with interlace allocation
  Option 1: Not introduce
  Option 2: Introduce performance requirements for CG-UCI multiplexed on PUSCH with interlaced resource allocation and without HARQ-ACK, CSI part 1 and CSI part 2
  Option 3: Consider introduce a Rel-15 requirement for HARQ-ACK multiplexing on PUSCH with more than 2 HARQ-ACK information bits and using it to cover CG-UCI multiplexing on CG-PUSCH in NR-U scenario with proper applicability rule