## Slide 1: WF on ultra-low BLER requirements
R4-2017057
Moderator (Ericsson)

## Slide 2: Agreements from first round (UE FMCS)
Preliminary requirement values for UE:
  15kHz, 2RX: [3.2] dB
  15kHz, 4RX: [3.3] dB
  30kHz 2RX: [0.6] dB
  30kHz, 4RX: [0.7] dB
  Can be updated next meeting if further simulations available

## Slide 3: Agreements from first round (BS)
Requirement values
15kHz, 5MHz Bandwidth, Type A mapping | -5.1 dB
15kHz, 10MHz Bandwidth, Type A mapping | -5.9 dB
30kHz, 10MHz Bandwidth, Type A mapping | -5.4 dB
30kHz, 40MHz Bandwidth, Type A mapping | -6.2 dB
15kHz, 5MHz Bandwidth, Type B mapping | -5.2 dB
15kHz, 10MHz Bandwidth, Type B mapping | -5.9 dB
30kHz, 10MHz Bandwidth, Type B mapping | -5.5 dB
30kHz, 40MHz Bandwidth, Type B mapping | -6.2 dB

## Slide 4: Agreements from the first round (CQI)
Use pass/fail criteria for the CQI test
LS to be sent to RAN5 once CQI requirement is finalized

## Slide 5: Agreements from the second round (CQI)
Parameters
  Can be fine tuned in the next meeting, but these parameters are suggested for simulation
Parameter |  |  | Unit | FDD |  | TDD
Bandwidth |  |  | MHz | 10 | 40 | 
Number of allocated PDSCH resource blocks |  |  |  | 52 | 106 | 
Subcarrier spacing |  |  | kHz | 15 | 30 | 
MCS table |  |  |  | Table 3 |  | 
PDSCH starting symbol/length |  |  |  | 2/12 |  | 
Number of PDSCH MIMO layers |  |  |  | 1 |  | 
PDSCH mapping type |  |  |  | Type A |  | 
DMRS type |  |  |  | Type 1 |  | 
DMRS duration |  |  |  | single-symbol DMRS |  | 
Number of additional DMRS |  |  |  | 1 |  | 
Slot pattern |  |  |  | N/A | 7D1S2U, S=6D: 4G: 4U | 
Propagation channel |  |  |  | AWGN |  | 
Antenna configuration |  |  |  | 1x2, ULA low​ 1x4, ULA low​ |  | 
Beamforming Model |  |  |  | As specified in Annex B.4.1 |  | 
ZP CSI-RS configuration | CSI-RS resource Type |  |  | Periodic |  | 
 | Number of CSI-RS ports (X) |  |  | 1 |  | 
 | CDM Type |  |  | No CDM |  | 
 | Density (ρ) |  |  | 1 |  | 
 | First subcarrier index in the PRB used for CSI-RS (k0) |  |  | Row 2,4 |  | 
 | First OFDM symbol in the PRB used for CSI-RS (l0) |  |  | 9 |  | 
 | CSI-RS periodicity and offset |  | slot | 5/1 | 10/1 | 
NZP CSI-RS for CSI acquisition | CSI-RS resource Type |  |  | Periodic |  | 
 | Number of CSI-RS ports (X) |  |  | 1 |  | 
 | CDM Type |  |  | No CDM |  | 
 | Density (ρ) |  |  | 3 |  | 
 | First subcarrier index in the PRB used for CSI-RS (k0, k1) |  |  | Row 1,(0,-) |  | 
 | First OFDM symbol in the PRB used for CSI-RS (l0) |  |  | 13 |  | 
 | NZP CSI-RS-timeConfig periodicity and offset |  | slot | 5/1 | 10/1 | 
CSI-IM configuration | CSI-IM resource Type |  |  | Periodic |  | 
 | CSI-IM RE pattern |  |  | 0 |  | 
 | CSI-IM Resource Mapping (kCSI-IM,lCSI-IM) |  |  | (4, 9) |  | 
 | CSI-IM timeConfig periodicity and offset |  | slot | 5/1 | 10/1 | 
ReportConfigType |  |  |  | Periodic |  | 
CQI-table |  |  |  | Table 3 |  | 
reportQuantity |  |  |  | cri-RI-PMI-CQI |  | 
timeRestrictionForChannelMeasurements |  |  |  | Not configured |  | 
timeRestrictionForInterferenceMeasurements |  |  |  | Not configured |  | 
cqi-FormatIndicator |  |  |  | Wideband |  | 
pmi-FormatIndicator |  |  |  | Wideband |  | 
Sub-band Size |  |  | RB | 8 | 16 | 
Csi-ReportingBand |  |  |  | 1111111 |  | 
CSI-Report periodicity and offset |  |  | slot | 5/0 | 10/9 | 
aperiodicTriggeringOffset |  |  |  | Not configured |  | 
Codebook configuration |  | Codebook Type |  | typeI-SinglePanel |  | 
 |  | Codebook Mode |  | 1 |  | 
 |  | (CodebookConfig-N1,CodebookConfig-N2) |  | Not configured |  | 
 |  | CodebookSubsetRestriction |  | 010000 |  | 
 |  | RI Restriction |  | 00000001 |  | 
Physical channel for CSI report |  |  |  | PUCCH |  | 
CQI/RI/PMI delay |  |  | ms | 8 | 9.5 | 
Maximum number of HARQ transmission |  |  |  | 1 |  | 
Target BLER |  |  |  | 10^-5 |  | 
PBCH |  |  |  | slot#0 per 20ms periodicity |  | 
PT-RS |  |  |  | Disabled |  | 
PDSCH is not scheduled on slots containing CSI-RS or slots which are not full DL |  |  |  |  |  | 

## Slide 6: Open issues (CQI)
Issue 1 Confidence level and X:
  Op1: 98.6% Confidence level with X = 0 dB
  Op2: 99% Confidence level with X = 0 dB
  Op3: 99.999% Confidence level with X = [0.5] dB
Issue 2: CQI Lower bound and number of SNR test points
  Option 1: Lower bound, 2 SNR test points
  Option 2: No lower bound, 2 SNR test points
  Option 3: Lower bound, 1 SNR test point
  Option 4: No lower bound, 1 SNR test point
Issue 3: Applicability rule for FMCS and CQI
  Option 1: Define applicability rule
  Option 2: No applicability rule