## Slide 1: WF on testability enhancements to reduce test time
vivo
3GPP TSG-RAN WG4 Meeting #97-e R4-2017597
Electronic Meeting, 2-13 Nov., 2020
Agenda item: 13.1
Document for: Approval

## Slide 2: Way forward
RAN4 agrees to further study the following Testability enhancements approaches to reduce test time
  Option1: As part of the enhanced test methods for FR2 study item, RAN4 should discuss beam sweeping techniques further
  Option2: Adopt 4x2 array as the antenna assumption for deriving measurement grid for PC3, especially for smart phone UE.
  Option3: Develop two sets of measurement grids for PC3, one is the same as current grids based on 8x2 array assumption, the other is relatively sparse grids based on 4x1 (or 4x2) assumption. Applicability depends on UE declaration
  Option4: RAN4 study RSRP accuracy at high downlink signal level and then check if RSRP could take place of EIS search as baseline for RX beam peak search
  Option5: For EIRP test of UL MIMO including TX beam peak search, only one link polarization is enough.
  Option6: For EIRP test when TX diversity (dual polarization transmission) is activated, only one link polarization is enough.
  Other proposals are not precluded

## Slide 3
Next steps for testability enhancements to reduce test time
  Detailed parameters of 4x2 array antenna assumption for PC3 should be aligned next meeting
  Simulated new measurement grids with estimated testing time based on 4X2 antenna array are encouraged
  The agreed MU of measurement grids for TRP, beam peak search, Spherical coverage in TR38.810 should be followed
  Further study the RSRP accuracy at high downlink signal level for RSRP based Rx beam peak search
  Companies are encouraged to bring analysis of influences to the UE, to study whether only one link polarization is enough, for 2Tx test cases (TxD and UL MIMO)
  Prioritization of the potential approaches is needed
  Others?
Way forward

## Slide 4: Reference
  [1] R4-1912108, “On Test Time Reduction for NR FR2 UE Test Cases”, Keysight, RAN WG4 #92bis, October 2019
  [2] R4-2014726, “Discussion on FR2 test time reduction”, Samsung, RAN4#97-e, Nov., 2020
  [3] R4-2014491, “Beam sweeping and test time reduction in FR2”, Fraunhofer HHI, Fraunhofer IIS, RAN4#97-e, Nov., 2020