## Slide 1: Rel-17 FR1 RF enhancement part 1 GTW status
Moderator (Huawei, HiSilicon)
3GPP TSG-RAN WG4 #98-e
Jan 25 – Feb 5, 2021
Electronic meeting

## Slide 2: Issue 1:PC2 Intra-band UL contiguous CA reference RF architecture
  Proposals:
  Option 1:
      A single TX PC2 PA is the baseline to develop MPR and A-MPR requirement;
      Two 100MHz PC2 PA (option 2) may reuse the same MPR values as already the case for PC3 but it should be verified why the worst case 2xPC3 PA 1RB+1RB MPR for non-contiguous UL CA is worse that the 1xPC3 PA related class C PA
      Additional requirement for two PC3 PAs architecture is FFS once single CC related requirements are finalized, potentially using a delta MPR compared to the option 1 baseline
  Option 2: Take “PC2 UL CA with one 26dBm PA 200MHz 1LO” as the reference RF architecture to define requirements, other architectures are not precluded. No need to define 2 sets of RF requirements.
  Option 3: 2PA with PC3 shall be considered as reference for defining MPR requirements. Whether other set of MPR requirements are needed depends on the how much difference compared to 2PA with PC3 case.
  Option 4:
      down select “two 100MHz PC2 PAs” to simplify the discussion.
      Keep both “one 200MHz PC2 PA)” and “two 200MHz PC3 PA” in this WI.
    1st round discussion status：
    Option 1 or Option 2 that with one PC2 PA as reference RF architecture: 8 companies
      Additional MPR/AMPR for other architecture can be added if necessary: 4 companies
    Both one PC2 PA and 2*200MHz PC3 PA architectures should be considered: 2 companies
    Option 4: 1 company
    Recommended WF:

## Slide 3
Issue 2: intra-band UL CA MIMO
Proposals:
Option 1: Do not define UL MIMO+UL CA HPUE requirements in this Rel-17 WI
Option 2: Add intra-band UL CA MIMO for both PC3 and PC2 into the WID
Option 3: Other
1st round discussion status：
Option 1: 5 companies
Option 2: 2 companies
Other: Whether or not UL MIMO + UL CA is part of R17 is not really relevant: if one PC2 PA is used then UL MIMO is covered easily with an additional PC2 PA. if two PC3 PA are used then TxDiv is needed by default thus UL MIMO should be feasible. (2 companies)
Recommended WF:

## Slide 4
Issue 3: intra-band UL NC CA
Refer to discussion in thread[137]

## Slide 5: Issue 4: switching time between SUL and NUL
Note 1 Table 5.2C-1, 5.2C-2, 5.2C-3 and 5.2C-4 in TS 38.101-1
Proposals
  Option 1: change Note1 as in R4-2101854:
  Option 2: No need to change the current contents of Note1
1st round discussion status：
Option 1: 3 companies
Option 2: 2 companies
Other : if we consider current UE and future possible more Tx chain UE, then note 1 may need to be improved.(1 company)
Recommended WF:
NR Band combination for SUL | NR Band (Table 5.2-1)
SUL_n41-n80 | n41, n80
SUL_n41-n81 | n41, n81
SUL_n41-n832 | n41, n83
SUL_n41-n95 | n41, n95
SUL_n77-n802 | n77, n80
SUL_n77-n842 | n77, n84
SUL_n78-n802 | n78, n80
SUL_n78-n812 | n78, n81
SUL_n78-n822 | n78, n82
SUL_n78-n832 | n78, n83
SUL_n78-n842 | n78, n84
SUL_n78-n862 | n78, n86
SUL_n79-n802 | n79, n80
SUL_n79-n812 | n79, n81
SUL_n79-n832 | n79, n83
SUL_n79-n84 | n79, n84
SUL_n79-n95 | n79, n95
NOTE 1: If a UE is configured with both NR UL and NR SUL carriers without enabling UL-MIMO in a cell, the switching time between NR UL carrier and NR SUL carrier is 0 us. NOTE 2: For UE supporting SUL band combination simultaneous Rx/Tx capability is mandatory. NOTE 3: For UE supporting SUL band combination, UL MIMO is not configured on SUL carrier | 
Table 5.2C-1: Operating band combination for SUL in FR1
CR R4-2101854