## Slide 1: WF on remaining BS and UE parameters for 6.425-7.125 and 10.0-10.5 GHz
Ericsson
R4-210xxxx
3GPP TSG-RAN WG4 Meeting # 98-e
Electronic Meeting, 25 Jan - 5 Feb., 2021

## Slide 2: Minimum channel BW / OBUE for 6.425-7.125 GHz
Minimum channel BW, 2 options:
  20 MHz
  50MHz
OBUE - 3 options:
Frequency offset of measurement filter ‑3dB point, f |  | 
Option 1 (channel BW = 20MHz) | Option 2 (channel BW = 50MHz) | Option 3 (channel BW = 50MHz)
0 MHz  f < 20MHz | 0 MHz  f < 10MHz | 0 MHz  f < 50MHz
20MHz  f < min(40MHz, fmax) | 10MHz  f < min(50MHz, fmax) | 50MHz  f < min(100MHz, fmax)
40MHz  f  fmax | 50MHz  f  fmax | 100MHz  f  fmax

## Slide 3: Minimum channel BW / OBUE for 10.0-10.5GHz
Minimum channel BW: 50MHz (agreed)
OBUE for cat B (agreed):
OBUE for cat A?
Limits (yellow) also relaxed by 1 dB,
as for cat B?
Frequency offset of measurement filter ‑3dB point, f | Basic limits (Note 1, 2)
0 MHz  f < 50MHz | 
50 MHz  f < min(100 MHz, fmax) | -13 dBm
100 MHz  f  fmax | -14 dBm
Frequency offset of measurement filter ‑3dB point, f | Basic limits (Note 1, 2)
0 MHz  f < 50MHz | 
50 MHz  f < min(100 MHz, fmax) | -13 dBm
100 MHz  f  fmax | -14 dBm
Frequency offset of measurement filter ‑3dB point, f | Basic limits (Note 1, 2)
0 MHz  f < 50MHz | 
50 MHz  f < min(100 MHz, fmax) | -13dBm
100 MHz  f  fmax | -12 dBm
Frequency offset of measurement filter ‑3dB point, f | Basic limits (Note 1, 2)
0 MHz  f < 50MHz | 
50 MHz  f < min(100 MHz, fmax) | -13dBm
100 MHz  f  fmax | -12 dBm

## Slide 4: ΔfOBUE / ΔfOOB
For 10.0-10.5GHz (agreed):
For 6.425-7.125GHz - 2 options:
Option 1 |  | Option 2 | 
ΔfOBUE | ΔfOOB | ΔfOBUE | ΔfOOB
50MHz | 70MHz | 100MHz | 80-100MHz
ΔfOBUE | ΔfOOB
100MHz | 100MHz

## Slide 5: Out of band blocking – 6.425-7.125GHz
3 options:
  Option 1:
    (TS 38.104)
  Option 2:
  Option 3:
    (n96)
Centre Frequency of Interfering Signal [MHz] | Interfering Signal
(FUL_low - 500) to (FUL_low -ΔfOOB) (FUL_high +ΔfOOB) to (FUL_high +500) | -35 dBm CW
1 to (FUL_low -500) (FUL_high +500) to 12750 | -15 dBm CW
Centre Frequency of Interfering Signal [MHz] | Interfering Signal
1 to (FUL_low -200) (FUL_high +200) to 12750 | -15 dBm CW
Centre Frequency of Interfering Signal [MHz] | Interfering Signal
1 to (FUL_low -ΔfOOB) (FUL_high +ΔfOOB) to 12750 | -15 dBm CW

## Slide 6: Out of band blocking –10.0-10.5GHz
2 options:
  Option 1:
    (TS 38.104)
  Option 2:
Centre Frequency of Interfering Signal [MHz] | Interfering Signal
1 to (FUL_low -200) (FUL_high +200) to 12750 | -15 dBm CW
Centre Frequency of Interfering Signal [MHz] | Interfering Signal
1 to (FUL_low -ΔfOOB) (FUL_high +ΔfOOB) to 12750 | -15 dBm CW

## Slide 7: BS antenna type for indoor
BS antenna type for indoor, 2 options:
  Option 1: AAS BS only
  Option 2: AAS BS and BS with omni antenna.
If no agreement, a possible compromise could be:
  ITU-R LS Reply: provide parameters for AAS BS only (any issue?)
  Capture in the TR that it’s not precluded to have BS with omni antenna for indoor.

## Slide 8: UE SEM
Agreement (to take into account new UE ACLR):
  Relax at the FOOB edge ± 0-1 by 3dB, from -13dBm/1% BW to -10dBm/1% BW (blue).
Should that relaxation be extended to the all OOB frequency range? (yellow)
ΔfOOB (MHz) | 5 MHz | 10 MHz | …
± 0-1 | -10 | -10 | …
± 1-5 | -10 | -10 | 
± 5-6 | -13 | -13 | 
± 6-10 | -25 |  | 
… |  |  | 

## Slide 9: BS ACS requirement (if time allows)
Agreed values:
  6.425-7.125GHz: 42dB
  10.0-10.5GHz: 40dB
To be agreed:
  Interferer type.
  Interferer power level.