## Slide 1: Way Forward on NR TxD & Power Class
vivo
3GPP TSG-RAN WG4 Meeting # 98-e
Electronic Meeting, 25 Jan - 5 Feb., 2021
R4-210xxxx

## Slide 2: EVM for Transparent TxD
Proposals:
  Option 1: As in agreed WF R4-2008465
  Option 2: As has been provided in R4-2016288:
    Option 2a.
      where
    Option 2b.
      Recommended WF:
  [Option 1]

## Slide 3: UE Behavior under Conformance Testing
  Background: Motivation is to guide how to test requirements that require power changes such as relative power control.
  Proposals:
  Option 1a: UE will keep the tx diversity status unchanged in conformance testing.
  Option 1b: Test mode signalling is implemented to instruct UE to keep TX div status unchanged
  Option 2a: TE will detect and sum for every power step and change in condition from declared connector, with no precondition
  Option 2b: TE will detect and sum for every power step and change in condition from declared connector, based on pre-condition that a repeatability of TxD activation/deactivation timing in a UE is maintained can be fulfilled.

## Slide 4: Power Splitting Behavior
Background: Motivation is to guide how to test requirements that require power changes such as relative power control
Question 1: What would be the impact for the requirements and testability with tentative equal power split restriction?
Proposals:
  Option 1: Only allow equal power split between connectors
    Excludes 17+17+20 dBm implementations
    Excludes power control optimizations
  Option 1a: Per instructed as test mode, UE should keep equal power split between connectors in all cases.
  Option 2: Allow any power split between connectors
      Recommended WF:
  [TBD]

## Slide 5: Applicability of Transparent TxD Requirement
The applicability of the newly introduced test procedure (if any) and specific requirement (if any) for transparent TxD UE :
•whether or not applicable to UE implementation without transparent TxD
Proposals
  Option 1: Not applicable
  Option 2: Applicable
Recommended WF
  [Option 1]

## Slide 6: Signaling for Transparent TxD
Whether and how RAN4 introduce signalling for transparent TxD:
  Option 1: Introduce some sort of signaling by UE
    Option 1a. Use ModifiedMPRbehavior bits to signal additional relaxations;
    Option 1b: Introducing a new (capability) signalling for TxD
      Capability reporting for supporting TxD
      [Capability reporting for TxD Enable/Disable status]
    Option 1c: Introducing a new power class (e.g. PC2.5) for TxD
  Option 2: Based on UE vendor declaration.
  Option 3: Using existing signalling to indicate the 2Tx implementation capability.
Recommended WF
  [TBD]

## Slide 7: CDD-related Requirement
For transparent TxD UE, necessity of CDD related requirements, e.g. requirement on TAE+CDD, is need to be further studied:
Proposals
  Option 1: Yes
  Option 2: No.
  Option 2b. No at least for Rel-16
Recommended WF
  [TBD]

## Slide 8: Rel-15 NSA power class
Proposals
  Option 1: The Pcmax for NR is modified according to the declared NR power capability for NSA so that the PHR becomes correct. (Based on R4-2015976 & R4-2015977)
  Option 2: Introduce the Rel-16 defined power class UE capability for Rel-15, and Indication of UE implementation by declaration. (Based on R4-2016479 observation 1)
  Option 3: The Pcmax for NR is modified to use the lower possible power class to decide the lower bound of the configured power. (Based on R4-2016479 observation 3 & R4-2016482, & R4-2102385)
  Option 4: Any other combined/refined revision.
  Option 5: Further revision not needed.
Recommended WF
  TBA

## Slide 9: Impact of Applicability of TxD to Rel-15 NSA power class
Whether applicability of TxD for Rel-15 would impact the previous Issue for NSA.
Proposals
  Option 1:Yes;
  Option 2: No.
Recommended WF
  TBA

## Slide 10: Power class fall back for SA UL-MIMO in Rel-15
Background & motivation:
  Rel-15: “If UE is scheduled for single antenna-port PUSCH transmission by DCI format 0_0 or by DCI format 0_1 for single antenna port codebook based transmission, the requirements in clause 6.2.1 apply.”
  Rel-16: “If UE is scheduled for single antenna-port PUSCH transmission by DCI format 0_0 or by DCI format 0_1 for single antenna port codebook based transmission, the requirements in clause 6.2.1 apply for the power class as indicated by the ue-PowerClass field in capability signalling.”
Proposals
  Option 1: Rel-15 is the same to Rel-16;
  Option 2: Rel-15 can still have different explanation compared to Rel-16.
Recommended WF
  TBA