## Slide 1: WF on transient period
Moderator (CMCC)
3GPP TSG-RAN WG4 #98-e
25 Jan. – 5 Feb. 2021
Electronic meeting
R4-2103151

## Slide 2
Issue 1-1-1 :CR on introduction of shorter Transient Period Capability
Agreements:
  Type 1 transient period placement in 2684 is agreed
  EVM measurement exclusion period needs to be agreed with type 1 placement as a package
Proposals for EVM measurement exclusion period：
WF:
  TBD
Reported transient capability (us) | EVM definition | tpstart (µs) | SCS (option1) | SCS (option2) | SCS (option3)
2 |  | 0.5 | 15KHz or 30kHz | 30kHz | 30kHz
4 |  | 1 | 15kHz | 15kHz | 30kHz
7 |  | 2 | 15kHz | 15kHz | 15kHz
NOTE 1: ,,and are defined in Annex F NOTE 2: is the EVM for a symbol right after a transition; is the EVM for a symbol right before a transition NOTE 3: tpstart denotes the start position of the EVM exclusion window as shown in Annex F.4 |  |  |  |  | 
Parameter | Unit | Average EVM Level
64 QAM | % | [10]
256 QAM | % | [5-8]
Table 1
Table 2

## Slide 3
Issue 1-2-6 EVM budget for symbol where the transient occurs
Proposals
  256QAM: [5%], or [8%],
  64QAM: [15%], or [10%],
WF
  64QAM: [10%]
  256QAM: [5-8%]

## Slide 4
Issue 1-2-2: Whether 20dB power change can represent the maximum power change in the network, if not, whether TE can provide the test condition for the maximum power change
Proposals
  Option 1: 20 dB power step is reasonable for on-on power change.
  Option 2: 55dB Large power change range case cannot be ignored.
WF
  To be decided at this meeting