## Slide 1: Way Forward on Assumptions for PC 1.5 in Bands n77 and n78
Qualcomm Incorporated, Verizon
DRAFT R4-2103227
3GPP TSG-RAN WG4 #98-e
Jan 25th ‒ Feb 5th, 2020
Electronic Meeting

## Slide 2: WF on UE RF assumptions
Smartphone Handheld UE MPR
  TBD
  The same assumptions previously used to derive PC1.5 MPR and therefore the MPR itself are reused for Band n77/n78 for handheld UEs
MPR applicability to TxDiv
  MPR applies to both UL MIMO and TxDiv
FWA MPR
  Continue to discuss whether to reuse the existing MPR requirements or to define new MPR requirements for FWA UEs, and study the impact to the specs if new requirements are needed
  For the next meeting, companies are free to provide assumptions with justification for FWA. It is not precluded that those assumptions are the same or different from previous assumptions for mobile handset as long as they are provided with justification.
Additional emission requirements for n77 and n78
  No additional emission requirements and no new NS for Band n77 and n78 for the purpose of additional emission requirements. This agreement can be revisited if a company discovers a regulatory requirement needing to be reflected.
Additional emission requirements for n77 and n78
  No need for A-MPR has been identified so far