## Slide 1: Way forward on NC UL CA PC2 evaluation assumptions and scenarios
Skyworks Solutions Inc.,…..
R4-2103237
3GPP TSG-RAN WG4 Meeting #98-e
Electronic meeting, 25 Jan. – 5 Feb. 2021

## Slide 2: Background: Architecture options discussed
To achieve PC2 capability the architecture must be able to achieve 26dBm with different allocation in each CC => >23dBm in one CC vs <23dBm in the other CC
To cover all PC2 cases including n77(2A) >200Mhz total Ul BW is needed
PC2 non-contiguous UL CA architecture options |  |  |  |  | 
Arch | description | Coherence with PC3 | constrains | MPR | prerequisite
#1 | 2x26dBm PA + 2LO with 100MHz BW | Equivalent to baseline can cover n77(2A) | no UL MIMO (or 4 PAs) | Baseline Supports any BW separation class | none
#2 | 1x26dBm PA + 1LO with 200MHz BW | was discussed but not finalized | need in gap exceptions need second PA to support UL MIMO | Can only be optional for bands <3.3GHz and depends on in gap exceptions | applicability of in gap exception in the bands <3.3GHz
#3 | 2x23dBm PA + 1LO with 200MHz BW | Not applicable | need in gap exceptions need second PA to support UL MIMO must use TxDiv or UL MIMO | Can only be optional for bands <3.3GHz and depends on in gap exceptionsneed assessment of additional MPR for TxDiv on top of UL CA | applicability of in gap exception in the bands <3.3GHz single CC TxDiv MPR/signalling

## Slide 3: WF on architecture: based on GTW agreements
2x26dBm PA + 2LO with 100MHz BW is the baseline for MPR/A-MPR evaluation and as it does not require in gap exceptions and can cover >200MHz separation classes
Other architecture options are limited to <3.3GHz bands (<200MHz BW) and need to be allowed for in gap exceptions.
  They cannot be used as baseline but they can be further discussed
  A clear band example where exceptions are acceptable needs to be used. From PC3 discussions there was some level of consensus that it can only be for TDD band and if the affected channel belongs to the same operator. Following architectures would be applicable:
  1x26dBm PA + 1LO with 200MHz BW
  2x23dBm PA + 1LO with 200MHz BW

## Slide 4: WF: MPR/AMPR evaluation assumptions
PA calibration for 20MHz QPSK DFT-s-OFDM 100RB0 waveform based on 4dB post PA losses and 1dB MPR.
  26dBm/antenna: 29dBm at 31dB ACLR
  23dBm/antenna: 26dBm at 30dB ACLR
Equal PSD and Equal back-off power split
Measurements is used where two PA are coupled on the output recreating the 10dB antenna isolation assumption
Emission requirements (ACLR/SEM/spurious emissions) are checked by summing the power of the two transmit paths
Since simulation are not available, at least for worst case corners are evaluated for different modulation order
Like for PC3 same MPR/A-MPR values for DFT-s and CP-OFDM are targeted

## Slide 5: WF: MPR/AMPR evaluation scenarios
Since same MPR is targeted CP-OFDM is used in each carrier but both CP-OFDM and DFT-s-OFDM can be evaluated
Worst case back-off IMD3 at -13dBm/MHz and -30dBm/MHz for 1RB+1RB at 15kHz and 30kHz SCS for MPR with 31dBc ACLR and
Worst case back-off IMD3 at -13dBm/MHz and -25dBm/MHz for 1RB+1RB at 15kHz and 30kHz SCS for NS04 A-MPR
1RB+1RB separation of ~100, 200, 600MHz to cover variation across BW separation classes
Other allocations sizes are recommended but the MPR vs allocation BW behavior from PC3 MPR can also be reused
20MHz channel 15kHz SCS and 40MHz channel 15kHz SCS with a gap of 20MHz (100MHz class and in gap ACLR)
40MHz channel 15kHz SCS and 40MHz channel 15kHz SCS with a gap of 120MHz (200MHz class)
100MHz channel 30kHz SCS and 100MHz channel 30kHz SCS with a gap of 400MHz (600MHz class for n77(2A))

## Slide 6: WF: proposals for MPR
Like for PC3 MPRIM3 to meet -30dBm/MHz and MPRIM3 to meet -13dBm/MHz curves are provided using the same BW definitions than PC3. values are multiples of 0.5dB
Consistency with PC3 should be checked
MPRIM3 to meet -30dBm/MHz
MPR in this clause is for intra-band non-contiguous CA power class 3 for UEs indicating IE dualPA-Architecture supported. The allowed maximum output power reduction is defined as:
MPR=MAWhere MA is defined as follows
MA = TBD; 0 ≤ B < 1.08
TBD; 1.08 ≤ B < 2.16
TBD; 2.16 ≤ B < 3.24
    TBD; 3.24 ≤ B < 5.04
TBD; 5.04≤ B < 10.08
TBD; 10.08 ≤ B < 16.38
TBD; 16.38 ≤ B < 21.78
TBD; 21.78 ≤ B
MPRIM3 to meet -13dBm/MHz
MPR in this clause is for intra-band non-contiguous CA power class 3 for UEs indicating IE dualPA-Architecture supported. The allowed maximum output power reduction is defined as:
MPR=MA
Where MA is defined as follows
MA = TBD; 0 ≤ B < 0.54
TBD; 0.54 ≤ B < 1.08
TBD; 1.08 ≤ B < 2.16
TBD; 2.16 ≤ B < 3.24
TBD; 3.24 ≤ B < 5.4
TBD; 5.4 ≤ B

## Slide 7: WF: proposals for NS04 A-MPR for n41(2A)
Like for PC3 A-MPRIM3 to meet -25dBm/MHz curve is provided using the same BW definitions than PC3. values are multiples of 0.5dB
Consistency with -30dBm/MHz IM3 should be checked
AMPRIM3 to meet -25dBm/MHz
AMPR in this clause is for intra-band non-contiguous CA_n41(2A) power class 3 for UEs indicating IE dualPA-Architecture supported. The allowed maximum output power reduction is defined as:
AMPRIM3=MAWhere MA is defined as follows
MA = TBD; 0 ≤ B < 1.08
TBD; 1.08 ≤ B < 2.16
TBD; 2.16 ≤ B < 3.24
TBD; 3.24 ≤ B < 5.04
TBD; 5.04 ≤ B < 10.08
TBD; 10.08 ≤ B < 16.38
TBD; 16.38 ≤ B < 21.78
TBD; 21.78 ≤ B

## Slide 8: References of related CRs introducing such cases:
[1] R4-2100289 MPR/A-MPR initial simulation assumptions for PC2 NR intra-band NC CA, LG Electronics France, LG Uplus, R4#98e
[2] R4-2100572 PC2 non-contiguous UL CA UE Architecture and MPR/A-MPR evaluation, Skyworks Solutions Inc. , R4#98e
[3] R4-2102185 Discussion on PC2 intra-band non-contiguous NR CA, ZTE Corporation, R4#98e