## Slide 1: WF on FDM operation for SL and Uu in licensed band
Xiaomi
3GPP TSG-RAN WG4#98-e Meeting draft R4-2103245
Electronic Meeting, Jan. 25-Feb. 5, 2021

## Slide 2: Background
During the RAN4#98-e meeting, the following topic has been discussed for FDM operation of partial licensed band used for SL as:
Whether to introduce FDM operation of UL and SL
Frequency separation
SL coverage with power control
RF architecture
Relationship with intra-band CA

## Slide 3: Whether to introduce FDM operation of UL and SL
  1, It has been agreed to introduce FDM operation of UL and SL.
  2, FDM operation with shared or different carriers ?
    Option 1: RAN should allow FDM operation with one single or shared carrier for SL and Uu in licensed band [Qualcomm] We think the above change makes the sentence clearer. If the word “single” should be in the sentence, then can you explain what is the difference between single and shared carrier.
    Option 2: RAN should allow FDM operation with different carriers for SL and Uu in licensed band.
  Recommended WF
    Both option 1 and option 2 in TDD band can be considered.
    Option 2 in FDD band can be considered [Qualcomm] Why is option 1 not included?
  3, FDM operation in TDD band or FDD band ?
    Option 1: TDD band
    Option 2: FDD band
  Recommended WF
    Both FDD on TDD band can be considered.

## Slide 4: Frequency Separation in adjacent channel
Candidate options:
  Option 1: RAN4 study frequency separation in case of FDM operation between SL and Uu
  Option 1a:RAN4 study frequency separation in FDM operation between SL and Uu to allow simultaneous UL Tx and SL Rx.
  Option 2: No frequency separation needs to be studied.
  Option 2a: RAN4 can allow FDM operation in TDD licensed band with restriction of SL Tx/Rx only allowed in UL configuration when NR Uu has not transmitted signalling.
Recommended WF
  Further discuss whether frequency separation study is needed.
[Qualcomm] Could you please define what is meant by adjacent channel in the WF

## Slide 5: Frequency Separation in non-adjacent channel
Candidate options:
  Option 1: RAN4 study frequency separation in case of FDM operation between SL and Uu
  Option 1a:RAN4 study frequency separation in FDM operation between SL and Uu to allow simultaneous UL Tx and SL Rx.
  Option 2: No frequency separation needs to be studied.
  Option 2a: RAN4 can allow FDM operation in TDD licensed band with restriction of SL Tx/Rx only allowed in UL configuration when NR Uu has not transmitted signalling.
Recommended WF
  Further discuss whether frequency separation study is needed.
[Qualcomm] could you please define what is meant by non-adjacent channel in the WF

## Slide 6: Power issue
The following power issue has been raised for FDM operation
  Coverage of SL due to power control may be seriously impacted by FDM operation [Qualcomm] Could you clarify the reason SL coverage is impacted?
  The power of the Uu TX and SL TX may have to be reduced to prevent cross-coupling.
Recommended WF:
  To further investigate the above power issue for FDM operation.

## Slide 7: RF Architecture
Candidate Option
  Option 1: Separate RF architecture (Please clarify whether is this separate RF chains including PAs or separate RF Ant)
  Option 2: Up to UE implementation
Recommended WF
  Separate RF architecture is agreed as one of the RF architecture. Further discuss the feasibility of shared RF architecture for FDM operation.
  [Qualcomm] We cannot agree with “Separate RF architecture is agreed as one of the RF architecture. Further discuss the feasibility of shared RF architecture for FDM operation.” We prefer Option 2

## Slide 8: Relationship to intra-band CA
Whether the RF architecture and core requirements of 2UL intra-band CA could apply to V2X intra-band con-current operation in band n79
Proposals
  Option 1: YES
  Option 2: NO
Recommended WF
  Option 2. Both the RF architecture and core requirements need further study comparing to intra-band CA.

## Slide 9: Reference
[1] R4-2102991, Email discussion summary for [98e][143] NRSL_enh_Part_2, Moderator (CATT), RAN4#98e
[2] R4-2100415, Discussion on operating scenarios for partial used SL operation, CATT, RAN4#98e
[3] R4-2101875, On operating scenarios for partially used SL operation, Xiaomi, RAN4#98e
[4] R4-2102343, Operating scenarios for partially used SL operation, Ericsson, RAN4#98e
[5] R4-2100283, Consideration on partial usage operation with PC5 and Uu in a licensed band, LG Electronics France, RAN4#98e