## Slide 1: WF on simulation assumptions for system performance evaluation Moderator(China Unicom)
3GPP TSG-RAN WG4 Meeting #98-e R4-21xxxxx
Electronic Meeting, Jan. 25– Feb. 05, 2021

## Slide 2: Dynamic system level simulation
Configuration parameters | Values
Scenario | Urban macro
ISD | 500 m
Duplexing | FDD
Carrier frequency | 1.8 GHz, 2.1GHz
Modulation | Up to 64QAM, 256QAM is optional
Numerology | 15 kHz
Simulation bandwidth | 40 MHz
Transmission scheme | SU-MIMO
Codebook | For 2Tx, codebook [1 1]T is used for transmit diversity
SU dimension | 1 layer
Antenna configuration at TRxP | 4Rx, (M,N,P,Mg, Ng) = (1,2,2,1,1; 1,2); 4Rx, (M, N, P, Mg, Ng) = (1, 4, 2, 1, 2) 32Rx, (M,N,P,Mg, Ng) = (8,8,2,1,1; 2,8)
Antenna configuration at UE | 1Tx, (M,N,P,Mg, Ng) = (1,1,1,1,1; 1,1), 2Tx, (M,N,P,Mg, Ng) = (1,1,2,1,1; 1,1)
UE maximal transmit power | For 1Tx, 23 dBm for each TXRU For 1Tx, 26 dBm for each TXRU (High power UE) For 2Tx, 23 dBm for each TXRU (High power UE)
Scheduling | PF
Receiver | MMSE-IRC
Channel estimation | Ideal
Power control parameter | P0=[-60~-76], alpha = [0.6, 0.8]
TRxP number per site | 3
TRxP number | 21
Channel model | UMa following TR 38.901
Electronic tilt | 102°
Traffic model | FTP3, packet size: 100k / 10k Byte, arrival rate: [1 packet / s, 1 packet/200ms]
Uplink duty cycle | 50%, 100%

## Slide 3: Monte Carlo simulation
Environment | ISD (KM) | ISD (miles)
Urban | .75 | .47
Suburban | 2.8 | 1.74
Rural | 6 | 3.73
Rural | 8 | 5
 | Base Station | UE
Carrier frequency | 2GHz | 
Channel bandwidth | 40MHz, 20 MHz, 10 MHz | 
UL duty cycle | 100% | 
Active UE number in UL | 3 | 
Inter-site distance | Use Table 2 | 
Cell layout | Wrap-around 19 tri-sector cells | 
Frequency reuse | 1x3x1 | 
Lognormal fading | 10 dB | 
Shadowing correlation | Between cells: 0.5, between sites: 1.0 | 
MCL (including antenna gain) | 70 dB (urban and suburban areas) 80 dB (rural area) | 
Antenna gain and horizontal antenna pattern | 17 dBi, = 65 degrees, Am = 20 dB | Omni-directional antenna with -3.5 dBi.
Noise figure | 5 dB | 9 dB
Transmit power | 46 dBm | 23 dBm
Antenna height | 45 m | 1.5 m
 | Base Station | HPUE
Carrier frequency | 2GHz | 
Channel bandwidth | 40MHz, 20 MHz, 10 MHz | 
UL duty cycle | [50%] | 
Active UE number in UL | 3 | 
HPUE ratio | [100%] | 
Inter-site distance | Use Table 2 | 
Cell layout | Wrap-around 19 tri-sector cells | 
Frequency reuse | 1x3x1 | 
Lognormal fading | 10 dB | 
Shadowing correlation | Between cells: 0.5, between sites: 1.0 | 
MCL (including antenna gain) | 70 dB (urban and suburban areas) 80 dB (rural area) | 
Antenna gain and horizontal antenna pattern | 17 dBi, = 65 degrees, Am = 20 dB | Omni-directional antenna with -3.5 dBi.
Noise figure | 5 dB | 9 dB
Transmit power | 46 dBm | 26 dBm
Antenna height | 45 m | 1.5 m
(a) With 23 dBm UE
(b) With 26 dBm UE

## Slide 4: Way Forward
Companies are encouraged to bring simulation results based on assumptions from previous pages.