## Slide 1: WF on Rel-17 NR HST FR2 enhancements, RRM requirements
3GPP TSG-RAN WG4 Meeting #98-e
Electronic Meeting, Jan. 25th – Feb. 5th, 2021
Agenda: 11.7.4
(DRAFT)R4-2103679
Document for: Approval
Nokia, Nokia Shanghai Bell,…

## Slide 2: Background
The Rel-17 NR HST FR2 Enhancements WI is described in RP-202118.
The Work plan of the WI, including RRM core and perfromance part can be found in R4-2014846.
R4-2017828 WF was approved previously on NR support for HST in FR2, RAN4#97-e.
Corresponding Email summary in RAN4#98-e:
  R4-2103475 Email discussion summary for [98e][236] NR_HST_FR2_enh_RRM, RAN4#98-e, first round.
  R4-2103717 Email discussion summary for [98e][236] NR_HST_FR2_enh_RRM, RAN4#98-e, second round

## Slide 3: RRM and Deployment Scenarios: General
Start with high-level discussion of RRM requirements, including the relevance of Rel-15/16 requirements to HSR FR2 and such topics as RRC IDLE mode, DRX, inter-frequency and inter-RAT measurements, etc. More detailed discussion shall take into account the conclusions from the deployment scenarios.
New deployments shall be discussed in the corresponding agenda item.

## Slide 4: Applicability of Rel-15/16 requirements to Rel-17 HST FR2
RRM Req. Category | Sub-Category | Whether or not applicable to FR2 HST
Idle/inactive state mobility | Cell selection/re-selection, measurement | FFS
Connected state mobility | Handover | FFS
 | Connection Mobility Control - RRC re-establishment | FFS
 | Connection Mobility Control - Random Access | No impact identified
 | Connection Mobility Control - RRC Release with Redirection | FFS
Timing | Autonomous timing adjustment | FFS
 | TX timing, timer, TA, Cell Phase Sync accuracy, MRTD/MTTD, deriveSSB-IndexFromCell tolerance | FFS
Signalling | RLM | FFS
 | Interruption | No impact identified
 | SCell Activation and Deactivation Delay | Not applicable to FR2 HST
 | UE UL carrier RRC reconfiguration delay | Not applicable to FR2 HST
 | Link Recovery | FFS
 | Active BWP switch delay | No impact identified
 | Active TCI state switching delay | FFS
 | PSCell Change | Not applicable to FR2 HST
 | Uplink spatial relation switch delay | FFS
 | UE-specific CBW change | No impact identified
 | Pathloss reference signal switching delay | No impact identified
Measurement Procedure | General measurement requirement | No impact identified
 | NR intra-frequency measurements | FFS
 | NR inter-frequency measurements | FFS
 | Inter-RAT measurement | FFS
 | L1-RSRP/L1-SINR Measurement | FFS
 | CSI-RS based L3 measurements | FFS Not applicable to FR2 HST
 | NR measurements with autonomous gaps | Not applicable to FR2 HST
Requirements’ classification categories:
  Not applicable to FR2 HST: the requirement is not applicable to Rel-17 FR2 HST UE
  No impact identified: no change on Rel-15/16 requirement is needed, and the same requirement applies to Rel-17 FR2 HST UE.
  FFS: need to discuss whether or not the requirement is applicable to Rel-17 FR2 HST UE and/or whether or not Rel-15/16 requirement needs to be changed/enhanced
Table (infromative): Applicaibility of Rel-15/16 requirements

## Slide 5: The scope of HST FR2 requirements
IDLE/INACTIVE mode requirements:
  Option 1: Reuse existing Rel-16 requirements
  Option 2: Study and define enhancements to support FR2 HST conditions
RRC CONNECTED mode requirements for DRX:
  Option 1: Do not define enhanced requirements for the case DRX is configured
    Option 1A: Legacy NR R16 requirements (non-HST) will apply for the case DRX is configured
    Option 1B: No RRM requirements will be defined for the case DRX is configured
  Option 2: Define requirements for the short DRX configurations (e.g. up to 80ms).
Requirements on Inter-frequency measurements:
  Option 1: Inter-frequency measurements are required for NR single carrier scenario in FR2.
  Option 2: Other options are not precluded
  Further input from operators is requiested
Inter-RAT measurements:
  Option 1: Inter-RAT measurements are required for NR SA single carrier scenario in FR2
  Option 2: Other options are not precluded
  Futher input from operators is requested

## Slide 6: The scope of HST FR2 requirements: Other
UE autonomous timing adjustment step:
  Option 1: Autonomous timing adjustment step Tq for FR2 in high speed scenario is 4.5Ts.
  Option2: Other options are not precluded
FFS: whether to consider location assisted information

## Slide 7: HST FR2 signalling: Deployment Flags
HST FR2 network deployment flag:
  Option 1: Add flag to enable the UE to differentiate between the HST and non-HST scenarios
  Option 2: HST FR2 CPE is a special dedicated device, flag is not needed
HST FR2 bidirectional mode flag:
  Option 1: Network informs UE whether it operates in bidirectional mode in high speed in FR2 by corresponding flag.
  Option2: Other options are not precluded

## Slide 8: HST FR2 signalling: UE Capability Fields
On the UE support of HST FR2:
  Option 1: The UE should inform network that it supports HST FR2/it is the FR2 HST CPE
  Option 2: Only roof-mounted CPE is considered that should always have a capability to work in HST FR2 scenario
UE capability field on the support of bidirectional operation:
  Option 1: Network informs UE whether it operates in bidirectional mode in high speed in FR2 by corresponding flag.
  Option 2: Other options are not precluded

## Slide 9: Number of RX Beams
Number of Rx beams:
  FFS: if reducing the number of RX beams used in IDLE and/or CONNECTED mode is needed
  FFS: the perfromance impact and UE gains in relation to the deployment scenarios

## Slide 10: IDLE/INACTIVITY Mode RRM requirements
The following issues shall be revisited after the agreement is reached on the applicability of existing Rel-15/16 IDLE/INACTIVE mode requirements and FR2 HST deployment scenarios are fixed:
  Whether enhacements are needed in measurement requirements of intra-frequency NR cells
  Whether enhacements are needed in cell reselection requirements
  Whether enhacements are needed in inter-frequency measurement (if found to be appblicable)
  Whether enhacements are needed in Inter-RAT measurements (if found to be applicable)

## Slide 11: Connected mode RRM requirements
Coninue discussing the following issues after the deployment sceanrios are fixed:
  Whether cell detection and identification enhancements are needed
  Whether the existing non-HST NR measurement requirements for FR2 are sufficient
  Whether L1-RSRP measurements enhancements are needed
  Whether it can be confirmed that the current FR2 NR HO requirements are also applicable for FR2 HST
  Whether geometry-added HO shall be considred
  Whether enhancements to the current Radio Link Monitoring requirements are needed
  Whether enhacements are needed in inter-frequency measurement (if found to be appblicable)
  Whether enhacements are needed in Inter-RAT measurements (if found to be applicable)

## Slide 12: Beam management requirements
Coninue discussing the following issues after the deployment sceanrios are fixed:
  Whether enhancements to the beam management requirements are needed
  Whether enhancements to the beam sweeping requirements are needed
  Whether it is necessary to consider the mitigation of transition/timing advance issue when beam changes in HST FR2 unidirectional deployment
  Target TCI state:
    Option 1: It is recommended that only known target TCI is considered in high speed FR2
    Option 2: other options are not precluded

## Slide 13: Contributions List in RAN4#98-e
T-doc No. | Title | Company
R4-2100220 | Discussion on RRM requirement for high speed train scenario in FR2 | Apple
R4-2100476 | Discussion on NR FR2 HST | CATT
R4-2100477 | Initial performance evaluation for cell identification in NR FR2 HST scenario | CATT
R4-2100866 | General discussion on RRM requirements for FR2 HST | CMCC
R4-2101142 | Overview of RRM requirements for NR high speed train scenario in FR2 | Ericsson
R4-2101708 | Preliminary discussion on NR support for high speed train scenario in FR2 | Huawei, HiSilicon
R4-2101268 | RRM requirements for NR HST in FR2 | Intel Corporation
R4-2101138 | On expected RRM impact for HST in FR2 | Nokia
R4-2100632 | FR2 HST RRM discussion | Qualcomm, Inc.
R4-2100917 | Discussion on RRM requirement for FR2 HST | Samsung