## Slide 1: [draft] WF on NR UE Power Saving Enhancements (All agreements in RAN4#98e in email thread #238)
MediaTek, vivo
3GPP TSG-RAN WG4 Meeting #98e R4-2103670
Electronic Meeting, Jan. 25-Feb. 5, 2021
Agenda Items: 11.9

## Slide 2: Scenarios for power saving
Issue 2-2-1: Confirmation on beneficial Scenarios, from UE power saving gain perspective
RAN4 to identify the scenarios that power saving gain can be observed.
Base on simulation results, it can be observed that
  With FTP model is considered with DRX of 40 ms, if L1 measurement intervals for RRM are also extended K times
    For FR1 SSB-based RLM/BFD relaxation, at least 3 sources show that the power saving gain is 8.7% to 16.4% for K=2, 13% to 20.5% for K=4, and 15.1% to 25.8% for K=8.
    For FR2 CSI-RS based RLM/BFD relaxation, one source shows that the power saving gain is 15.6% for K=2, 21.8% for K=4.

## Slide 3: Scenarios for power saving
Issue 2-2-2: Feasible Scenarios for Power Saving, from system impact perspective
Base on simulation results, it can be observed that
  Regarding delta SINR, for FR1 SSB-based RLM OOS relaxation,
    with mobility of 3 km/h, at least 2 sources show that the delta SINR is 1.3 dB to 2dB for K=2 , 2.6 dB for K=4, less than 8dB for K=8.
    with mobility of 30 km/h, at least 2 sources show that the delta SINR is 2.8 dB to 4.6dB for K=2 , 5.1 to 6.2 dB for K=4, 7.4 to 8.8 dB for K=8.
  Regarding increased RLF latency, for FR1 SSB-based RLM OOS relaxation,
    with mobility of 3 km/h, at least 2 sources show that the increased latency is less than 40ms for K=2, less than 120ms for K=4, and less than 280ms for K=8 with 95% probability.
      The increase is less than 2.5% for K=2, less than 7.5% when K=4 and less than 17.5% when K=8, as T310 = 1000ms and N310 = 1.
    with mobility of 30 km/h, at least 2 sources show that the increased latency is less than 40ms for K=2, less than 120ms for K=4, and less than 280ms for K=8 with 95% probability.
      The increase is less than 2.5% for K=2, less than 7.5% when K=4 and less than 17.5% when K=8, as T310 = 1000ms and N310 = 1.
The following scenarios are feasible for power saving
  SSB-based and CSI-RS based RLM/BFD measurement relaxation in FR1 for low mobility and high/medium SINR UE.
  FFS CSI-RS based RLM/BFD measurement relaxation in FR2 for low mobility and high/medium SINR UE
  FFS SSB-based RLM/BFD measurement relaxation in FR2 for stationary and high/medium SINR UE

## Slide 4: Scenarios for power saving
Issue 2-2-3: DRX cycle
The applicability of DRX cycles for RLM/BFD relaxation should be studied and decided based on the ongoing simulation study.
  FFS DRX cycle length <= 80 ms

## Slide 5
Issue 2-3-1: Criteria which the UE is allowed to relax the RLM/BM requirements
At least take UE mobility into account as the relaxation criteria.
  FFS whether to also take serving cell’s quality into account
Issue 2-3-2: How to consider UE mobility as relaxation criteria
FFS the following options
  Option 1: R16 low-mobility criterion should not be directly reused in R17 SINR-based criterion for RLM/BFD relaxation.
  Option 2: R16 RRM relaxation criterion can be used as baseline for RLM/BFD relaxation.
  Option 3: “low mobility criteria” should consider both UE velocity and the channel quality variation.
  Option 4: Consider time associated with a given condition when determining UE mobility state.
  Option 5: Low mobility scenario under which the UE is allowed to apply the RLM/BM requirements is determined and configured to UE by the network

## Slide 6
Issue 2-3-3: How to consider serving cell’s quality as relaxation criteria
Take serving cell’s quality into account for the relaxation criteria
  FFS how to consider serving cell’s quality. E.g. Based on SINR or BLER.
  FFS how to address different UE implantation issues.
Issue 2-3-4: Network or UE to determine if the relaxation criteria is fulfilled
Network to enable and disable this feature.
  FFS Should the relaxation criteria be predefined or configurable?
  FFS Should it be network or UE to determine the relaxation criteria is fulfilled or not?

## Slide 7
Issue 2-4-1: Scheme of RLM/BFD measurements relaxation
Use of a scaling factor to extend the RLM/BFD evaluation period.
Issue 2-4-2: relaxation factor determination
Scaling factor defining the relaxed RLM/BFD evaluation period is defined based on
  DRX cycle and RLM-RS periodicity
    FFS based on max(TDRX, TSSB)
    FFS other factors are not precluded, e.g. estimated SINR level, UE mobility, N factor, P factor, RS type, FR1 or FR2.
Issue 2-4-3: relaxation factor: different relaxation factor in FR1 and FR2
RAN4 further to discuss whether different relaxation factors can be allowed for FR1 and FR2 based on simulation study.

## Slide 8
Issue 2-5-1: Reverting to the normal RLM operation
The UE while performing relaxed RLM upon detecting certain number of out-of-sync indications or upon triggering T310 or upon observed link quality degradation reverts to the normal RLM operation (i.e. without relaxation).
FFS the following options
  Option 1a: revert when the relaxation criterion is not met
  Option 1b: revert when N310 starts to count, i.e. 1 out-of-sync indication.
  Option 1c: revert when T310 is running, i.e. N310 out-of-sync indication.
  Option 1d: revert when observed link quality degradation.

## Slide 9
Issue 2-5-2: Reverting to the normal BM operation
Option 1: Reverting to the normal BFD operation upon detect 1 beam failure instance indication.
Option 2: The UE while performing relaxed BM upon beam failure detection reverts to the normal BM operation (i.e. without relaxation).
Option 3: There might be no benefit to configure conditions for UE reverting to normal BFD.
Other options are not precluded.

## Slide 10
Issue 2-5-3: Relaxation of BM when not all serving cells in intra-band CA/DC meets relaxation criteria
The following options have been discussed in this meeting
  Option 1: For intra-band CA case, the UE should relax only on serving cells where the relaxed criteria is fulfilled.
  Option 2: For intra-band CA case, RAN4 to define the same measurement relaxation rules for the serving cells.
  Other options are not precluded.
Issue 2-5-4: Relaxation on PDCCH monitoring
Not to further discuss whether PDCCH monitoring should be relaxed until RAN1 design is stable.