## Slide 1: Way forward on UE/BS demodulation on NR 47GHz band
Ericsson
3GPP TSG-RAN WG4 Meeting #98-e
Electronic meeting, 25 January – 5 February 2021
Agenda item: 9.25.4.2, 9.25.4.3
Document for: Approval
R4-2103875

## Slide 2: Agreements for UE demodulation requirements on NR 47GHz band
Whether if the existing UE performance requirements applicable for 47GHz band or not
  Interested companies are encouraged to provide the evaluation results whether the existing UE demodulation requirements are applicable for 47GHz band or not
    For evaluation, use MCS 18 Rank 1 (Test 1-3 in TS38.101-4 Table 7.2.2.2.1-3) and MCS 17 Rank 2 (Test 2-6 in Table 7.2.2.2.1-4) for n262, as an example.
      Other scenarios are not precluded
    Phase noise (PN) model is up to UE implementation
Set Noc level for n262 in TS38.101-4 Table 4.5.3.2-1 based on REFSENS defined in RF session

## Slide 3: Agreements for BS demodulation requirements on NR 47GHz band
Whether if the existing BS performance requirements applicable for 47GHz band or not
  Option 1: Keep the existing RAN4 assumption that BS requirements are applicable up to 52.6GHz
  Option 2: Need further study whether the existing BS performance requirements are applicable for 47GHz band or not
Requirements applicability: The baseline assumption is the existing BS requirements are applicable up to 52.6GHz
Companies can bring more analysis to further check whether above assumption is valid or not
Test feasibility: Companies are encouraged to bring more analysis for link-budget issue and absolute power level in receiver side to ensure 47GHz performance requirements testable
Update of BS demodulation requirements in TS38.141-2
  No updates on ΔOTAREFSENS, EISREFSENS_50M and ΔFR2_REFSENS, are expected for n262
  MU and TT may need to be updated according to the conclusion in RF session
Notes: Huawei: If everyone have confidence, the existing performance requirements valid for up to 52.6GHz. Where is in specifications?
Did RAN4 already have such agreements? We also realize it’s also impractical to evaluate the PN model into simulation since it’s implementation basis.
Nokia: To Huawei, the BS requirements specified with any limitation for upper ranges, but in UE side we have limitation. We think the receiver from demodulation aspect is not sensitive to the frequency and can be applied for above 52.6GHz.
PN model already included in simulation, the PN model choosing up to companies.
Intel: We are also not sure whether we have enough margin to support up to 52.6GHz. We can address by further simulation if needed.
Samsung: For Channel model, no issue. For PN model, we think the impairment margin with 52.6GHz, it should be enough.
Nokia: We think it’s first meeting, we are willing to see more analysis.
E///: PN has impact on very high SNR, but for test cases SNR is limited should be OK, PN model should up to BS implementation.
Agreements:
The baseline assumption: The existing BS requirements are applicable up to 52.6GHz
Companies can bring more analysis to further check whether above assumption valid or not
Companies are encouraged to bring more analysis to link-budget issue to ensure 47GHz performance requirements testable