## Slide 1: WF for TDD repeater
CMCC
3GPP TSG-RAN WG4 Meeting # 98-e R4-2103881
Electronic Meeting, Jan. 25-Feb. 5, 2021

## Slide 2: Background on NR repeater
RAN#90e approved a new “New WID on NR Repeaters” with RAN4 as the responsible WG.
The objective of the WID is listed as below:
Normative work phase objective [RAN4]
Specify RF and EMC requirements for NR repeaters
Consider FR1 (FDD and TDD) and FR2 (TDD) bands
For the above objective, the leveraging of RF specifications for LTE repeater and IAB should be sought.
It is assumed that the repeater does not perform adaptive beamforming towards the UE.
It is assumed that the TDD repeater meets both BS and UE emission requirements (or the more stringent absolute level in dBm) in all slots.
The following constraint may be considered for TDD repeaters, as needed, to contain the workload associated with this project:
TX EIRP/TRP/power of Repeater not exceeding any UE power class defined in the band
Note: FR1 FDD repeaters testing is assumed to be conducted. This assumption can be revisited in RAN#91.

## Slide 3: WF on synchronization
RAN4 specify RF requirements based on the assumptions of TDD repeater has to synchronize to the gNB for TDD DL-UL pattern
FFS whether dedicated requirements need to be specified for the sync with gNB
FFS the exact methods to achieve sync with gNB in repeater side, implementation based on solution not excluded;
RAN4 should respect the WID scope, to focus the discussion which aligned with the WID
Note: The definition of “ precise of synchronization between TDD repeater and the gNB for TDD DL-UL pattern” need to be further clarified in RAN4

## Slide 4: WF on knowledge of UL/DL split
  RAN4 specify RF requirements based on the assumptions of repeater should be aware of the UL/DL split
    FFS on how repeater know DL/UL split
      Option 1: via the cell broadcast information
      Option 2: via proprietary application layer signaling
      Option 3: via detecting over the air
      Option 4: via pre-configuration
    FFS on whether dedicated requirements is needed to make sure repeater could decode UL/DL configuration.

## Slide 5: WF on dynamic TDD
  FFS on whether to support dynamic TDD
    Companies are encouraged to provide more arguments/proposals on the feasibility, need and how to support dynamic TDD for FR1 and FR2.
    Signaling and procedures that would involve other groups is out of the scope of the WI
    Impacts of dynamic TDD operation by repeaters on co-existence to other networks would need to be studied/taken into account

## Slide 6: WF on group delay
  Clarification on the definition of group delay requirements
    Group delay is the potential delay of repeater, including the propagation delay and possible processing delay
  FFS on whether group delay requirement is needed, following aspects should be considered
    If the GP is not large enough to accommodate the additional delays
    To avoid L1-changes, for example CP design changes to avoid UL cross-symbol interference between the repeater signal and UE signal that is not amplified by repeater

## Slide 7: WF on UL timing knowledge
    FFS whether UL timing related requirements are defined for TDD repeater.
    The following reasons were raised in RAN4#98e to be aware of the UL timing knowledge
      Option 1: to help repeater know when to switch from DL to UL to receive the signal from UE
      Option 2: to help repeater determines when to forward the signal to gNB
      Option 3: to avoid potential interference from misaligned UL timing
    How to be aware of the UL timing knowledge
      Option 1: Repeater can derive the UL timing autonomously
      Option 2: some mechanism needs to be standardized within the WI scope (i.e. RAN4)