## Slide 1
WF on single link tests for NR V2X demodulation performance
3GPP TSG-RAN WG4 Meeting #98-e Electronic Meeting, 25 Jan. – 5 Feb., 2021
Agenda Item: 7.3.6.1
R4-2103810
LG Electronics

## Slide 2: Information for font color
Green part
  Agreements in 1st round and GTW session
Blue part
  Option with majority companies’ view (single company has different view)

## Slide 3: PSSCH demodulation
Additional following test is introduced
  Option 1: 64QAM for 30km/h relative velocity (LG, Qualcomm, MediaTek, CATT)
  Option 2: 16QAM for 260km/h relative velocity and 64QAM for 30km/h relative velocity (Intel, Huawei, CATT)
Test for 256QAM modulation order
  256QAM is not introduced in Rel-16. Considering RAN4 work load and time limitation in Rel-16, RAN4 can further discuss and define corresponding requirements if needed in Rel-17 timeframe i.e. Rel-17 side-link enhancement WI.
Test for gNB based sync
  gNB sync source based test is not introduced in Rel-16. Considering RAN4 work load and time limitation in Rel-16, RAN4 can further discuss and define corresponding requirements if needed in Rel-17 timeframe i.e. Rel-17 side-link enhancement WI.

## Slide 4: PSSCH demodulation
Test 1: Remaining issues for QPSK for 500km/h relative velocity (already agreed the test)
  20 PRB for PSSCH resource allocation
    Option 1: 10 PRB sub-channel size and number of allocated sub-channels is 2 (Intel, Huawei, LG, Qualcomm, MediaTek)
    Option 2: 20 PRB sub-channel size and number of allocated sub-channel is 1 (CATT, MediaTek, LG, Qualcomm)
  PSFCH periodicity
    4 periodicity
  DMRS pattern
    {3,4} DMRS symbols
  Propagation condition
    Option 1: TDLA30 (Intel, Huawei, LG, MediaTek)
    Option 2: TDLB100 or allocation 3symbol for PSCCH (LG, Qualcomm)
  Beta value for 2nd stage SCI
    Beta value = 3.5

## Slide 5: PSSCH demodulation
Test 2: Remaining issues for 16QAM for 260km/h relative velocity
  If the test is introduced, following parameters are considered
  20 PRB for PSSCH resource allocation
    Option 1:10 PRB sub-channel size and number of allocated sub-channels is 2 (Huawei, Qualcomm, LG, Intel, CATT(?))
    Option 2: 20 PRBs PSSCH allocation with single sub-channel size. (CATT, Qualcomm, LG)
  DMRS pattern
    Option 1: {3,4} DMRS symbols (Intel, Qualcomm, LG)
    Option 2: {2,3} DMRS symbols (Huawei, CATT, Qualcomm, LG, Intel)  agreeable
  Beta value for 2nd stage SCI
    Beta value = 5

## Slide 6: PSSCH demodulation
Test 3: Remaining issues for 64QAM for 30km/h relative velocity
  PRB for PSSCH resource allocation
    Option 1: 10 PRBs PSSCH allocation (Intel, LG, Qualcomm)
    Option 2: 10 PRB sub-channel size and number of allocated sub-channels is 2 (Huawei, MediaTek)
    Option 3: 20 PRBs PSSCH allocation with single sub-channel size (CATT, MediaTek)
  PSFCH periodicity
    Option 1: 1 periodicity (CATT, MediaTek)
    Option 2: 4 periodicity (Intel, Huawei, LG, Qualcomm)
  DMRS pattern
    2 DMRS symbols when PSFCH periodicity is 1 or 4
  Beta value for 2nd stage SCI
    Beta value = 5

## Slide 7: PSCCH demodulation
Remaining issue for PSCCH demodulation test
  Payload size
    Option 1: 24bit (MediaTek, CATT)
    Option 2: 26bit (Qualcomm, LG, Intel, Huawei, MediaTek)

## Slide 8: RMC naming
RMC naming
  Option 1: follow RMC naming of LTE V2X (LG)
    E.g., PSSCHCD.x, PSCCHCC.y
  Option 2: follow RMC naming of TS38.101-4 NR demodulation (Intel, Qualcomm, Intel)
    E.g., R.PSSCH.x, R.PSCCH.y

## Slide 9: Specification structure
Additional agreement for specification structure for NR V2X
  Option 1: No add sub-clause with number of Rx antenna (LG, CATT)
  Option 2: Add sub-clause with number of Rx antenna (Intel, Huawei)
11. V2X Requirements 11.1 Demodulation performance requirements (conducted requirements) 11.1.1 General 11.1.2 PSSCH demodulation requirements 11.1.2.1 2 Rx requirements 11.1.3 PSCCH demodulation requirements 11.1.3.1 2 Rx requirements 11.1.4 PSBCH demodulation requirements 11.1.4.1 2 Rx requirements 11.1.5 PSFCH demodulation requirements 11.1.5.1 2 Rx requirements 11.1.6 Power imbalance performance with two links 11.1.6.1 2 Rx requirements 11.1.7 HARQ buffer soft combining test 11.1.8 PSCCH/PSSCH decoding capability test 11.1.9 PSFCH decoding capability test 11.1.9.1 2 Rx requirements
example for option 2