## Slide 1: WF on Rel-16 NR HST UE capabilities
CMCC
3GPP TSG-RAN WG4 Meeting # 98-bis-e R4-2105831
Electronic Meeting, 12th – 20th April, 2021

## Slide 2: Separately support NR HST RRM and NR-LTE inter-RAT HST RRM
Add two new UE capabilities to
  10-4) Support of intra-NR HST RRM measurement with speed up to 500km/h
  10-5) Support of NR-LTE inter-RAT RRM measurement with speed up to 500km/h
  Note 1: UE can indicate support of 10-4 or 10-5 only if 10-1 is NOT supported.
  Note 2: The principle of adding the capabilities is to avoid the NBC issues

## Slide 3
Features | Index | Feature group | Components | Prerequisite feature groups | Need for the gNB to know if the feature is supported | Consequence if the feature is not supported by the UE | Type | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | Capability interpretation for mixture of FDD/TDD and/or FR1/FR2 | Note | Mandatory/Optional
10. NR HST | 10-4 | RRM enhanced requirements specified within NR HST | Optional with capability signalling |  | Yes | The performance of RRM within NR HST scenario cannot be guaranteed | Per UE | NO | FR1 only | UE can indicate support of 10-4 only if 10-1 is not supported |  | Optional with capability signalling
 | 10-5 | RRM enhanced requirements specified for NR-E-UTRAN inter-RAT measurement for NR HST | Optional with capability signalling |  | Yes | The performance of RRM in NR-E-UTRA inter-RAT measurement for HST scenario cannot be guaranteed | Per UE | NO | FR1 only | UE can indicate support of 10-5 only if 10-1 is not supported |  | Optional with capability signalling
Capture the above new features (10-4 and 10-5) in UE feature list

## Slide 4: Clarification on Need for the gNB to know if the feature is supported
Clarify that there is need for the network to know if the UE supports any of the feature groups specified for Rel-16 HST.
Capture the changes in UE feature list

## Slide 5: Clarification on UE behaviors
FFS whether the clarification on UE behaviors are needed.
  Option 1: UE is capable of HighSpeedParameters-r16 only with its NR module but not capable of HighSpeedEnhParameters-v1610 or highSpeedEnhParameters-r14 with its LTE module the UE is not required to meet the specified connected or idle mode measurement requirements for R16 HST inter-RAT NR-LTE enhancement.
    A UE is capable of operating in NR under 500km/h and measure target LTE cell of 500km/h speed with its NR baseband module, however it cannot operate in LTE cell of 500km/h when switched its baseband to the LTE module. This kind of UE reports supporting 10-1 since its NR module is capable of operating/measuring under 500km/h speed. (R4-2106442)
  Option 2 : When both 10-4, 10-5 are reported by UE( 10-4 is set to 1, and 10-5 is set to 0) and if network indicates flag 1 (reuse the existing signalling), UE is not required to meet the specified connected or idle mode measurement requirements for R16 HST inter-RAT NR-LTE enhancement.
  Other options are not precluded.

## Slide 6: References
R4-2104858 | On R16 NR HST UE capabilitiesOn R16 NR HST UE capabilities | Apple
R4-2106442 | Discussion on UE capabilities | Intel Corporation