## Slide 1: WF on UE RF requirements for PC 1.5 in Band n79
CMCC
3GPP TSG-RAN WG4 Meeting # 98-bis-e R4-210XXXX
Electronic Meeting, Apr. 12-20, 2021

## Slide 2
Agreements
UE RF requirements for PC1.5 in band n79:
  UE MOP and Tx power tolerance
    MOP and tolerance is 29 dBm +2/-3dB
  Configured transmitted power
    DT_RxSRS is the same as PC2 n79 (assuming 2T/4R)
  UL-MIMO
    MOP and tolerance for UL MIMO is 29 dBm +2/-3dB
  MPR
    The general requirement PC1.5 MPR will apply to n41, n77, n78, and n79
    Whether PC1.5 MPR needs to be re-evaluated can be discussed in the PC1.5 MPR topic
  A-MPR
    Companies are encouraged to identify whether co-existence A-MPR is needed for PC1.5 n79. If there is no co-existence analysis at May RAN4 meeting, it will be no modification to the section 6.2.3 (A-MPR) in 38.101-1 for PC1.5 n79

## Slide 3: Reference
[1] R4-2105012 Discussion on the PC1.5 UE RF requirements of NR n79, CMCC
[2] R4-2105013 Draft CR on PC1.5 UE RF requirements of n79 in Rel-17 TS 38.101-1, CMCC
[3] R4-2104893 Considerations for PC1.5 with band n79, Apple
[4] R4-2104957 Discussion on PC1.5 with n79, vivo
[5] R4-2107353 PC 1.5 in Band n79. Qualcomm Incorporated
[6] R4-2105010 Draft CR on PC1.5 HPUE SAR issue into Rel-16 TS 38.101-1, CMCC
[7] R4-2105011 Draft CR on PC1.5 HPUE SAR issue into Rel-17 TS 38.101-1, CMCC